## Slide 1: 3GPP TSG-RAN WG4 Meeting #92 Ljubljana, Slovenia, 26 - 30 August, 2019
Huawei, HiSilicon, China Telecom, MediaTek
Way forward on LTE FDD intra-band contiguous CA performance with minimum channel spacing
R4-1910571

## Slide 2: Background (1/5)
Minimum channel spacing for CA defined in TS 36.101 section 5.7.1A as yellow highlighted below:

## Slide 3: Background (2/5)
Demodulation performance requirements for intra-band contiguous CA with minimum channel spacing were defined in TS36.101 Section 8.2.2.8 from Release 12 that are only applicable for Band 41, i.e., CA_41C and CA_41D, as per the operator’s request with limited spectrum allocation

## Slide 4: Background (3/5)
Nominal and minimum channel spacing for different bandwidth combinations
Channel bandwidth (MHz) |  | Nominal channel spacing under non-CA (MHz) | Nominal channel spacing under intra-band contiguous CA (MHz) | Minimum channel spacing under intra-band contiguous CA (MHz)
CC#1 | CC#2 |  |  | 
3 | 5 | 4 | 3.9 | 3.9
5 | 5 | 5 | 4.8 | 4.8
5 | 10 | 7.5 | 7.2 | 6.9
5 | 15 | 10 | 9.3 | 9.3
5 | 20 | 12.5 | 11.7 | 11.4
10 | 10 | 10 | 9.9 | 9.3
10 | 15 | 12.5 | 12.0 | 11.4
10 | 20 | 15 | 14.4 | 13.8
15 | 15 | 15 | 15.0 | 13.8
15 | 20 | 17.5 | 17.1 | 15.9
20 | 20 | 20 | 19.8 | 18.3

## Slide 5: Background (4/5)
Occupied aggregated channel bandwidth with nominal and minimum channel spacing
Channel BW (MHz) |  | Nominal channel spacing under non-CA(MHz) | Occupied BW with non-CA and nominal channel spacing(MHz) | Nominal channel spacing under intra-band contiguous CA (MHz) | Occupied BW with intra-band contiguous CA and nominal spacing (MHz) | Minimum channel spacing under intra-band contiguous CA (MHz) | Occupied BW with intra-band contiguous CA and minimum spacing (MHz)
CC#1 | CC#2 |  |  |  |  |  | 
3 | 5 | 4 | 8 | 3.9 | 8 | 3.9 | 8
3 | 10 | 6.5 | 13 | 6 | 12.85 | 6 | 12.85
3 | 15 | 9 | 18 | 8.4 | 18 | 8.4 | 18
3 | 20 | 11.5 | 23 | 10.5 | 22.85 | 10.5 | 22.85
5 | 5 | 5 | 10 | 4.8 | 9.8 | 4.8 | 9.8
5 | 10 | 7.5 | 15 | 7.2 | 14.95 | 6.9 | 14.65
5 | 15 | 10 | 20 | 9.3 | 19.8 | 9.3 | 19.8
5 | 20 | 12.5 | 25 | 11.7 | 24.95 | 11.4 | 24.65
10 | 10 | 10 | 20 | 9.9 | 19.9 | 9.3 | 19.3
10 | 15 | 12.5 | 25 | 12.0 | 24.75 | 11.4 | 24.15
10 | 20 | 15 | 30 | 14.4 | 29.9 | 13.8 | 29.3
15 | 15 | 15 | 30 | 15.0 | 30 | 13.8 | 28.8
15 | 20 | 17.5 | 35 | 17.1 | 34.85 | 15.9 | 33.65
20 | 20 | 20 | 40 | 19.8 | 39.8 | 18.3 | 38.3

## Slide 6: Background (5/5)
Available spectrum that can be fit by intra-band contiguous CA with minimum channel spacing
Region | Country | Bandwidth (MHz) | Band | Achievable Intra-band contiguous CA combination
Europe | UK | 14.8 | Band1 | 5+10 with minimum channel spacing
West European Region | Germany | 14.85 | Band1 | 5+10 with minimum channel spacing
Southern-East Asia | Indonesia | 14.9 | Band1 | 5+10 with minimum channel spacing
CEE&Nordic European Region | Austria | 19.6 | Band1 | 10+10 with minimum channel spacing
Southern Africa | Zimbabwe | 14.8 | Band3 | 5+10 with minimum channel spacing
Central Asia & Caucasia | Kyrgyzstan |  |  | 
Middle East | Pakistan |  |  | 
Middle East | Belarus |  |  | 
Middle East | Kyrgyzstan |  |  | 
Southern-East Asia | China (Macao) | 19.4 | Band3 | 10+10 with minimum channel spacing
Middle East | United Arab Emirates | 19.6 | Band3 | 10+10 with minimum channel spacing
Southern-East Asia | Laos |  |  | 
West Europe | France |  |  | 
West Europe | France | 24.9 | Band3 | 5+20 with minimum channel spacing
NorthEast Europe | Poland | 29.7 | Band3 | 15+15 with minimum channel spacing
Central Asia & Caucasia | Turkey | 29.8 | Band3 | 10+20 with minimum channel spacing
Middle East | United Arab Emirates | 34.6 | Band3 | 15+20 with minimum channel spacing
Middle East | United Arab Emirates | 39.6 | Band3 | 20+20 with minimum channel spacing

## Slide 7: Way forward
Define demodulation performance requirements for intra-band contiguous CA with minimum channel spacing for FDD with the following bandwidth combinations:
  5+10MHz,
  5+20MHz
  10+10MHz
  10+20MHz
  15+15MHz
  15+20MHz
  20+20MHz
Simulation
  The test configurations of R.9 TDD for TDD intra-band contiguous CA with minimum channel spacing can be used for simulation alignment