## Slide 1
3GPP TSG-RAN WG4 Meeting #92BIS R4-1910932
Chongqing, China, 14th – 18th Oct, 2019
Agenda Item: 8.17.2.3
WF on UE demodulation for NR HST
CMCC

## Slide 2: Agreements
Maximum Doppler
    for HST-SFN with 30KHz SCS, the DL maximum Doppler frequency is proposed to be 1667Hz
    for HST-SFN with 15KHz SCS, the DL maximum Doppler frequency is proposed to be 780 Hz
MCS
    it is proposed to consider MCS17

## Slide 3: Agreements
Channel model
    it is proposed to consider following three options :
      Solution 1: for HST-SFN scenario, Ds=700m, Dmin=150m and Ds= 300m, Dmin=2m are considered for both 30KHz SCS and 15 KHz SCS. For HST single tap, Ds=700m, Dmin=150m and Ds= 300m, Dmin=2m are considered for both 30KHz SCS and 15 KHz SCS.
      Solution 2: for HST-SFN scenario, Ds=700m, Dmin=150m are considered for both 30KHz SCS and 15 KHz SCS. For HST single tap, Ds=300m, Dmin=2m are considered for both 30KHz SCS and 15 KHz SCS.
      Solution 3: for SCS=30KHz, Ds=700m, Dmin=150m are considered for both HST-SFN and HST single tap. For SCS=15KHz, Ds=300m, Dmin=2m are considered for both HST-SFN and HST single tap.

## Slide 4: Agreements
Signaling
    it is proposed to introduce network flag to indicate UE to apply the advanced receiver in HST-SFN scenario.
    it is proposed to introduce UE capability to indicate whether UE supports advanced receiver in HST-SFN scenario