## Slide 1: WF on Power Saving RRM requirements
CATT, Vivo
3GPP TSG-RAN WG4 Meeting #92bis R4-1910948
Chongqing, China, 14-18 Oct 2019

## Slide 2: Background
Specify network-configured mechanism to relax intra and inter-frequency RRM measurement for neighbour cells for RRC_IDLE/INACTIVE with minimal mobility performance impacts [RAN2, RAN4]
  Specify RRM measurement relaxation by allowing measurements with longer intervals, and/or by reducing the number of cells/carriers to be measured [RAN4, RAN2]
  Define triggering criteria for the UE to move between relaxed and normal RRM measurements, that considers at least if UE is not at cell edge, or if UE is stationary or with low mobility [RAN2, RAN4].
    Evaluate and specify requirements (if needed) depending on RAN2 criteria [ RAN4]
NOTE: No new measurement quantities should be introduced

## Slide 3: WF on RRM measurement relaxation
The following options should be considered for RRM measurement relaxation if the measurement relaxation criteria defined in RAN2 are met in next meeting:
  Option1: RRM measurement relaxation by allowing measurements with longer intervals, and/or by reducing the number of carriers to be measured;
  Option2: RRM measurement relaxation of neighbour cell monitoring in LTE MTC/NB-IoT can be reused for defining the RRM requirements for UE power saving in NR
  Other option is not precluded.

## Slide 4: WF on RRM requirement for MIMO layer adaption
RRM requirements for case 1:
  The current BWP switch delay and interruption requirements for Type 1 and Type 2 UE in 38.133 are reused
  RRM requirements for case 2 :
  depends on RF room conclusions and will be further discussed in RAN4#93 meeting
  Note: case 1 and case 2 are defined in [1].

## Slide 5: Reference
1. R4-1907615 WF on switching and interruption time for MIMO layer adaption for power saving CATT, Huawei, Huawei Device, vivo