## Slide 1: WF on NR V2X RRM requirement
LG Electronics
3GPP TSG-RAN WG4 #92bis Meeting
Chongqing, China, 14th – 18th Oct, 2019
R4-1911347

## Slide 2
Selection/Reselection to SyncRef UE
  For detection time of SyncRef UE
    Agree simulation assumption in RAN4#92bis
    Companies are encourage to provide simulation results in RAN4#93
  For dropping rate of SL for selection/reselection
    Reuse LTE-V2X requirements
Selection/Reselection to gNB or eNB in EN-DC or NE-DC
  UE chooses gNB or eNB corresponding to Pcell as synchronization reference source when they’re in the same priority
  RAN4 do not specify how to choose serving cell as synchronization reference source when multiple active serving cells under the same RAT(NR or LTE) are configured as candidate synchronization reference sources as LTE-V2X
  RAN4 do not specify how to facilitate the communication between UEs that synchronized to asynchronized synchronization reference sources.
Synchronization(1/2)

## Slide 3
Initiation/cease of SLSS transmission
  When NR serving cell is used as synchronization reference source, evaluation time is
    RRM impact due to timing misalignment between GNSS & gNB/eNB
      RAN4 does not specify it
Synchronization(2/2)
DRX cycle | Tevaluate,NR SLSS [s] (number of DRX cycles
No DRX | max(2x200ms, ceil( (5+1) x Kp) x SMTC period)Note 1 x CSSFintra
DRX cycle≤ 320ms | max(2x200ms, ceil(1.5x (5+1) x Kp) x max(SMTC period,DRX cycle)) x CSSFintra
DRX cycle>320ms | ceil( (5+1) x Kp ) x DRX cycle x CSSFintra
NOTE 1: If different SMTC periodicities are configured for different cells, the SMTC period in the requirement is the one used by the cell being identified | 

## Slide 4
Autonomous Resource Reselection measurement
  Evaluate only L1 SL-RSRP measurement for autonomous resource selection/reselection. For it, RAN4 need to wait RAN1 agreement for RS design related L1 SL-RSRP
Congestion Control measurement
  Reuse LTE-V2X S-RSSI measurement accuracy if S-RSSI is decided to be used as metric for NR V2X congestion control measurement.
Measurement

## Slide 5
Interruption to SL due to NR Uu BWP switching
  For case of NR V2X in ITS and concurrently supporting NR Uu
    Reuse Rel-15 interruption length regarding higher priority of NR Uu to NR V2X
  For case of NR V2X in licensed band
    Reuse Rel-15 interruption length, if the scenario is agreed in RF session
Interruption to Uu due to SL BWP configuration/reconfiguration
  Reuse Rel-15 interruption requirement due to RRC based BWP switching if NR V2X SL is defined in licensed band
Interruption(1/2)

## Slide 6
    When Uu BWP is different from SL BWP for NR V2X in shared licensed band
  Reuse Rel-15 interruption length if NR V2X SL is defined in licensed band
        When NR Uu BWP switching, and NR V2X SL BWP configuration/reconfiguration (if supported) are performed simultaneously
  NR V2X SL BWP configuration/reconfiguration is not expected during NR Uu operation and NR Uu BWP switching is not expected during NR V2X SL operation in UE side
Interruption(2/2)

## Slide 7
        SL RLM
  Study SL V2X RLM requirements in NR V2X for unicast based on RAN1/2 agreements on RLM metrics.
        HARQ
  RAN4 do not specify RRM requirement related to HARQ
Unicast, groupcast