## Slide 1: Way forward on R16 NR RRM enh - Multiple Scell activation/deactivation
Apple, …
R4-1911433
3GPP TSG-RAN WG4 Meeting #92bis
Chongqing, China, 14th – 18th October 2019

## Slide 2: Background
In RP-191601, the following scope has been approved for RRM enhancements:
RRM requirements of multiple Scell activation/deactivation in both FR1 and FR2
  Scell activation and deactivation delay and interruption requirements for multiple SCell activation/deactivation in FR1, and FR2, and FR1+FR2
    the corresponding delay requirements for both FR1 and FR2 should be power class agnostic

## Slide 3: Agreements in RAN4 #92bis
Principle to define the activation requirement for multiple Scells
  while activating an SCell, if any other SCell is activated or deactivated, UE is assumed to do activation on multiple SCells in parallel, provided that “the SSB SCS of SCell being activated on the same band is the same” or “the SSB SCS of SCell being activated on the same band is different and the combination of SCSs of data and SSB for all CCs in the same band is supported by UE.
    Except MAC-CE processing and search.
  While activating an unknown SCell, if any other unknown SCell is activated, the activation delay of the concerned SCell should further consider the number of parallel cell detection performed by UE on multiple SCCs.
    The number of searcher is assumed as 2 in RRM requirements.
Activation delay is expected to be increased if the interruption due to activating/deactivating on another cell causes the UE to miss receiving an SSB on cell currently being activated

## Slide 4: Remaining issue for RAN4 #93 (1/2)
HARQ feedback priority
  FFS: whether in the activation procedure of target deactivated Scell, HARQ feedback’s priority on other CCs is higher or lower than target deactivated SCell RF tuning/AGC settling or not.

## Slide 5: Remaining issue for RAN4 #93 (2/2)
FFS on Scell activation and deactivation delay and interruption requirements
  The delay of multiple Scell activation may be different due to following factors:
    FR1 only, FR2 only, or FR1+FR2
    Known or Unknown SCells
    Inter-band only, intra-band only or both
    CA and DC (sync or async. among CCs)
    Limitation on number of searchers of UE
    Simultaneous and non-simultaneous SCell activation command
    Collision between RF re-tuning on one CC and SMTC duration on the other CC
Companies are encourage to provide analysis on multiple SCell activation delay based on above factors.