## Slide 1: WF on NR MIMO OTA
CAICT, Spirent, CMCC, SGS Wireless
3GPP TSG-RAN WG4 Meeting #92bis R4-1911637
Chongqing, China, 14 – 18 October 2019
Agenda item: 10.2.1
Document for: Approval

## Slide 2: Environmental conditions
  The Environmental condition for FR1:
    Companies provide analysis results or measurement results next meeting to make the final decision.

## Slide 3: Test methods for FR1
  MPAC method
    Adopt 16 probes ring configuration (uniformly spaced) for NR FR1 MPAC system
    Select 1.2m range length (i.e. from the center of the chamber to the measurement probes) as the minimum for FR1 MPAC system.

## Slide 4: Test methods for FR2
  Orientations for FR2 MIMO OTA static testing
    Option 1: Non-3D sphere testing
    -Define below items step-by-step:
        Step1. UE rotation
        Step2. potential UE orientations and rotation steps
    Option 2: 3D sphere testing
      The testing time should be considered when selecting the step size & spatial region in this option.

## Slide 5: MU work for FR1
  Agreements
    Split FR1 MU discussion into two frequency ranges, i.e. (410MHz<f≤3 GHz) and (3 GHz<f≤7.125GHz), and focus on MU elements discussion to accelerate the progress.
    In MIMO OTA SI, do preliminary MU element and key values discussion for both ranges.
  Next step for RAN4 93 meeting to finalize FR1 MU work
    MU Elements and description
    Example MU values for CE, amplifiers and gNodeB

## Slide 6: Unfinished Objectives in the SID
Make decision on environmental condition for FR1
Define the applicable test methodology verification procedures
Develop the preliminary uncertainty assessment for the methodology
Develop channel model and emulated environment validation procedure to ensure correct implementation
Define Quality of Quiet Zone validation procedures for NR FR1 and FR2 systems
Define the UE Direction of Travel for FR2 channel models
Define Test system layout for FR2, including max limit of PSP
Study feasible SNR ranges for FR2 MIMO OTA testing

## Slide 7: Spatial correlation validation procedure for FR1
  Spatial correlation validation
    Option1: reuse LTE validation procedure
    Option2: Consider two directions line validation
    Option3: circle validation
    Other approach are not precluded
Option1
Option2
Option3

## Slide 8: Actions for next meeting
Provide full package for FR1 MPAC method, including system layout diagram, test procedure, Quality of Quiet Zone validation procedures, channel model validation procedure, preliminary MU elements and description
Provide full package for RTS method, including system layout, test procedure, Quality of Quiet Zone validation procedures, channel model validation procedure, preliminary MU elements and description
Make decision on FR2 system layout, PSP limit and range length
Define UE Direction of Travel for FR2 channel models
Further check on introducing 64QAM RMC in FR2 MIMO OTA based on the testability study
Define UE orientations for FR2
Further check the need of Tx Beam Lock for FR2 to ensure stable uplink conditions