## Slide 1: 3GPP TSG-RAN WG4 Meeting #92bis Chongqing, China, 14th – 18th October 2019
Huawei, HiSilicon
Way forward on RRM requirements of R16 enhancement for NB-IoT
R4-1911851

## Slide 2: WUS
Rel-15 WUS reception requirements apply for Rel-16 UE.

## Slide 3: PUR
UE should perform NRSRP measurement within tie range
  [T1-320ms, T1+320ms], where T1 is the time when TA is obtained
  [T2-320ms, T2], where T2 is the time when TA is validated
The range and resolution of threshold for NRSRP change is
  From 34dB to 10dB with 4dB resolution, and from 10dB to 2dB with 2dB resolution, for K=1 and the positive threshold for K=2 (for UE moving away from eNB)
  From -22dB to -10dB with 4dB resolution, and from -10dB to -2dB with 2dB resolution, for the negative threshold for K=2 (for UE moving towards eNB)

## Slide 4: Multi carrier operation non-anchor RRM
RAN4 decides that for the measurement samples from different carriers,
  Option 1: the results are feasible for the UE to use,
    the UE is allowed to translate the non-anchor NRSRP sample results by the corresponding RSRP offset value configured by the network
    Filter according to legacy requirements using the translated samples
    skip NRSRQ evaluation
  Option 2: the results are not feasible and only samples from the same carrier is allowed to the filter
Any filtered results, either from anchor or non-anchor carrier, can trigger neighbor cell measurement and/or relaxed monitoring abortion
A threshold should be used so that if the two samples of measured RSRP and/or RSRQ are spaced by a period longer than the threshold the results do not count

## Slide 5: Multi carrier operation connected channel quality report
Define in TS 36.133 for connected channel quality report the hypothetical NPDCCH parameters and the requirements that the channel quality report provides the minimum NPDCCH repetition level to satisfy the BLER of 1% according to the parameters
Define in TS 36.133 for connected channel quality report the reporting accuracy. Reuse the existing downlink channel quality measurement accuracy if possible

## Slide 6: Multi carrier operation msg3 based channel quality report
Use the msg3 based quality report requirements for anchor carriers as the baseline and enhance the wording to apply to the non-anchor carriers msg3 based reporting