## Slide 1: 3GPP TSG-RAN WG4 Meeting #92bis Chongqing, China, 14 – 18 October 2019
Huawei, HiSilicon
WF on Rel-16 eMTC RRM
R4-1912005

## Slide 2: DL quality report
Define the MPDCCH parameters for DL quality reporting as.
Measurement period for DL quality reporting in idle mode is T2.
For DL quality reporting with 8-bit in idle mode, the report mapping is defined as
Attribute | Normal coverage/CEModeA | Enhanced coverage/CEModeB
DCI format | 6-1A | 6-1B
Starting OFDM symbols | 2; Bandwidth >= 10MHz 3; 3MHz <= Bandwidth < 10MHz 4; Bandwidth = 1.4MHz | 
MPDCCH repetition level Note1 | 1 | n.a.
MPDCCH Aggregation level (ECCE) Note2 | 24 | 
M-PDCCH Transmission type | Distributed | 
NOTE 1: Not applicable if repetition number in DL quality information is larger than 1. NOTE 2: Not applicable if repetition number in DL quality information equals to 1. |  | 
Reported value | MPDCCH repetition level
noMeasurement | No measurement reporting
candidateRep-A | 1
candidateRep-B | 2
candidateRep-C | 4
candidateRep-D | 8
candidateRep-E | 16
candidateRep-F | 32
candidateRep-G | 64
candidateRep-H | 128
candidateRep-I | 256
Reported value | MPDCCH aggregation level
noMeasurement | No measurement reporting
candidateRep-A | 1
candidateRep-B | 2
candidateRep-C | 4
candidateRep-D | 8
candidateRep-E | 16
candidateRep-F | 12
candidateRep-G | 24
reported repetition number larger than 1
reported repetition number equals to 1

## Slide 3: WUS
Rel-15 WUS reception requirements apply for Rel-16 UE.

## Slide 4: PUR
UE should perform RSRP measurement within time range
  [T1-320ms, T1+320ms], where T1 is the time when TA is obtained
  [T2-320ms, T2], where T2 is the time when TA is validated
The range and resolution of threshold for RSRP change is
  From 34dB to 10dB with 4dB resolution, and from 10dB to 2dB with 2dB resolution, for K=1 and the positive threshold for K=2 (for UE moving away from eNB)
  From -22dB to -10dB with 4dB resolution, and from -10dB to -2dB with 2dB resolution, for the negative threshold for K=2 (for UE moving towards eNB)

## Slide 5: Mobility enhancement
Re-use the current measurement period for CRS based measurement for RSS based measurement.
RAN4 can investigate if improved accuracy requirements can be defined for RSS based measurement.
RAN4 should discuss whether RSS measurement requirements, if defined, are applicable to neighbour cell or not.