## Slide 1: WF on RRM Requirements for NR-U
Ericsson
3GPP TSG-RAN WG4 Meeting #92-Bis R4-1912082
Chongqing, P. R. of China, 14th – 18th October, 2019
Agenda Item: 8.1.4

## Slide 2: Serving Cell Evaluation
Ms is the number of DRX cycles where SMTC occasions are not available at the UE for measurement
M1=2 if SMTC periodicity (TSMTC) > 20 ms and DRX cycle ≤ 0.64 second, otherwise M1=1
Ms=8 when DRX cycle length < 1.28 seconds, and Ms=4 when DRX cycle length ≥ 1.28 seconds
RAN4 agrees to set Mp=4 and Mq=8

## Slide 3: Cell Re-Selection
Mn < Mm
Md>Me>Mm
Mn=2, and Mm=8 when DRX cycle length<1.28 and Mm=4 when DRX cycle length ≥ 1.28
Me=2*Mm, and Md=2*Me

## Slide 4: Paging Interruption
Paging interruption delay requirements are defined for NR-U UEs in IDLE/INACTIVE state by taking into account the extended time needed to acquire the MIB and SIB1 due to LBT failure based on the simulation study

## Slide 5: Handover
L1,max and L’1,max are set to 4 and 8 when TSMTC > 40 ms and TSMTC ≤ 40 ms respectively
L3,max is set to 2 and 4 when TRA > 40 ms and TRA ≤ 40 ms respectively
L2,max =8 when DRX cycle length < 1.28 seconds, and L2,max =4 when DRX cycle length ≥ 1.28 seconds
The UE stops the handover procedure if it fails to fulfil any of the following conditions: L1 > L1,max, L´1 > L´1,max, L2> L2,max, or L3> L3,max

## Slide 6: RRC Re-Establishment
Maximum allowed number of missed SMTC cycles for intra-frequency cell search
Maximum allowed number of missed SMTC cycles for inter-frequency cell search
Maximum allowed number of missed PRACH occasions
SMTC period (TSMTC) | Maximum allowed number of missed SMTC cycles (K1,max)
TSMTC ≤ 40 ms | 12
TSMTC > 40 ms | 8
SMTC period (TSMTC, i) | Maximum allowed number of missed SMTC cycles (K2.i,max)
TSMTC, i ≤ 40 ms | 10
TSMTC, i > 40 ms | 6
PRACH configuration period (Tconfig) | Maximum allowed number of missed PRACH occasions (K3, max)
Tconfig ≤ 40 ms | 8
Tconfig > 40 ms | 4

## Slide 7: RRC Connection with Redirection
Maximum allowed number of missed SMTC cycles for cell search in RRC connection release with redirection
Maximum allowed number of missed PRACH occasions in RRC connection release with redirection
SMTC period (TSMTC) | Maximum allowed number of missed SMTC cycles (L1,max)
TSMTC ≤ 40 ms | 8
TSMTC > 40 ms | 4
PRACH configuration period (Tconfig) | Maximum allowed number of missed PRACH occasions (L3, max)
Tconfig ≤ 40 ms | 8
Tconfig > 40 ms | 4

## Slide 8: RLM: in-sync
Configuration | TEvaluate_in_SSB (ms)
no DRX | Max(100, Ceil((5 + Lin)*P)*TSSB)
DRX cycle≤320 | Max(100, Ceil(1.5*(7.5 + Lin)*P)*Max(TDRX,TSSB))
DRX cycle>320 | Ceil((5 + Lin)*P)*TSSBDRX
NOTE 1: TSSB is the periodicity of the SSB configured for RLM. TDRX is the DRX cycle length. NOTE 2: Lin is the number of SSBs not available at the UE during TEvaluate_in_SSB, where Lin ≤ Lin,max. NOTE 3: Lin,max=20 for Max(TDRX,TSSB)≤40 where TDRX=0 for non-DRX, Lin,max=10 for 40<Max(TDRX,TSSB)≤320, Lin.max=5 for TDRX>320. | 
When is Lin is exceeded, UE layer 1 shall not send any indication to higher layers and shall try to complete the next in-sync evaluation period

## Slide 9: RLM: out-of-sync
Configuration | TEvaluate_out_SSB (ms)
no DRX | Max(100, Ceil((10 + X + Lout)*P)*TSSB)
DRX cycle≤320 | Max(100, Ceil((15 + X + Lout)*P)*Max(TDRX,TSSB))
DRX cycle>320 | Ceil((10 + X + Lout)*P)*TDRX
NOTE 1: TSSB is the periodicity of the SSB configured for RLM. TDRX is the DRX cycle length. NOTE 2: Lout is the number of SSBs not available at the UE during TEvaluate_out_SSB, where Lout ≤ Lout,max. NOTE 3: Lout,max=40+X for Max(TDRX,TSSB)≤40 where TDRX=0 for non-DRX, Lout,max=20+X for 40<Max(TDRX,TSSB)≤320, Lout,max=10+X for TDRX>320. NOTE 4: X is for additional delay depending on the number Ndet of samples needed to determine the presence of SSB by UE. X=0 and Ndet=1 for SINR≥[-6] dB, X=TBD and Ndet=2 for SINR<[-6] dB. | 
For out-of-sync, define evaluation period based on Lout and multiple (e.g., 2) samples for detecting the presence of RLM-RS
Upon out-of-sync evaluation failure for an RLM-RS resource the UE behavior is the same as if the radio link quality were below Qout for this RLM-RS resource. Furthermore, the UE shall try to complete the next out-of-sync evaluation period
X=Ndet-1

## Slide 10: Beam Management: General
RAN4 prioritizes the SSB based beam failure detection and candidate beam detection for NR-U. RAN4 will revisit CSI-RS based BFD/CBD when RAN1 decided the CSI-RS configuration for BFD-RS/CBD-RS

## Slide 11: Beam Management: BFD
Set the SSB based BFD evaluation period for NR-U as follows
In the case of BFD evaluation failure, i.e., LBFD exceeds LBFD_max, UE behaviour is the same as if the radio link quality were below Qout_LR for this BFD-RS resource

## Slide 12: Beam Management: CBD
Set the SSB based CBD evaluation period for NR-U as follows
In the case of CBD evaluation failure, i.e., LCBD exceeds LCBD_max, UE should skip the new beam selection process.

## Slide 13: Beam Management: L1-RSRP
RAN4 prioritizes the SSB based L1-RSRP measurements for reporting for NR-U. RAN4 will revisit CSI-RS based L1-RSRP measurements when RAN1 decided the CSI-RS configuration for L1-RSRP measurements
Set the SSB based L1-RSRP evaluation period for NR-U as follows
UE report ‘not valid’ to the network in the case of L1-RSRP measurement failure, i.e., L1 exceeds L1max
Use RSRP_0 to indicate ‘not valid’

## Slide 14: Interruptions
The interruption due to deactivated Scell measurements applies in all scenarios A-C
  The interruption due to deactivated Scell measurements for an NR-U aggressor cell can reuse the requirements for release 15 NR deactivated Scell measurements
The definition of Tharq in activation and interruption requirements is clarified such that for NR-U it represents the earliest attempt for the UE to send HARQ feedback, regardless if the feedback is successful, or fails due to uplink LBT

## Slide 15: Scell Activation: Known Cell Defintion
The period before the reception of the SCell activation command is extended:
Non-DRX: (5+LDL) measCycleSCell + UL ,
DRX: max((5+LDL) measCycleSCell, (5+ LDL) DRX cycles) + UL
  where LDL≤ LDL,max is the number of measurement occasions with SSBs not available at the UE due to CCA,
  UL≤UL,max is the additional delay due to UE inability to send a valid measurement report on a carrier frequency with CCA (UL=0 for UL channel access category 1)
LDL,max=TBD and UL,max=TBD, upon exceeding any of which the SCell can be considered unknown
SSB remains detectable according to the cell identification conditions in clause 9.2 and 9.3 in the occasions where the SSB is available at the UE

## Slide 16: Scell Activation Delay
THARQ = THARQ,ref+HARQ , where THARQ,ref is the timing between DL data transmission and acknowledgement as specified in TS 38.213 [3], and HARQ≤HARQ,max is the delay in HARQ feedback due to UL LBT failure and UE reattempt to transmit HARQ feedback provided the resources are configured for the UE (HARQ =0 for channel access category 1).
  HARQ,max=TBD, upon exceeding which UE can stop attempting to transmit HARQ feedback and can abandon SCell activation
Tactivation_time is defined as follows (where L1≤L1max, L2≤L2max, and L3≤L3max are the corresponding numbers of SSB occasions not available at the UE due to CCA failure):
  For a known SCell:
TFirstSSB+ Trs *L1+ 5ms, if the SCell measurement cycle is equal to or smaller than 160ms.
(TSMTC_MAX + Trs )*(1+L2)+ 5ms, if the SCell measurement cycle is larger than 160ms.
  For an unknown SCell:
(TSMTC_MAX + Trs )*(2+L3)+ 5ms, provided the SCell can be successfully detected in one attempt.
  L1max, L2max, and L3max are TBD, upon exceeding which the UE can stop activating the SCell and can abandon the SCell activation procedure.
TCSI_reporting = TCSI_reporting,ref +CSI, where TCSI_reporting,ref is the delay (in ms) including uncertainty in acquiring the first available downlink CSI reference resource, UE processing time for CSI reporting and uncertainty in acquiring the first available CSI reporting resources as specified in TS 38.331 [2], and CSI≤CSI,max is the additional delay due to UL LBT failure and UE reattempt to transmit CSI report provided the resources are configured for the UE (CSI =0 for channel access category 1).
  CSI,max=TBD, upon exceeding which UE can stop attempting to transmit CSI report and can abandon the SCell activation procedure

## Slide 17: Scell Activation: Interruption Time
The timing of the interruption window for SCell activation in NR-U is defined so that the corresponding interruptions shall not occur before slot n+1+(THARQ+HARQ,L)/slot_length and shall not occur after slot n+1+((THARQ+HARQ,L) +3ms + TSMTC_MAX + TSMTC_duration)/slot_length, where L is the number of UE failures to access the channel to transmit HARQ feedback.

## Slide 18: PScell Addition: Known Cell Definition
The known PSCell definition needs to be updated for NR-U
Measured SSB remains detectable according to the cell identification conditions in the occasions where the SSB is available at the UE.
The time before the reception of the PSCell configuration command is extended to account for DL LBT, e.g., to [5] seconds+ L*TRS +, where L is the number of SMTC occasions not available at the UE due to CCA, and  is the reporting delay due to UL LBT failure and UE reattempt(s) to report at least 1 measurement for the PSCell being configured provided the UL resources are configured for the UE (=0 for channel access category 1).
The maximum values of L and  are TBD, upon exceeding which the UE shall assume the PSCell is unknown.

## Slide 19: PScell Addition Delay
To account for DL and UL LBT, Tconfig PSCell is extended, to be specified in TS 36.133
Tconfig_PSCell = TRRC_delay + Tprocessing + Tsearch +T∆ + (TPSCell_ DU,ref+PRACH)+ 2 ms , with Tsearch=0 for the known PSCell and Tsearch=(3+L1)* Trs for unknown PSCell, T∆=Trs*(1+L2), and where the other parameters are defined as above
The maximum value of PRACH (PRACH,max) is TBD, upon exceeding which the UE can stop attempting to transmit PRACH and can abandon the PSCell addition procedure
The maximum values of L1 and L2 are TBD and may depend on TRS, upon exceeding which the UE can restart the search and timing acquisition procedures, but the UE can abandon the PSCell addition after N unsuccessful attempts to complete the search and the timing acquisition procedures

## Slide 20: BWP Switching: DCI Based
The total time period over which DCI-based DL BWP switching occurs shall be:
n+ TBWPswitchDelay + TDCI_DL slots
  TDL is the time period (in slots) starting from slot n+ TBWPswitchDelay and over which DL slot is unavailable at the UE due to DL CCA failures in the serving cell
  When TDCI_DL > Tmax then the UE is not expected to receive the PDSCH on the new BWP.
  Tmax = TBD.
The total time period over which DCI-based UL BWP switching occurs shall be:
n+ TBWPswitchDelay + TDCI_UL, (slots)
  TDCI_UL is the time period (in slots) staring from slot n+ TBWPswitchDelay and over which UL slot is unavailable at the UE due to UL CCA failures in the serving cell
  When TDCI_UL > Tmax then the UE is not expected to transmit the PUSCH on the new BWP
  Tmax = TBD

## Slide 21: BWP Switching: Timer Based
The total time period over which timer-based DL BWP switching occurs shall be:
n+ TBWPswitchDelay + TTimer_DL (slots)
  TDL is the time period starting from slot n+ TBWPswitchDelay and over which DL slot is unavailable at the UE due to DL CCA failures in the serving cell. It is expressed in slots.
  When TTimer_DL > Tmax then the UE is not expected to receive the PDSCH on the new BWP
  Tmax = TBD
The total time period over which time-based UL BWP switching occurs shall be:
  n+ TBWPswitchDelay + TTimer_UL (slots)
  TTimer_UL is the time period starting from slot n+ TBWPswitchDelay and over which UL slot is unavailable at the UE due to UL CCA failures in the serving cell. It is expressed in slots
  When TTimer_UL > Tmax then the UE is not expected to transmit the PUSCH on the new BWP.
  Tmax = TBD

## Slide 22: BWP Switching: RRC Based
The total time period over which RRC-based DL BWP switching occurs shall be:
+ TRRC_DL (slots)
  TRRC_DL is the time period (in slots) starting from slot and over which the DL slot is unavailable at the UE due to CCA failures in the serving cell
  When TRRC_DL > Tmax then the UE is not expected to receive the PDSCH on the new BWP
The total time period over which RRC-based UL BWP switching occurs shall be:
+ TRRC_DL, (slots)
  TRRC_DL is the time period (in slots) starting from slot and over which the DL slot is unavailable at the UE due to CCA failures in the serving cell
  When TRRC_DL > Tmax then the UE is not expected to receive the PDSCH on the new BWP

## Slide 23: Active TCI State Switching: Known State Definition
TCI state remains detectable during the TCI switching period meeting the SNR of the TCI state condition, which is ≥ -3dB, in the occasions where the SSB is available at the UE
The maximum time between receiving of the TCI state switching command and the last transmission of the RS resource for beam reporting or measurement for the target TCI state is extended, e.g., [1280]+ L*TSSB ms+, where L is the number of measurement occasions with SSBs not available at the UE due to CCA, and  is the reporting delay due to UL LBT failure and UE reattempt to report at least 1 measurement for the target TCI state provided the UL resources are configured for the UE (=0 for channel access cat1)
The maximum values of L and  are TBD, upon exceeding which the UE shall assume the TCI state is unknown

## Slide 24: Active TCI State Switching Delay, Known Cell
MAC-CE based TCI state switching:
  UE is required to receive PDCCH using the new TCI state (after switching or the active TCI state list update) in
slot n + (THARQ,ref+HARQ) + 3 ms + TOk*(Tfirst-SSB+TSSB-proc+TSSB*LMAC,known),
and receive PDCCH using the old TCI state until
slot n + (THARQ,ref+HARQ) + 3 ms + TOk*(Tfirst-SSB+TSSB*LMAC,known),
where the parameters are as defined in R4-1912084
  The maximum value of HARQ is TBD, upon exceeding which the UE may stop attempting to transmit HARQ feedback and may abandon the active TCI state switching procedure
  The maximum value of LMAC,known is TBD and may depend on TSSB, upon exceeding which the UE may stop the switching and abandon the active TCI state switching procedure
RRC based TCI state switching:
  UE is required to receive PDCCH using the new TCI state in
slot n + TRRC_processing + TOk*(Tfirst-SSB + TSSB-proc+TSSB* LRRC,known),
where the parameters are as defined in R4-1912084
  The maximum value of LRRC,known is TBD and may depend on TSSB, upon exceeding which the UE may stop the switching and abandon the active TCI state switching procedure

## Slide 25: Active TCI State Switching Delay, Unknown Cell
For MAC-CE based switching
  UE is required to receive PDCCH using the new TCI state in
  slot n+(THARQ,ref+HARQ)+3 ms+(TL1-RSRP+TCSI-RS/SSB*L1MAC,unknown)+TOuk*(Tfirst-SSB+TSSB-proc+TSSB*L2MAC,unknown),
  and receive PDCCH using the old TCI state until
slot n+(THARQ,ref+HARQ)+3 ms+(TL1-RSRP+TCSI-RS/SSB*L1MAC,unknown)+TOuk*(Tfirst-SSB+TSSB*L2MAC,unknown),
where the parameters are as defined above
  The maximum value of HARQ is TBD, upon exceeding which the UE may stop attempting to transmit HARQ feedback and may abandon the active TCI state switching procedure
  The maximum value of L1MAC,unknown is TBD and may depend on TCSI-RS,SSB, upon exceeding which the UE may restart the L1-RSRP measurement, but the UE may abandon the active TCI state switching procedure after N unsuccessful attempts to complete the L1-RSRP measurement
  The maximum value of L2MAC,unknown is TBD and may depend on TSSB, upon exceeding which the UE may stop the switching and abandon the active TCI state switching procedure
RRC-based switching
  UE is required to receive PDCCH using the new TCI state in
slot n + TRRC_processing + (TL1-RSRP + TCSI-RS/SSB*L1RRC,unknown) + TOuk*(Tfirst-SSB + TSSB-proc+TSSB* L2RRC,unknown),
where the parameters are as defined above
  The maximum value of L1RRC,unknown is TBD and may depend on TCSI-RS,SSB, upon exceeding which the UE may restart the L1-RSRP measurement, but the UE may abandon the active TCI state switching procedure after N unsuccessful attempts to complete the L1-RSRP measurement
  The maximum value of L2RRC,unknown is TBD and may depend on TSSB, upon exceeding which the UE may stop the switching and abandon the active TCI state switching procedure

## Slide 26: SI Reading
Observation 1:
  SI acquisition time for RRC Release with Redirection and RRC Re-establishment procedures, TSI-NR, are given by TSI-NR = TMIB + TSIB1
Define SI acquisition time for NR-U as TSI-NR-U = TMIB-NR-U + TSIB1-NR-U, where TMIB-NR-U is the MIB acquisition time for NR-U and TSIB1-NR-U is the SIB1 acquisition time for NR-U
TMIB-NR-U = TSMTC * GMIB, where TSMTC is the configured SMTC period and GMIB = NMIB + NLBT-failure, where NLBT-failure is the number of LBT failures by the time BS transmits NMIB PBCH.
NMIB = 3
Observation 2:
  Soft-combining may need to be assumed for SIB1 acquisition depending on the side condition and SIB1 transmission assumption
To decide NSIB1, RAN4 first needs to discuss the PDSCH transmission parameters for SIB1 acquisition such as:
  PDSCH transmission parameters, e.g., PRB size, TBS, modulation, etc.
  Whether or not it is assumed soft-combining of PDSCH within SIB1 TTI. If yes, how many?
  Metric to decide the number of PDSCH transmissions, e.g., PDSCH decoding success rate of 90%
  Side condition, e.g., SNR=-6dB
Based on the assumption interested companies will provide the simulation results and decide NSIB1 according to the results

## Slide 27: Measurement Reporting Delay
The UL LBT failure impact on UE measurement reporting is specified in TS 38.133 for UL channel access categories other than the channel access category 1
Existing reporting requirements apply for the reporting based on the UL channel access category 1
For periodic reporting, no need to resend the old measurement report which was not sent due to UL LBT failure
For aperiodic reporting, upon an UL LBT failure, the UE may reattempt one or more times to access the channel and send the report, provided the UE is configured with the necessary UL resources. When the reporting delay exceeds a limit or the number of acceptable unsuccessful reporting attempts due to UL LBT failures is above a limit, the UE shall abandon the reporting procedure
For aperiodic reporting, the measurement reporting delay on a carrier frequency with CCA shall not exceed the intra-frequency cell identification time period (T identify intra without index or T identify intra with index) plus an additional delay (UL) due to UL LBT failures, where
  If the (DL) measurement is also on a carrier frequency with CCA, then the intra-frequency cell identification period for NR-U shall be used to determine the reporting delay, otherwise the NR intra-frequency cell identification period shall be used
  UL depends on the number of UL LBT failures

## Slide 28: Reporting Criteria
For UE capable of and configured with wideband operation with CCA, 1 report for RSSI and channel occupancy measurements is capable of minimum 1 RSSI measurement and 1 channel occupancy measurement per subband.
For UE not capable of or not configured with wideband operation with CCA, 1 report for RSSI and channel occupancy measurements is capable of minimum 1 RSSI measurement and 1 channel occupancy measurement per carrier frequency with CCA.
For UE capable of and configured with wideband operation with CCA, clarify (e.g., in a note in the reporting criteria table) that each 1 reporting criterion is capable of respective measurements per subband.
For UE not capable of or not configured with wideband operation with CCA, clarify (e.g., in a note in the reporting criteria table) that each 1 reporting criterion is capable of respective measurements per carrier frequency with CCA.

## Slide 29: Measurement Capability
For NR-U Scenarios A and C, the number of frequency layers in RRC_CONNECTED is the same as for Rel-15 SA NR, excluding the frequency layers for inter-RAT RSTD measurements. The total number of effective carrier frequency layers is 13, i.e., the same as in Rel-15 SA NR
For NR-U Scenario C, the number of frequency layers in RRC_IDLE is the same as for Rel-15 SA NR. The total number of effective carrier frequency layers is 14, i.e., the same as in Rel-15 SA NR
For NR-U Scenario B, the number of frequency layers in RRC_CONNECTED is the same as for Rel-15 EN-DC, excluding the frequency layers for inter-RAT RSTD measurements. The total number of effective carrier frequency layers is 13, i.e., the same as in Rel-15 EN-DC

## Slide 30: Measurement Gaps
Observation 1
  NR-U deployments will be unplanned, or less planned than licensed NR deployments
Observation 2
  Due to the unplanned nature of NR-U deployment, it is likely that a relatively large number of NR-U operating frequencies (interfrequency/interRAT) may need to be provided to NR-U capable UEs
Observation 3
  Many RRM delays are extended for a carrier frequency where CCA is used, compared with carrier frequencies where CCA is not used
Observation 4
  The system needs for RRM on licensed carriers are typically not relaxed when NR-U is deployed.
Observation 5
  There is a strong motivation to introduce the independent FR1+NR-U measurement capability
RAN4 discusses feasibility to measure NR-U bands with an independent gap pattern
RAN4 discusses suitable capabilities which will ease the UE implementation burden

## Slide 31: CSSF (Scaling Factor)
The CSSFwithin_gap,i specification in 38.133 does not need to be updated for NR-U other than to clarify that the existing definition of CSSF applies to frequencies where CCA is performed as well as frequencies where CCA is not performed

## Slide 32: RSSI and Channel Occupancy Measurements
Configuring the measurement duration and bandwidth shall be independent of the SCS used in the measurement resources, e.g., as fractions or multiples of a subframe and in MHz, respectively, or configured with respect to a reference SCS which may be different from the SCS of the measurement resources
RSSI and channel occupancy measurement resources shall not be limited to SSB time resources or SSB frequencies
Inform RAN1 about the above observations
RAN4 to define intra-frequency (on PCC, PSCC, and SCC), inter-frequency, and inter-RAT measurement requirements for RSSI and channel occupancy
RAN4 to define intra-frequency, inter-frequency, and inter-RAT measurement accuracy requirements for RSSI and channel occupancy
RAN4 to define measurement reporting mapping for RSSI. FFS whether measurement report mapping is needed for channel occupancy, depending on its definition to be decided by other groups
RAN4 to decide the measurement gap patterns applicable for RSSI and channel occupancy measurements and specify the applicability

## Slide 33: Intra-Frequency Measurements: Lmax
Procedure | Rel-15 samples | Maximum number of DL LBT failures |  | 
 |  | Parameter name | Parameter value | Condition
PSS/SSS detection, no gaps | 5 | LPSS/SSS,max | 20 | Max(TDRX,TSMTC)≤40
 |  |  | 10 | 40<Max(TDRX,TSMTC)≤320
 |  |  | 5 | TDRX>320
PSS/SSS detection for deactivated SCell, no gaps | 5 | LPSS/SSS,deact,max | 20 | Max(TDRX, measCycleSCell)≤40
 |  |  | 10 | 40< Max(TDRX, measCycleSCell)≤320
 |  |  | 5 | TDRX>320
Time index detection, no gaps | 3 | Lind,max | 12 | Max(TDRX, TSMTC)≤40
 |  |  | 6 | 40< Max(TDRX, TSMTC)≤320
 |  |  | 3 | TDRX>320
Time index detection for deactivated SCell, no gaps | 3 | Lind,deact,max | 12 | Max(TDRX, measCycleSCell)≤40
 |  |  | 6 | 40< Max(TDRX, measCycleSCell)≤320
 |  |  | 3 | TDRX>320
Measurement, no gaps | 5 | Lmeas,max | 20 | Max(TDRX, TSMTC)≤40
 |  |  | 10 | 40< Max(TDRX, TSMTC)≤320
 |  |  | 5 | TDRX>320
Measurement on deactivated SCell, no gaps | 5 | Lmeas,deact,max | 20 | Max(TDRX, measCycleSCell)≤40
 |  |  | 10 | 40< Max(TDRX, measCycleSCell)≤320
 |  |  | 5 | TDRX>320
PSS/SSS detection, with gaps | 5 | LPSS/SSS,gaps,max | 20 | Max(TDRX,TSMTC, MGRP)≤40
 |  |  | 10 | 40<Max(TDRX,TSMTC, MGRP)≤320
 |  |  | 5 | TDRX>320
Time index detection, with gaps | 3 | Lind,gaps,max | 12 | Max(TDRX, TSMTC, MGRP)≤40
 |  |  | 6 | 40< Max(TDRX, TSMTC, MGRP)≤320
 |  |  | 3 | TDRX>320
Measurement, with gaps | 5 | Lmeas,gaps,max | 20 | Max(TDRX, TSMTC, MGRP)≤40
 |  |  | 10 | 40< Max(TDRX, TSMTC, MGRP)≤320
 |  |  | 5 | TDRX>320

## Slide 34: Intra-Frequency Measurements: UE Behavior
Upon exceeding the maximum acceptable number of DL LBT failures, the UE has to restart the corresponding procedure, e.g., PSS/SSS detection, time index detection, or measurements
At least for aperiodic measurements, the number of restarts due to exceeding the corresponding maximum number of DL LBT failures can be limited, after which the measurement procedure can be abandoned

## Slide 35: Intra-Frequency Measurements: no Gaps
DRX cycle | TPSS/SSS_sync_intra
No DRX | max( 600ms, ceil( (5+LPSS/SSS) x Kp) x SDMTC period )Note 1 x CSSFintra
DRX cycle≤ 320ms | max( 600ms, ceil(1.5x (5+LPSS/SSS) x Kp) x max(SDMTC period,DRX cycle)) x CSSFintra
DRX cycle>320ms | ceil((5+LPSS/SSS) x Kp) x DRX cycle x CSSFintra
NOTE 1: If different SMTC periodicities are configured for different cells, the SMTC period in the requirement is the one used by the cell being identified. NOTE 2: LPSS/SSS is the number of SMTC periods not available at the UE during TPSS/SSS_sync_intra, where LPSS/SSS ≤ LPSS/SSS,max. NOTE 3: LPSS/SSS,max =20 for Max(DRX cycle,SMTC period)≤40 where DRX cycle is 0 for non-DRX, LPSS/SSS,max =10 for 40<Max(DRX cycle,SMTC period)≤320, LPSS/SSS,max =5 for DRX cycle>320. | 
DRX cycle | TSSB_time_index_intra
No DRX | max(120ms, ceil( (3+Lind) x Kp ) x SMTC period)Note 1 x CSSFintra
DRX cycle≤ 320ms | max(120ms, ceil (1.5 x (3+Lind) x Kp) x max(SMTC period,DRX cycle)) x CSSFintra
DRX cycle>320ms | Ceil((3+Lind) x Kp) x DRX cycle x CSSFintra
NOTE 1: If different SMTC periodicities are configured for different cells, the SMTC period in the requirement is the one used by the cell being identified. NOTE 2: Lind is the number of SMTC periods not available at the UE during TSSB_time_index_intra, where Lind ≤ Lind,max. NOTE 3: Lind,max =12 for Max(DRX cycle,SMTC period)≤40 where DRX cycle is 0 for non-DRX, Lind,max =6 for 40<Max(DRX cycle,SMTC period)≤320, Lind,max =3 for DRX cycle>320. | 
DRX cycle | T SSB_measurement_period_intra
No DRX | max(200ms, ceil( (5+ Lmeas) x Kp) x SDMTC period)Note 1 x CSSFintra
DRX cycle≤ 320ms | max(200ms, ceil(1.5x (5+ Lmeas) x Kp) x max(SDMTC period,DRX cycle)) x CSSFintra
DRX cycle>320ms | ceil((5+ Lmeas) x Kp ) x DRX cycle x CSSFintra
NOTE 1: If different SMTC periodicities are configured for different cells, the SMTC period in the requirement is the one used by the cell being identified NOTE 2: Lmeas is the number of SMTC periods not available at the UE during T SSB_measurement_period_intra, where Lmeas ≤ Lmeas,max. NOTE 3: Lmeas,max =20 for Max(DRX cycle,SMTC period)≤40 where DRX cycle is 0 for non-DRX, Lmeas,max =10 for 40<Max(DRX cycle,SMTC period)≤320, Lmeas,max =5 for DRX cycle>320. | 

## Slide 36: Intra-Frequency Measurements: Deactivated SCell, no Gaps
DRX cycle | TPSS/SSS_sync_intra
No DRX | (5+ LPSS/SSS) x measCycleSCell x CSSFintra
DRX cycle≤ 320ms | (5+ LPSS/SSS) x max(measCycleSCell, 1.5xDRX cycle) x CSSFintra
DRX cycle> 320ms | (5+ LPSS/SSS) x max(measCycleSCell, DRX cycle) x CSSFintra
NOTE 1: LPSS/SSS is the number of SMTC periods not available at the UE during TPSS/SSS_sync_intra, where LPSS/SSS ≤ LPSS/SSS,deact,max. NOTE 2: LPSS/SSS, deact,max =20 for Max(DRX cycle, measCycleSCell)≤40 where DRX cycle is 0 for non-DRX, LPSS/SSS, deact,max =10 for 40<Max(DRX cycle, measCycleSCell)≤320, LPSS/SSS, deact,max =5 for DRX cycle>320. | 
DRX cycle | TSSB_time_index_intra
No DRX | (3+Lind) x measCycleSCell x CSSFintra
DRX cycle≤ 320ms | (3+Lind) x max(measCycleSCell, 1.5xDRX cycle) x CSSFintra
DRX cycle> 320ms | (3+Lind) x max(measCycleSCell, DRX cycle) x CSSFintra
NOTE 1: Lind is the number of SMTC periods not available at the UE during TSSB_time_index_intra, where Lind ≤ Lind,deact,max. NOTE 2: Lind,deact,max =12 for Max(DRX cycle, measCycleSCell)≤40 where DRX cycle is 0 for non-DRX, Lind,deact,max =6 for 40<Max(DRX cycle, measCycleSCell)≤320, Lind, deact,max =3 for DRX cycle>320. | 
DRX cycle | T SSB_measurement_period_intra
No DRX | (5+ Lmeas) x measCycleSCell x CSSFintra
DRX cycle≤ 320ms | (5+ Lmeas) x max(measCycleSCell, 1.5xDRX cycle) x CSSFintra
DRX cycle> 320ms | (5+ Lmeas) x max(measCycleSCell, DRX cycle) x CSSFintra
NOTE 1: Lmeas is the number of SMTC periods not available at the UE during T SSB_measurement_period_intra, where Lmeas ≤ Lmeas,deact,max. NOTE 2: Lmeas,deact,max =20 for Max(DRX cycle, measCycleSCell)≤40 where DRX cycle is 0 for non-DRX, Lmeas,deact,max =10 for 40<Max(DRX cycle, measCycleSCell)≤320, Lmeas,deact,max =5 for DRX cycle>320. | 

## Slide 37: Intra-Frequency Measurements, with Gaps
DRX cycle | TPSS/SSS_sync_intra
No DRX | max(600ms, (5+LPSS/SSS) x max(MGRP, SDMTC period)) x CSSFintra
DRX cycle≤ 320ms | max(600ms, ceil(1.5x (5+LPSS/SSS)) x max(MGRP, SDMTC period,DRX cycle)) x CSSFintra
DRX cycle>320ms | (5+LPSS/SSS) x max(MGRP, DRX cycle) x CSSFintra
NOTE 1: LPSS/SSS is the number of SMTC periods not available at the UE during TPSS/SSS_sync_intra, where LPSS/SSS ≤ LPSS/SSS,gaps,max. NOTE 2: LPSS/SSS,gaps,max =20 for Max(DRX cycle,SMTC period,MGRP)≤40 where DRX cycle is 0 for non-DRX, LPSS/SSS,gaps,max =10 for 40<Max(DRX cycle,SMTC period,MGRP)≤320, LPSS/SSS,gaps,max =5 for DRX cycle>320. | 
DRX cycle | TSSB_time_index_intra
No DRX | max(120ms, (3+Lind) x max(MGRP, SMTC period)) x CSSFintra
DRX cycle≤ 320ms | max(120ms, ceil(1.5x (3+Lind)) x max(MGRP, SMTC period,DRX cycle) x CSSFintra)
DRX cycle>320ms | (3+Lind) x max(MGRP, DRX cycle) x CSSFintra
NOTE 1: Lind is the number of SMTC periods not available at the UE during TSSB_time_index_intra, where Lind ≤ Lind,gaps,max. NOTE 2: Lind,gaps,max =12 for Max(DRX cycle,SMTC period)≤40 where DRX cycle is 0 for non-DRX, Lind,gaps,max =6 for 40<Max(DRX cycle,SMTC period)≤320, Lind,gaps,max =3 for DRX cycle>320. | 
DRX cycle | T SSB_measurement_period_intra
No DRX | max(200ms, (5+Lmeas) x max(MGRP, SDMTC period)) x CSSFintra
DRX cycle≤ 320ms | max(200ms, ceil(1.5x (5+Lmeas)) x max(MGRP, SDMTC period,DRX cycle)) x CSSFintra
DRX cycle>320ms | (5+Lmeas) x max(MGRP, DRX cycle) x CSSFintra
NOTE 1: Lmeas is the number of SMTC periods not available at the UE during T SSB_measurement_period_intra, where Lmeas ≤ Lmeas,gaps,max. NOTE 2: Lmeas,gaps,max =20 for Max(DRX cycle,SMTC period,MGRP)≤40 where DRX cycle is 0 for non-DRX, Lmeas,gaps,max =10 for 40<Max(DRX cycle,SMTC period,MGRP)≤320, Lmeas,gaps,max =5 for DRX cycle>320. | 

## Slide 38: Inter-Frequency Measurements: Lmax
Procedure | Rel-15 samples | Maximum number of DL LBT failures |  | 
 |  | Parameter name | Parameter value | Condition
PSS/SSS detection, with gaps | 8 | LPSS/SSS,gaps,max | 32 | Max(TDRX,TSMTC, MGRP)≤40
 |  |  | 16 | 40<Max(TDRX,TSMTC, MGRP)≤320
 |  |  | 8 | TDRX>320
Time index detection, with gaps | 3 | Lind,gaps,max | 12 | Max(TDRX, TSMTC, MGRP)≤40
 |  |  | 6 | 40< Max(TDRX, TSMTC, MGRP)≤320
 |  |  | 3 | TDRX>320
Measurement, with gaps | 8 | Lmeas,gaps,max | 32 | Max(TDRX, TSMTC, MGRP)≤40
 |  |  | 16 | 40< Max(TDRX, TSMTC, MGRP)≤320
 |  |  | 8 | TDRX>320

## Slide 39: Inter-Frequency Measurements: UE Behavior
Upon exceeded maximum number if DL LBT failures, the UE has to restart the corresponding procedure, e.g., PSS/SSS detection, time index detection, or measurements
At least for aperiodic measurements, the number of restarts due to exceeding the corresponding L*,max can be limited, after which the measurement procedure can be abandoned

## Slide 40: Inter-Frequency Measurements: Details
Condition NOTE1,2 | TPSS/SSS_sync_inter
No DRX | max(600ms, (8+LPSS/SSS) x max(MGRP, DSMTC period)) x CSSFinter
DRX cycle ≤ 320ms | max(600ms, ceil((8+LPSS/SSS)x1.5) x max(MGRP, DSMTC period, DRX cycle)) x CSSFinter
DRX cycle > 320ms | (8+LPSS/SSS) x DRX cycle x CSSFinter
NOTE 1: DRX or non DRX requirements apply according to the conditions described in clause 3.6.1. NOTE 2: In EN-DC operation, the parameters, timers and scheduling requests referred to in clause 3.6.1 are for the secondary cell group. The DRX cycle is the DRX cycle of the secondary cell group. NOTE 3: LPSS/SSS is the number of SMTC periods not available at the UE during TPSS/SSS_sync_inter, where LPSS/SSS ≤ LPSS/SSS,max. NOTE 4: LPSS/SSS,max =32 for Max(DRX cycle,SMTC period,MGRP)≤40 where DRX cycle is 0 for non-DRX, LPSS/SSS,max =16 for 40<Max(DRX cycle,SMTC period,MGRP)≤320, LPSS/SSS,max =8 for DRX cycle>320. | 
Condition NOTE1,2 | TSSB_time_index_inter
No DRX | max(120ms, (3+Lind) x max(MGRP, SMTC period)) x CSSFinter
DRX cycle ≤ 320ms | max(120ms, ceil((3+Lind) x 1.5) x max(MGRP, SMTC period, DRX cycle)) x CSSFinter
DRX cycle > 320ms | (3+Lind) x DRX cycle x CSSFinter
NOTE 1: DRX or non DRX requirements apply according to the conditions described in clause 3.6.1. NOTE 2: In EN-DC operation, the parameters, timers and scheduling requests referred to in clause 3.6.1 are for the secondary cell group. The DRX cycle is the DRX cycle of the secondary cell group. NOTE 3: Lind is the number of SMTC periods not available at the UE during TSSB_time_index_inter, where Lind ≤ Lind,max. NOTE 4: Lind,max =12 for Max(DRX cycle,SMTC period,MGRP)≤40 where DRX cycle is 0 for non-DRX, Lind,max =6 for 40<Max(DRX cycle,SMTC period,MGRP)≤320, Lind,max =3 for DRX cycle>320. | 

## Slide 41: Inter-Frequency Measurements: Details (cont.)
Condition NOTE1,2 | T SSB_measurement_period_inter
No DRX | max(200ms, (8+Lmeas) x max(MGRP, SDMTC period)) x CSSFinter
DRX cycle ≤ 320ms | max(200ms, ceil((8+Lmeas) x 1.5) x max(MGRP, SDMTC period, DRX cycle)) x CSSFinter
DRX cycle > 320ms | (8+Lmeas) x DRX cycle x CSSFinter
NOTE 1: DRX or non DRX requirements apply according to the conditions described in clause 3.6.1 NOTE 2: In EN-DC operation, the parameters, timers and scheduling requests referred to in clause 3.6.1 are for the secondary cell group. The DRX cycle is the DRX cycle of the secondary cell group. NOTE 3: Lmeas is the number of SMTC periods not available at the UE during T SSB_measurement_period_inter, where Lmeas ≤ Lmeas,max. NOTE 4: Lmeas,max =32 for Max(DRX cycle,SMTC period,MGRP)≤40 where DRX cycle is 0 for non-DRX, Lmeas,max =16 for 40<Max(DRX cycle,SMTC period,MGRP)≤320, Lmeas,max =8 for DRX cycle>320. | 

## Slide 42: SFTD Measurements (TS 36.133)
Introduce a maximum value for NLBT-fail. When reaching the maximum value, the UE terminates the SFTD measurement. A suitable maximum value, and whether it shall depend e.g. on SMTC period or DRX cycle, is for further investigation
Time difference between frame timing acquisition for PCell and PSCell, respectively, shall fullfill |t1-t2| < max(40ms, SMTC)
For inter-RAT SFTD towards NR-U with LBT, the UE shall continue to search for a cell until whichever comes first of: (a) a cell is found whereby SFTD is reported, (b) the SFTD measurement is deconfigured by MeNB, (c) the PCell is changed, or (d) a UE timer expires
  A suitable UE timer value is for further investigation
The inter-RAT SFTD reporting delay requirement is based on that the UE shall be capable of reporting SFTD at latest X ms after the start of a period with Y consecutively transmitted SSBs
  Values of X and Y depend on the configuration in use, and are for further investigation