## Slide 1: WF on FR1 intra-band contiguous UL CA RF requirement
Huawei, HiSilicon
R4-1912422
3GPP TSG-RAN WG4 #92bis
Oct 14th – 18th, 2019
Chongqing, China

## Slide 2: Background
ACLR MBW for MPR simulation assumption was agreed in the last meeting [1] as:
100% aggregated channel bandwidth(BWchannel_CA) for wanted and 99% aggregated channel bandwidth for adjacent
It was proposed to define BWchannel_CA as BWChannel_CA – 2*max(GB(low),GB(high)) for both wanted and adjacent in [2]. Since min GB is varied with the SCS adoption, BWchannel_CA will be varied with the SCS if it is defined accordingly.
In TS 38.101-1, common largest SCS is specified for calculating the nominal channel space for CA
FOOB for intra-band contiguous UL CA was agreed in the last meeting as BWchannel_CA+5MHz

## Slide 3: WF
RAN4 define ACLR MBW as BWChannel_CA – 2*max(GB(low),GB(high)) for both wanted and adjacent.
BWChannel_CA ,GB(low) , and GB(high) definition for UL CA FOOB and ACLR MBW are not flexible with SCS.
For BWChannel_CA= + Foffset,high + Foffset,low, GB(low), and GB(high) definition, the SCS for each CC use the largest μ value among the subcarrier spacing configurations supported in the operating band for both of the channel bandwidths according to Table 5.3.5-1 in TS 38.101-1.

## Slide 4: Reference
[1] R4-1910273, “WF for intra-band UL CA for FR1 power class 3”, RAN4 #92, Huawei, HiSilicon, Qualcomm, Skyworks, MTK
[2] R4-1909583 “General Requirements for Intra-band Contiguous ULCA for FR1”, RAN4 #92, Qualcomm
[3] R4-1912383 “overview of FR1 UE RF requirement for Rel-16”, Huawei, HiSilicon, RAN4 #92bis