## Slide 1: Way forward on CLI remaining RRM open issues
3GPP TSG-RAN WG4 Meeting #92BIS Chongqing, China, 14 - 18 Oct. 2019
Agenda Item: 8.2.3
R4-1912667
LG Electronics

## Slide 2: Timing error for CLI measurement
Definition for DL timing error (TCLI)
  Consider cell phase synchronization error for TCLI derivation and for residual timing error assumptions for deriving measurement accuracy
  TCLI = Tc*NTA_offset + Tother
    Tother = Tpropagation_delay + Tcell_phase_synchronization
    Tother = 4.67usec for FR1 and 3.67usec for FR2
      under the assumption that ISD=500m for FR1 and ISD=200m for FR2
Residual timing error for measurement accuracy
  4.67usec for FR1 and 3.67usec for FR2

## Slide 3: Residual timing error (for information only)
Residual timing error for measurement accuracy
  For example of FR1, if Tpropagation_delay =1.67usec, -1.33usec < Tother < 4.67usec.
  A UE know NTA_offset value, but the UE cannot know Tpropagation_delay and Tcell_phase_synchronization since there is no any timing tracking for SRS measurement.
  SRS resources are transmitted unknown neighbor cells, so the UE can assume average cell phase synchronization error as 0, then constant offset value will be between NTA_offset and NTA_offset+Tpropagation_delay. Therefore, maximum residual timing error will be 4.67usec.

## Slide 4: SRS-RSRP measurement requirement
Companies are encouraged to provide simulation results for SRS-RSRP measurements based on R4-1907392 using following options:
  Reference SNR point for side condition is SNR with zero timing error
    Option 1: SNR 3dB
    Option 2: SNR -1dB
    Other higher SNR level is not precluded
  The number of sample for measurement accuracy
    Option 1: 1 samples
    Option 2: 3 samples
  Timing error
    4.67usec for FR1 and 3.67usec for FR2
To finalize CLI core part, RAN4 should decide one option for above issues in next meeting.

## Slide 5: UE behavior for CLI measurement
Scheduling restriction for CLI measurement
  SRS-RSRP measurement
    Depending on the UE capability, UE is not expected to receive PDCCH/PDSCH on SRS-RSRP measured OFDM symbols, and on Y data symbol before SRS-RSRP measured symbol in intra-band CA.
      Y = 1 : 15kHz/30kHz SCS for FR1 and 60kHz SCS for FR2
      Y = 2 : 60kHz SCS for FR1 and 120kHz SCS for FR2
  CLI-RSSI measurement
    Depending on the UE capability, UE is not expected to receive PDCCH/PDSCH on CLI-RSSI measured OFDM symbols , and on X data symbol before SRS-RSRP measured symbol in intra-band CA.
      X = 1 : 15kHz/30kHz SCS for FR1 and 60kHz SCS for FR2
      X = 2 : 60kHz SCS for FR1 and 120kHz SCS for FR2