## Slide 1: Way forward on PDSCH CA normal demodulation requirements
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #92bis
Chongqing, China, 14th – 18th October, 2019 Agenda Item: 8.18.1
R4-1912709

## Slide 2: SCS and Channel bandwidth
      Single carrier SCS
  FR1
    FR1 FDD:15kHz
    FR1 TDD: 30kHz, FFS 15kHz
  FR2: 120kHz
      Single carrier channel bandwidth for the FR1 FDD 15kHz, FR1 TDD 30kHz and FR2 120kHz SCS
  All configurable channel bandwidths
      Scenarios with different SCSs on different CCs for inter-band CA
  FR1 FDD 15 kHz SCS and TDD 30 kHz SCS
      If TDD 15 kHz requirements will be defined then
  All configurable channel bandwidths for TDD 15 kHz will be considered
  TDD 15 kHz is only tested in inter-band CA scenarios (i.e. FR1 TDD 15 kHz SCS and TDD 30 kHz SCS)

## Slide 3: Test parameters
      Rank:
  FR1: Rank 2 for 2Rx and 4Rx
  FR2:
    Option 1: Rank 2
    Option 2: Rank 1
      MCS:
  FR1: MCS 13 (16QAM, CR 1/2)
  FR2:
    Option 1: MCS 13 (16QAM, CR 1/2)
    Option 2: MCS 4 (QPSK, CR 1/3)
    Option 3: MCS 10 or 11 (16 QAM)
    Other options are not precluded
      Receiver type: MMSE-IRC
      Not cover 16 HARQ processes

## Slide 4: Test parameters
      PDSCH scheduling:
  Self-carrier scheduling for each carrier
      PUCCH capacity
  Check if there is PUCCH capacity issue for the maximum numbers of CCs in the Sep version of Rel-16 core spec
      HARQ process number for TDD-FDD CA: FFS
      Single carrier performance for TDD-FDD CA
  Further discuss whether the requirement of one TDD/FDD carrier in TDD-TDD/ FDD-FDD CA can be applied for TDD-FDD CA with TDD Pcell or FDD Pcell.

## Slide 5: Test applicability rule
      Test applicability for different CA duplex mode
  Option 1: Test all the supported CA duplex mode
  Other options are not precluded
      FFS categorizing of CA capabilities
      FFS on test of different CA capabilities
      FFS on selection of CA configuration(s) for test among supported CA configurations
      FFS on selection CBW combination for test for selected CA configuration

## Slide 6: Feasible FR2 SNR levels
Take into account values from table below in definition of FR2 Normal CA requirements
Operating band | SNR (dB) / Aggregated Channel bandwidth |  | 
 | 200 MHz | 400 MHz | 800 MHz
n257 | 21.8 | 18.8 | 15.8
n258 | 21.8 | 18.8 | 15.8
n260 | 16 | 13 | 10
n261 | 21.8 | 18.8 | 15.8