## Slide 1: WF on IAB RRM Requirements
Qualcomm, Samsung, AT&T, DOCOMO, KDDI
3GPP TSG-RAN WG4 Meeting #92 Chongqing, China, Oct 14th - 18th, 2019
R4-1912715

## Slide 2: Background - I
RAN4 already agreed to the following during this meeting.
Requirements | Comments | Is requirement needed?
Cell reselection | Intra-frequency Inter-frequency | No
Handover |  | FFS Yes No
RRC Connection Mobility Control | RRC re-establishment Random access RRC release with redirection | Yes
SCell activation/deactivation delays |  | No
Interruptions related to SCells addition, release, activation, deactivation | Interruptions on serving cells due to any of the addition, release, activation, or deactivation procedures | No
PSCell addition/release delays |  | No
Active BWP switching | Interruptions at active BWP switching Active BWP switching delay | No
TCI switching | TCI switching delay | FFS

## Slide 3: Background - II
RAN4 already agreed to the following during this meeting.
Requirements | Comments | Is requirement needed?
RLM | Requirements for RLM, e.g., based on SSB, CSI-RS or both | FFS for PCell and/or PSCell
Link recovery procedures | Requirements for SSB-based and CSI-RS based beam failure detection and candidate beam detection | FFS for PCell and PSCell
Measurements requirements (time duration, number of cells, etc.) |  | FFS for L1-RSRP evaluation period. Needs further discussion for L3-RSRP evaluation period.
Measurement accuracy requirements |  | FFS for L1-RSRP Needs further discussion for L3-RSRP
MT timing related requirements | MT maximum receive timing difference MT transmit timing MT maximum transmit timing difference Timing Advance | MT transmit timing (Te and Tq) Timing Advance FFS: MT maximum receive timing difference MT maximum transmit timing difference
Switching time between MT and DU | --- | FFS
DU timing related requirements | 3 us requirement T_delta command | Yes (3 us requirement / cell phase synch) FFS for Tdelta command

## Slide 4: Background - III
IAB network planning depends very much on defining some minimum RRM requirements for the IAB MTs. Without RRM requirements it is not possible for an operator to plan for an IAB network.
Ensuring inter-operability among different IAB nodes is very important to guarantee the performance of an IAB network. Inter-operability can be achieved by defining RRM requirements for IAB nodes.
FR2 is the main use case for Rel-16 IAB networks. Defining beam management related requirements is essential to guarantee performance in FR2 IAB network.
Reference: R4-1909929, Defining RRM requirements for IAB nodes.

## Slide 5: Way Forward - I
RAN4 agrees to define IAB RRM requirements based on the following table.
Requirements | Comments | Is requirement needed?
Cell reselection | Intra-frequency Inter-frequency | No (already agreed)
Handover |  | FFS
RRC Connection Mobility Control | RRC re-establishment Random access RRC release with redirection | Yes (already agreed)
SCell activation/deactivation delays |  | No (already agreed)
Interruptions related to SCells addition, release, activation, deactivation | Interruptions on serving cells due to any of the addition, release, activation, or deactivation procedures | No (already agreed)
PSCell addition/release delays |  | No (already agreed)
Active BWP switching | Interruptions at active BWP switching Active BWP switching delay | No (already agreed)
TCI switching | TCI switching delay | Yes

## Slide 6: Way Forward - II
RAN4 agrees to define IAB RRM requirements based on the following table.
Requirements | Comments | Is requirement needed?
RLM | Requirements for RLM, e.g., based on SSB, CSI-RS or both | Yes for PCell and PSCell
Link recovery procedures | Requirements for SSB-based and CSI-RS based BFD and CBD | Yes for PCell and PSCell
Measurements requirements (time duration, number of cells, etc.) |  | No
Measurement accuracy requirements |  | No
MT timing related requirements | MT transmit timing (Te and Tq) Timing Advance | Yes (already agreed)
 | MRTD MTTD | - Yes for NR CA and EN-DC
Switching time between MT and DU | --- | TBD in RAN4 RF session
DU timing related requirements | 3 us requirement | Yes (already agreed)
 |  | No
 | T_delta command |