## Slide 1: Way Forward on MR-DC RRM
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN WG4 Meeting #92bis R4-1912717
Chongqing, China, 14-18 Oct 2019

## Slide 2: Background
For early Measurement reporting following was agreed:
  Requirements for early measurement reporting will be the same in Inactive mode and Idle mode using same principle as currently defined Inactive measurement requirements.

## Slide 3: Way Forward
For Idle measurements for early Measurement reporting companies are encouraged to provide input and views on following:
  For NR,
    Should RAN4 use the concept of UE idle mode measurement capability (total number of carrier) for defining requirements for early measurement reporting?
    Should RAN4 adopt the concept of overlapping and non-overlapping carriers for defining requirements for early measurement reporting?
  For NR, the number of carriers the UE should be able to report early measurements:
    NR inter-frequency carriers
  Use of measurement thresholds to decide when measurements for early reporting should be performed by the UE.
  Impact on mobility measurement performance from measurements for early reporting.

## Slide 4: Way Forward
For Idle measurements for introducing Inter-RAT early measurements in 36.133 companies are encouraged to provide input and views on following:
  For LTE,
    Principle of introducing NR inter-RAT measurements for early reporting in LTE.
    Number of NR carriers supported for early measurement reporting.
    Detected cell status upon transitioning from connected to:
      Idle mode, or
      inactive mode

## Slide 5: Way Forward
For Idle measurements for UE behaviour, companies are encouraged to provide input and views on following, based on RAN2 outcome:
  For NR,
    At cell change, while the T331 timer is running, what is UE behaviour regarding measurements configured for EMR when:
      One cell change occur
      More than one cell change occur
    At cell change, what is the UE behaviour related to reporting of EMR
      RAN4 needs to define UE behaviour and the applicable requirements for EMR when a cell change occurs while the timer T331 is running
        Option1: UE always stops
        Option 2: UE always continues
        Option 3: UE is either stops/restarts or continues the early measurement, e.g., based on the T331 timer and the time point of the cell change relative to the timer, measurement type (inter-frequency, inter-RAT, or intra-frequency), and/or the type of the change or no change in the cell/carrier relation caused by the cell change
          For example, the UE could restart the measurement if the carrier relation or measurement type changes, say from overlapping carriers to non-overlapping carriers or from intra-frequency to inter-frequency, while the UE could continue if the carrier relation or measurement type do not change
        If the stops the early measurements, will they be reported?
          FFS: The stopped early measurement based on old samples (before the cell change) may still be reported to the network, at least when the remaining time to the expiry of the T331 timer is short or not sufficient for the new measurement (after the cell change)
        If the UE continued, which requirement applies?
          The early measurement, which was continued over a time period with one or more cell changes and was performed on a carrier which was a non-overlapping carrier with the serving carrier before and/or after the cell change, shall meet the requirement corresponding to that for the non-overlapping carrier
          FFS for other scenarios
  The concept of unknown cells considering early measurement reporting.
    The UE shall not report or indicate the availability of measurements for EMR for unknown cells
    If a cell measured for EMR purpose gets unknown while the T331 timer is running, the UE has to perform the cell identification prior to measuring that cell
  Impact on early measurements after T331 stops and before reporting EMR
    Observation: A UE may continue the measurements at least on the overlapping carriers (e.g., for mobility purpose) even after T3331 stops and report them for EMR purpose
    If the UE continues a measurement after T331, e.g. on the overlapping carrier, RAN4 specifies applicable requirements if such measurements can be reported for EMR

## Slide 6: Way Forward
For Direct Scell activation, companies are encouraged to provide input and views on following delay requirements:
  For NR, based on the agreement in RAN4#92:
    RAN4 to discuss T2 and T3 definitions:
      T2:
        Tuncertainty + ra-ResponseWindow
        The delay for obtaining a valid TA command for the target PCell
        The time to acquire TA in PCell which depends on RA response window (10ms or less) and time from PRACH transmission to start of window as specified in TS 38.213 clause 8.2
      T3:
        N1 + 0.5 ms
        The delay for applying the received TA for uplink transmission in the target PCell, and greater than or equal to k+1 slot, where k is defined in clause 4.2 in TS 38.213
        The delay for applying the received TA in the target PCell as specified in TS 38.213 clause 4.2
    Input also on following aspects,
      Input on whether to replace Tinterupt_window to adapt it to NR requirements
      Provide input on the values for TRRC_processing, T1, Tactivation_time, Tinterrupt, TCSI_report,