## Slide 1: 3GPP TSG-RAN WG4 Meeting #92Bis Chongqing, China, 14 - 18 October, 2019
Huawei, HiSilicon
Way forward on NR HST PUSCH demodulation requirements
R4-1912728

## Slide 2: Maximum Doppler shift
Maximum Doppler shift
  Single tap HST 350km/h
    15kHz SCS: 1340Hz
    30kHz SCS: 2334Hz
  Single tap HST 500km/h
    15kHz SCS :
      Option 1: 1944Hz
      Option 2: 1750Hz
    30kHz SCS:
      Option 1: 3334Hz
      Option 2: 3000Hz

## Slide 3: Channel Model
HST single tap channel model for 350km/h and 500km/h
  Tunnel channel model
    Ds = 300m
    Dmin = 2m
  Open space
    Ds = 700m
    Dmin = 150m
Fading channel
  Focus on the PUSCH requirements with HST scenario firstly
  Start after March on study of PUSCH requirements with multi-path fading channel under high Doppler value

## Slide 4: PUSCH
Waveform
  Focus on CP-OFDM waveform.
  Start on study of PUSCH requirements with DFT-s-OFDM waveform after March, 2020
SCS
  15kHz
    350km/h: 2.1GHz
    500km/h: 1.9GHz or 2.1GHz
  30kHz for 3.6GHz
CBW for CP-OFDM
  Focus on 10MHz CBW/15KHz SCS, 40MHz CBW/30KHz SCS
  Start to work on 5MHz CBW/15KHz SCS, 10Mhz CBW/30KHz SCS after March, 2020
  Similar applicability rule of channel bandwidths as existing PUSCH performance requirements will be used for HST
Antenna configuration
  For tunnel
    Option 1: 1x1
    Option 2: 1x2 (baseline for simulation alignment)
  For open space
    Option 1: 1x2 (baseline for simulation alignment)
    Option 2: 1x8
MCS
  Option 1: MCS#2
  Option 2: MCS#16
  Option 3: MCS#2 and MCS#16
  MCS#2 and MCS#16 for simulation alignment

## Slide 5: PUSCH
Reference signal
  Option 1: DMRS (Baseline)
  Option 2: DMRS + PT-RS
    Option 1: 1+1 DMRS + PTRS L=1 or 2
    Other options are not precluded
DMRS Configuration if no PTRS
  For 350km/h targeting velocity: DMRS 1+1+1 (type 1, single-symbol DMRS).
  For 500km/h targeting velocity
    30kHz SCS: DMRS 1+1+1 for simulation alignment
    15kHz SCS: 1: 1+1+1 (type 1, single-symbol DMRS)
l0 for PUSCH mapping type A
  Provide the simulation results for 350km/h and 500km/h and evaluate the following configurations and make decision:
    Option 1: l0 = 3
    Option 2: l0 = 2
  Same value for both 350km/h and 500km/h can be considered
Test metric
  70% of maximum throughput

## Slide 6: Simulation assumption for PUSCH
Parameter | Value |  |  |  | 
 | v = 350km/h |  | v = 500km/h |  | 
Transform precoding | Disabled |  | Disabled |  | 
Number of Tx | 1 |  | 1 |  | 
Number of Rx | Option 1: 1 Rx Option 2: 2 Rx (baseline) |  | Option 1: 2 Rx (baseline) Option 2: 8 Rx |  | 
Number of layers | 1 |  | 1 |  | 
SCS | 15kHz, 30kHz |  | 15kHz, 30kHz |  | 
Reference signal | DMRS type 1 with 1+1+1 |  | DMRS type 1 with 1+1+1 |  | 
l0 | Option 1: l0 = 3 Option 2: l0 = 2 |  | Option 1: l0 = 3 Option 2: l0 = 2 |  | 
symbols length | 14 |  | 14 |  | 
start symbol index | 0 |  | 0 |  | 
Time domain resource allocation type | type A |  | type A |  | 
Frequency domain resource | Full applicable test bandwidth |  | Full applicable test bandwidth |  | 
MCS index | 2 and 16 (both for alignment) |  | 2 and 16 (both for alignment) |  | 
Maximum Doppler shift | 15kHz SCS: 1340Hz | 30kHz SCS: 2334Hz | 15kHz SCS: Option 1: 1944Hz Option 2: 1750Hz |  | 30kHz SCS: Option 1: 3334Hz Option 2: 3000Hz
Carrier frequency (GHz) | 15kHz SCS: 2.1GHz 30kHz SCS: 3.6GHz |  | 15kHz SCS: [2.1GHz or 1.9GHz] 30kHz SCS: 3.6GHz |  | 
Propagation condition | HST single-tap channel model: Tunnel: Ds=300m, Dmin=2m Open space: Ds=700m, Dmin=150m |  |  |  | 
SCS and BW | 15kHz: 10MHz; 30kHz: 40MHz |  |  |  | 
Timing offset | 0 |  |  | 0 | 
Frequency offset | 0 |  |  | 0 | 
Code block group, Frequency hopping, Limited buffer rate matching | Disabled |  |  | Disabled | 
Number of HARQ transmissions | 4 |  |  | 4 | 
Testing metric | SNR @70% of maximum throughput |  |  | SNR @70% of maximum throughput | 

## Slide 7: UL timing adjustment
Candidate scenarios on table:
Scenario for requirements
  Scenario Y
  Other scenarios can be discussed after March.
SRS
  Transmit SRS (optional) for uplink timing advance requirement
    Option 1:
      Transmit SRS in the last symbol in the special slot for TDD mode
      Transmit SRS in slot#1 in radio frames for FDD mode
    Other options are not precluded
DMRS
  Option 1: 1+1
  Option 2: 1+1+1
  Other options not precluded
Parameter | Scenario X | Scenario Y | Scenario Z
Channel model | Stationary UE: AWGN Moving UE: TDLC300-400 | Stationary UE: AWGN Moving UE: AWGN | Stationary UE: AWGN Moving UE: AWGN
UE speed | 120 km/h | 350 km/h | 500 km/h
CP length | Normal |  | 
A | 10 µs |  | 
Δω | 0.04 s-1 | 0.13 s-1 | 0.18 s-1