## Slide 1: 3GPP TSG-RAN WG4 Meeting #92b Chongqing, China, 14- 18 Oct, 2019
Samsung
Way forward on NR HST PRACH
R4-1912729

## Slide 2: Background
The following WF was approved:
  R4-1910128 WF on demodulation for NR BS HST demodulation requirements , RAN4#92

## Slide 3: PRACH
Channel model
  AWGN
  TDL-C fading channel, Frequency offset is 400Hz
PRACH format
  For 350km/h velocity, use PRACH format 0
  For 500km/h velocity, use PRACH format A2/B4/C2
    FFS if PRACH format 0 shall be used
Restricted set for PRACH format 0
  Both Type A and Type B
Test case applicability is FFS

## Slide 4: Frequency offset
Frequency offset under AWGN for PRACH format 0 for 350km/h
  Restricted set Type A
    High-mobility scenario: 1340Hz
    FFS: Low mobility scenario with 0Hz
  Restricted set Type B
    High-mobility scenario
      Option 1: 2334Hz
      Option 2: 1875Hz
    FFS: Low mobility scenario with 0Hz
Frequency offset for PRACH formats with short sequence length targeting 500km/h
  Align with PUSCH maximum Doppler shift

## Slide 5: Test Preamble Parameters
Format 0
  Restricted set type A
    Option 1: {Ncs, logical sequence index, V} ={15, 384,30} (Reusing the existing LTE format 0 parameters with type A )
    Option 2: {Ncs, logical sequence index, V} ={15, 384,36}
    Other options are not precluded
    Sequence should not have unusually good performance
  Restricted set type B
    Option 1: {Ncs, logical sequence index, V} ={15, 30,30} (Reusing the existing LTE format 0 parameters with type B)
    Option 2: {Ncs, logical sequence index, V} ={15, 384,36}
    Other options are not precluded
    Sequence should not have unusually good performance
Notes: Samsung: the values are from LTE.
Ericsson:

## Slide 6: Test Preamble Parameters
Short sequence format
  15kHZ
    Option 1: {Ncs, logical sequence index, V} ={23,0,0} (Reusing the existing NR parameters for short format under 15KHz)
    Other options are not precluded
  30KHZ
    Option 1: {Ncs, logical sequence index, V} ={46, 0,0} (Reusing the existing NR parameters for short format under 30KHz)
    Other options are not precluded
Timing error tolerance for AWGN and TDLC 300-100
  Other values are not precluded.
Format | Scs | AWGN | TDLC300-100
0 | 1.25 | 1.04us | 2.55us
A2,B4,C2 | 15 | 0.52us | 2.03us
 | 30 | 0.26us | 1.77us