## Slide 1: WF on inter-frequency without MG
CMCC
R4-1912739
3GPP TSG-RAN WG4 Meeting #92bis
Chongqing, China, 14th – 18th October 2019

## Slide 2: Impact on specs
Definition of inter-frequency measurement without MG
CSSF within gap and CSSF outside gap
The delay requirements for inter-frequency measurement without MG
Scheduling and measurement restriction
UE capability

## Slide 3: Definition
The UE can perform inter-frequency SSB based measurements without measurement gaps if
  the SSB is completely contained in the active BWP of the UE.

## Slide 4: CSSF factor
The definitions of CSSF within gap and outside gap are not changed.
The number of searchers is up to 2 when discussing the requirement of CSSF outside gap.
For CSSF outside gap, the performance of PCC in NR SA should remain the same. Therefore, the inter frequency MO without gap shares the same searcher as all the other SCCs.
Notes: 1910819

## Slide 5: The delay requirements
Option 1: proposal in slide 6~9 with CSSFinter= CSSFoutside_gap,i
Option 2: same as inter-frequency measurement requirements in Rel-15
Other options are not precluded
Decision will be made in next meeting

## Slide 6: The delay requirements (1)
DRX cycle | TPSS/SSS_sync_inter
No DRX | max( 600ms, ceil( 5 x Kp) x SMTC period )Note 1 x CSSFinter
DRX cycle≤ 320ms | max( 600ms, ceil(1.5x 5 x Kp) x max(SMTC period,DRX cycle)) x CSSFinter
DRX cycle>320ms | ceil(5 x Kp) x DRX cycle x CSSFinter
NOTE 1: If different SMTC periodicities are configured for different cells, the SMTC period in the requirement is the one used by the cell being identified | 
Table1: Time period for PSS/SSS detection, (Frequency range FR1)
DRX cycle | TPSS/SSS_sync_inter
No DRX | max(600ms, ceil(Mpss/sss_sync_inter x Kp) x SMTC period)Note 1 x CSSFinter
DRX cycle≤ 320ms | max(600ms, ceil(1.5 x Mpss/sss_sync_inter x Kp) x max(SMTC period,DRX cycle)) x CSSFinter
DRX cycle>320ms | ceil(Mpss/sss_sync_inter x Kp) x DRX cycle x CSSFinter
NOTE 1: If different SMTC periodicities are configured for different cells, the SMTC period in the requirement is the one used by the cell being identified | 
Table2: Time period for PSS/SSS detection, (Frequency range FR2)

## Slide 7: The delay requirements (2)
DRX cycle | TSSB_time_index_intra
No DRX | max(120ms, ceil( 3 x Kp ) x SMTC period)Note 1 x CSSFinter
DRX cycle≤ 320ms | max(120ms, ceil (1.5 x 3 x Kp) x max(SMTC period,DRX cycle)) x CSSFinter
DRX cycle>320ms | Ceil(3 x Kp) x DRX cycle x CSSFinter
NOTE 1: If different SMTC periodicities are configured for different cells, the SMTC period in the requirement is the one used by the cell being identified | 
Table3: Time period for time index detection (Frequency range FR1)
Condition NOTE1,2 | TSSB_time_index_inter
No DRX | max(200ms, MSSB_index_inter x max(MGRP, SMTC period)) x CSSFinter
DRX cycle ≤ 320ms | max(200ms, (1.5 x MSSB_index_inter) x max(MGRP, SMTC period, DRX cycle)) x CSSFinter
DRX cycle > 320ms | MSSB_index_inter x DRX cycle x CSSFinter
NOTE 1: DRX or non DRX requirements apply according to the conditions described in clause 3.6.1 NOTE 2: In EN-DC operation, the parameters, timers and scheduling requests referred to in clause 3.6.1 are for the secondary cell group. The DRX cycle is the DRX cycle of the secondary cell group. | 
Table4: Time period for time index detection (Frequency range FR2)

## Slide 8: The delay requirements (3)
DRX cycle | T SSB_measurement_period_intra
No DRX | max(200ms, ceil( 5 x Kp) x SMTC period)Note 1 x CSSFinter
DRX cycle≤ 320ms | max(200ms, ceil(1.5x 5 x Kp) x max(SMTC period,DRX cycle)) x CSSFinter
DRX cycle>320ms | ceil( 5 x Kp ) x DRX cycle x CSSFinter
NOTE 1: If different SMTC periodicities are configured for different cells, the SMTC period in the requirement is the one used by the cell being identified | 
Table5: Measurement period for interfrequency measurements without gaps(Frequency FR1)
DRX cycle | T SSB_measurement_period_intra
No DRX | max(400ms, ceil(Mmeas_period_inter x Kp) x SMTC period)Note 1 x CSSFinter
DRX cycle≤ 320ms | max(400ms, ceil(1.5x Mmeas_period_inter x Kp) x max(SMTC period,DRX cycle)) x CSSFinter
DRX cycle>320ms | ceil(Mmeas_period_inter xKp) x DRX cycle x CSSFinter
NOTE 1: If different SMTC periodicities are configured for different cells, the SMTC period in the requirement is the one used by the cell being identified | 
Table6: Measurement period for interfrequency measurements without gaps(Frequency FR2)

## Slide 9: The delay requirements (4)
Mpss/sss_sync_inter: For a UE supporting FR2 power class 1, Mpss/sss_sync_inter = 64 samples. For a UE supporting FR2 power class 2, Mpss/sss_sync_inter = 40 samples. For a UE supporting FR2 power class 3, Mpss/sss_sync_inter = 40 samples. For a UE supporting FR2 power class 4, Mpss/sss_sync = 40 samples.
MSSB_index_inter: For a UE supporting power class 1, MSSB_index_inter = 40 samples. For a vehicle mounted UE supporting power class 2, Mpss/sss_sync_inter = 24 samples. For a UE supporting power class 3, MSSB_index_inter = 24 samples. For a UE supporting power class 4, Mmeas_period_inter = 24 samples.
Mmeas_period_inter: For a UE supporting FR2 power class 1, Mmeas_period_inter =64 samples. For a vehicle mounted UE supporting FR2 power class 2, Mpss/sss_sync_inter=40 samples. For a UE supporting FR2 power class 3, Mmeas_period_inter =40 samples. For a UE supporting FR2 power class 4, Mmeas_period_inter = 40 samples.
When interfrequency SMTC is fully non overlapping with measurement gaps or interfrequency SMTC is fully overlapping with MGs, Kp=1
When interfrequency SMTC is partially overlapping with measurement gaps, Kp = 1/(1- (SMTC period /MGRP)), where SMTC period < MGRP

## Slide 10: Scheduling and measurement restriction
The scheduling and measurement restriction for intra-frequency measurements under the condition of deriveSSB_IndexFromCell is not enabled can be used as baseline for inter-frequency measurement without measurement gaps

## Slide 11: UE capability
FFS on the need of UE capability for UE supporting inter-frequency without MG.
For release 16 UE which supports inter-frequency measurement without gap, a measurement gap pattern may still be provided by the network.
  When configured MG is fully overlapped with interfrequency SMTC and interfrequency SSB is completely contained in the active BWP of the UE, the UE is expected to meet rel-15 gap based requirements.