## Slide 1: Way Forward on One-time UE transmit timing adjustment
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN WG4 Meeting #92bis R4-1912763
Chongqing, China, 14-18 Oct 2019

## Slide 2: Background
During the RAN4#92bis meeting a number of issues were discussed considering one shot timing adjustment.
Following issues were listed:
  The impacts of uplink reception at gNB side due to one-shot adjustment
  The accuracy of one-shot timing adjustment (Te1)
  The threshold H for applying one-shot adjustment
  Interruption requirement due to one-shot adjustment
  Maximum value limitation for one-shot timing adjustment

## Slide 3: Background
UE has at least following reference signals for time tracking:
  SSB
  UE is required to adjust UL transmit timing according to 38.133
  gNB is expecting that the UE adjusts the UL transmit timing according to 38.133

## Slide 4: Background
Due to UE Rx beam change, the first DL path may change e.g. from path 1 to path 2.
This may lead to a need to adjust the UL transmit timing.
Problem:
  UE changes Rx beam autonomously
  gNB expect UL transmit timing adjustment according to 38.133
  Such path change may lead to jump in DL timing
  Such jump may need larger adjustment in UL timing

## Slide 5: Way Forward
Companies should analyse and give input on the open issues on page 2 for RAN4#93.
Following should be considered:
  RS available for time tracking
Rel-15 solution or potentially later