## Slide 1: WF on TCI state and spatial relation switch
Mediatek Inc.
3GPP TSG-RAN WG4 #92bis Meeting
Chongqing, China, 14th - 18th Oct, 2019
R4-191xxxx

## Slide 2: Issue 1:TCI state switch of the CSI-RS for CQI and spatial relation switch
Background
  CSI-RS for CQI reporting configuration can be updated with new TCI state by RRC, MAC CE or DCI
  The UE uplink channel and RS can be QCLed with a downlink RS based on the spatial relation configuration. Spatial relation can also be configured or indicated by RRC, MAC CE or DCI.

## Slide 3: Issue 1:TCI state switch of the CSI-RS for CQI and spatial relation switch
RAN4 should finalize the following requirements in Rel-16 time frame
  The possible scenarios for CSI-RS configuration update for CQI
    Option 1: New TCI state is configured for the same CSI-RS for CQI to align with the target TCI state for PDSCH
    Option 2: New CSI-RS configuration with new TCI state is configured to align with the target TCI state for PDSCH
  UE behavior when the TCI-state for CQI reporting is not within the active TCI state list for PDSCH
  The possible delay requirement for CSI-RS configuration update for CQI
  The delay requirement for spatial relation switch for uplink

## Slide 4: For information: CSI-RS configuration update for CQI
  There are three scenarios for time relation between CSI-RS configuration update for CQI and the active TCI state list update
  The CSI-RS configuration update for CQI and the active TCI state list update are finished basically at the same time
  The CSI-RS configuration update for CQI is finished before the active TCI state list update
  The CSI-RS configuration update for CQI is configured after completing the active TCI state list update

## Slide 5: Issue 2:Known Condition
  RAN4 should discuss the following definition of Known condition:
The TCI state is known if it has been meeting the following conditions: - TCI state switch command is received within [1280] ms of the last transmission of the RS resource for beam reporting or measurement for the target TCI state - The UE has sent at least 1 measurement report for the target TCI state within TBD ms - The TCI state remain detectable from the last transmission of the RS resource used for the L1-RSRP measurement reporting during the TCI state switching period - The SSB associated with the TCI state remain detectable [with at least one spatial Rx filter] from the last transmission of the RS resource for the L1-RSRP measurement reporting during the TCI switching period - SNR of the TCI state is ≥ -3dB

## Slide 6: For Information: Known Condition
In FR2, it should be considered whether the Rx beam has to be changed during the TCI state switch.
If the SNR side condition is only met with Rx beam #1 in the 1st half of the switching delay and only met with Rx beam #2 in the 2nd half, then UE actually has to search the new Rx beam during the TCI switching. In this case, the TCI state should be unknown.

## Slide 7: Issue 3:Definition of first-SSB
RAN4 should discuss whether should be further clarified.
  In unknown TCI state switch with QCL Type-D
    is time to first SSB transmission after L1-RSRP measurement by the UE
  In unknown TCI state switch involving with QCL Type-A, B, C only
    is time to first SSB transmission after MAC CE command by the UE.
  In RRC based known TCI state switch
    is time to first SSB transmission after RRC processing by the UE.

## Slide 8: For Information: Definition of first-SSB
In current requirement, is defined as the first SSB transmission after MAC CE command in MAC-CE based TCI state switching. However, in the case that UE should measure L1-RSRP after MAC CE decoded in unknown TCI state switch involving changes in QCL Type-D, UE should wait the first SSB to time tracking when UE finished the L1-RSRP measurement.

## Slide 9: Issue 4:QCL-related issues
  Issue 4-1: Whether should be update to 1 when TCI state switching involves QCL-Type A, B, C only for unknown case.
  Issue 4-2: Whether the TCI state switch requirements should only apply to the case where the CSI-RS based TCI state is Type-A, B, C QCL-ed with an SSB.

## Slide 10: For Information: QCL-related issues
Issue 4-1
  In current specification, when SSB based L1-RSRP measurement in unknown TCI state switching because it believes time tracking can be done at the same time with SSB based L1-RSRP measurement. However, it will be no SSB based L1-RSRP measurement procedure once TCI state switching only involving QCL Type-A, B, C only.

## Slide 11: For Information: QCL-related issues
Issue 4-2
  Currently, additional time tracking time will be always added in CSI-RS based L1-RSRP measurement. UE still cannot know how to use suitable SSB for time tracking when CSI-RS is not configured to QCLed with any SSB.

## Slide 12: Issue 5:RRC based TCI state switching delay
  Issue 5-1: Whether the delay requirement for RRC based TCI state switching is only applicable to the case that only one TCI state is configured in TCI state list in RRC reconfiguration.
  Issue 5-2: Whether to update the scheduling restriction in TCI state switch as follow:
  During the RRC based TCI state switching, the UE is not required to receive PDCCH/PDSCH or transmit PUCCH/PUSCH during the RRC reconfiguration procedure and on the OFDM symbols occupied by CSI-RS, SSB or SSB and CSI-RS QCL-ed to the target TCI state until the end of switching period.

## Slide 13: For Information: RRC based TCI state switching delay
Issue 5-1:
  The agreed RRC based TCI state switching delay requirement is originated from RAN4’s previous discussion about one special RRC reconfiguration scenario: the UE will be configured with only one TCI state in TCI state list of RRC reconfiguration to indicate the TCI state switch implicitly. Otherwise, the TCI state switching time will be definitely extended to consider MAC-CE and DCI time.

## Slide 14: For Information: RRC based TCI state switching delay
Issue 5-2:
  In currently agreed RRC based TCI state switching, UE is not required to receive PDCCH/PDSCH or transmit PUCCH/PUSCH until the end of TCI state switching delay. However, the reasonable scheduling restriction will only happen in RRC reconfiguration time and the SSB/CSI-RS occasion symbols for measurement with the target TCI state.