## Slide 1: Way forward on LTE HST BS demodulation requirements
3GPP TSG-RAN WG4 Meeting #92big
Chongqing, China, 14th – 18th, Oct 2019
Agenda item: 7.13.4 [LTE_high_speed_enh2-Perf]
Document for: Approval
R4-1912777
NTT DOCOMO, INC.

## Slide 2: Background
In RAN#80, the new WI on further performance enhancement in high speed scenario was approved [1].
In RAN4 #90, the work plan [2] and WF on BS demodulation [3] were approved.
In RAN4 #90bis, WF on BS demodulation [4] was approved.
In RAN4 #91, WF on BS demodulation [5] was approved.
In RAN4 #92, WF on BS demodulation [6] was approved.
In RAN4 #92bis, BS performance requirements for high speed were discussed based on contributions [7-16]

## Slide 3: PUSCH for HST
Agreement:
  PUCCH format
    format 2 (BS may use PUCCH format 2 for Doppler tracking)
  maximum Doppler shift
    1944Hz
      If 70%ile of the max. throughput is not achievable with 1944Hz:
      -Option 1: fallback to 1750Hz, or
      -Option 2: accept %ile of max. throughput lower than 70%ile with 1944Hz
  MCS
    QPSK 1/3 (MCS 6)
  Antenna configuration
    1x1 for tunnel and 1x2 for open space
  CBW
    1.4/3/5/10/15/20 MHz
  Test metric
    Both 30% and 70% of the maximum throughput
  Companies are encouraged to provide the simulation result with Doppler=1944Hz in RAN4#93. Companies may also provide the simulation results with Doppler=1750Hz.

## Slide 4: PUSCH for HST
Agreement: Introduce the following HST scenarios
Parameter | Value | 
 | Open space | Tunnel for multi-antennas
 | Bi-directional | Bi-directional
Ds | 1000 m | 300 m
Dmin | 50 m | 2 m
v | 500 km/h | 500 km/h
fd | 1944Hz If 70%ile of the max. throughput is not achievable with 1944Hz: Case 1: fallback to 1750Hz, or Case 2: accept %ile of max. throughput lower than 70%ile with 1944Hz | 

## Slide 5: PUSCH for HST
Agreement: Introduce the following new test cases
Parameters | Value | 
 | Scenario 1 (Open space) | Scenario 3 (Tunnel)
CBW | 1.4/3/5/10/15/20 MHz | 1.4/3/5/10/15/20 MHz
CP | Normal | Normal
FRC | A.3-2 to A.3-7 (QPSK 1/3) | A.3-2 to A.3-7 (QPSK 1/3)
Antenna configuration | 1Tx2Rx | 1Tx1Rx
Reference receiver | MRC | MRC
Noise estimation | Practical | Practical
Time and frequency track | Practical | Practical
Test metric | [70%ile] of the max. throughput 30%ile of the max. throughput | [70%ile] of the max. throughput 30%ile of the max. throughput
NOTE: The configuration of PUCCH (format 2) is optional |  | 

## Slide 6: PRACH restricted set type B
Agreement:
  Introduce new test cases with frequency offset = 1944Hz for PRACH restricted set type B. Define test cases for PRACH formats 0/1/2/3.
    PRACH format: 0/1/2/3
    Channel model: AWGN
    Frequency offset: 1944 Hz
    Antenna configuration: 1x2 / 1x4 / 1x8
    Other assumptions are same as existing PRACH restricted set type B requirement

## Slide 7: Reference
[1] RP-181482, “New Work Item on Further performance enhancement for LTE in high speed scenario”, SoftBank, RAN#80
[2] R4-1900804, “Work plan for LTE high speed in Rel.16”, NTT DOCOMO, INC., Huawei, HiSilicon, RAN4#90
[3] R4-1902522, “Way Forward on BS demodulation scenarios and requirements for HST”, Ericsson, NTT Docomo, RAN4#90
[4] R4-1904793, “Way forward on BS demodulation requirement for HST enhancement”, NTT DOCOMO, INC., RAN4#90bis
[5] R4-1907747, “Way forward on LTE HST BS demodulation performance requirements”, Nokia, Nokia Shanghai Bell, NTT DOCOMO, INC., Ericsson, RAN4#91
[6] R4-1910102, “Way forward on LTE BS demodulation performance requirements”, NTT DOCOMO, INC., RAN4#92
[7] R4-1912447, “Views on PUSCH and PRACH for LTE HST enhancement”, NTT DOCOMO, INC., RAN4#92bis
[8] R4-1911125, “Discussion and simulation results for BS demodulation requirements for LTE HST enhancement”, Huawei, HiSilicon, RAN4#92bis
[9] R4-1911126, “Discussion and simulation results for PRACH restricted set type B”, Huawei, HiSilicon, RAN4#92bis
[10] R4-1911382, “Dicussion and simulation results for HST PUSCH in LTE Rel-16”, Samsung, RAN4#92bis
[11] R4-1911383, “Dicussion and simulation results for HST PRACH in LTE Rel-16”, Samsung, RAN4#92bis
[12] R4-1911778, “Doppler shift evaluation for LTE HST Bidirectional Scenario”, Ericsson, RAN4#92bis
[13] R4-1911779, “Doppler shift evaluation for LTE HST Unidirectional Scenario”, Ericsson, RAN4#92bis
[14] R4-1912476, “Simulation results of PRACH preamble restricted set type B for Rel-16 LTE HST”, Nokia, Nokia Shanghai Bell, RAN4#92bis
[15] R4-1912478, “On PUSCH simulation results for Rel-16 LTE HST”, Nokia, Nokia Shanghai Bell, RAN4#92bis
[16] R4-1912479, “BS demodulation simulation results of PUSCH for Rel-16 LTE HST”, Nokia, Nokia Shanghai Bell, RAN4#92bis