## Slide 1: 3GPP TSG-RAN WG4 Meeting #92bis Chongqing, China, 14th – 18th October 2019
Huawei, HiSilicon
Way forward on RRM requirements of R16 enhancement for NB-IoT
R4-1912783

## Slide 2: Wake-up signal
Based on the Rel-16 WUS contributions provided to RAN4#92bis meeting, it is observed that Rel-15 WUS reception requirements can be used for Rel-16 WUS receptions.

## Slide 3: Preconfigured UL resource
The first and the second measurement conditions agreed at RAN4#92 meeting (R4-1910576) include parameters M and N, whose values are defiend as follows:
  When TA is obtained in RRC_CONNECTED mode: M=[TEvaluate_Qin_ NB-IoT /2]
  When TA is obtained in RRC_IDLE mode:
    Option 1:
      M = min (Tmeasure_intra_UE NB-IoT in nonDRX, DRX_cycle length)
      N = min (Tmeasure_intra_UE NB-IoT in nonDRX, DRX_cycle length)
    Other options are not precluded.

## Slide 4: Multi carrier operation non-anchor RRM
If the following conditions are met:
  The relaxed cell monitoring criteria defined in TS 36.304 clause 5.2.4.12, and
  Transmit power difference of NRS between anchor carrier and non-anchor paging carrier is signalled to the UE via the existing parameter nrs-PowerOffsetNonAnchor, and
  UE is not configured with any positioning measurements,
Then UE:
  Stops monitoring neighbor cells
  May stop performing NRSRP measurements on anchor carrier
  May continue to perform NRSRP measurements only on the non-anchor carrier
  May continue to evaluate relaxed monitoring conditions using non-anchor carrier NRSRP measurements and nrs-PowerOffsetNonAnchor for translation to their equivalent NRSRP in anchor carrier
  Exiting this state will be based on not fulfilling the relaxed conditions in TS 36.304 clause 5.2.4.12.

## Slide 5: Multi carrier operation non-anchor RRM
Issue 1:
For the sparse PO case, there are sufficient number of NRS subframes available for performing NRSRP measurement on the non-anchor carrier.
In the non-sparse PO case, the feasibility of conducting serving cell NRSRP measurement is FFS once further agreement has been reached with regard to N and M configurations in RAN1,
where N= number of NRS subframes starting from the subframe containing the PO, i.e., within the NPDCCH search space, and M= number of NRS subframe before the subframe containing the PO.
Issue 2:
Filtering the samples from anchor and non-anchor carriers is FFS