## Slide 1: Way forward on feMob in LTE R16
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #92bis R4-1912784
ChongQing, China, 14-18 Oct. 2019

## Slide 2: Reduction of user data interruption
eMBB LTE handover delay definition:
Definition of HO delay is split into two parts:
Delay (1): from HO command to PRACH preamble transmission
Delay(1) is defined as:
D1 = TRRC_procedure + Tsearch + TIU + 20
Definitions of each term is same as that in the existing handover RRM requirements.
Interruptions in delay (1):
  - For intra-frequency:
    Case 1 (BWsource ≠ BWtarget): FFS.
    Case 2 (BWsource = BWtarget): FFS
  - For inter-frequency:
    reuse existing SCell addition interruption requirement in DC as a starting requirement
      Note: the async inter-frequency intra-band case is not feasible for eMBB
Delay (2) is for source cell release:
  Start point is FFS
  End point is FFS
  The interruptions in delay (2) is FFS

## Slide 3: Conditional handover
CHO delay requirement:
The starting point of the CHO procedure is from the end of the last TTI containing the RRC command carrying the CHO command. Handover delay is split into the following phases
Phase 0: CHO command RRC processing
Phase 1: Measurement
Phase 2: HO execution
Handover delay is defined as:
DCHO = TRRC_1 + Tmeasure + TIU + TRRC_2 + 20
Where:
UE RRC processing time is broken into two segments:
TRRC_1: First segment of RRC processing time to process CHO command.
TRRC_2: Second segment of RRC processing time, starts after UE realizes the condition is met and identity of target cell is determined
Tmeasure: from the end of CHO RRC command is successfully decoded (no later than TRRC_1) until [UE realizes a handover condition for CHO is met].