## Slide 1: Way Forward on 5G Broadcasting
Qualcomm
3GPP TSG-RAN WG4 Meeting #92bis
Chongqing , China, 14th August – 18th October, 2019
R4-1912790
Document for: Approval

## Slide 2: RRM Requirement
MBSFN measurement period
  Long numerology: MAX(640 ms, period during which the UE decodes 5 symbols containing PMCH transmissions)
  Short numerology: follow legacy MBFSN measurement period
The current measurement requirements on FeMBMS/Unicast-mixed carrier in R14 can be reused in R16 for LTE-based 5G terrestrial broadcast
MCH BLER report period
  Follow legacy MBSFN
Phase synchronization accuracy
CP length for MBSFN subframe | Requirement
100µs |  5 s
300µs |  5 s

## Slide 3: RRM Requirement
Numerology switch interruption requirement
  Option 1(HW): The current numerology switching delay requirements and interruption requirements due to numerology switching in R14 can be reused in R16 for LTE-based 5G terrestrial broadcast
  Other options are not precluded
Cell identification and detection requirement
  No additional requirement is needed, legacy requirement applies to Rel-16 for mixed cells
RSRP/RSRQ accuracy requirement
  Follow legacy MBSFN accuracy requirement

## Slide 4: RSRP report mapping
  Option 1 (QC)
    For long numerology with 370.37Hz SCS
    For short numerology with 2.5kHz SCS
Reported value | Measured quantity value | Unit
MBSFN_RSRP_00 | MBSFN_RSRP  -156 | dBm / 370Hz
MBSFN_RSRP_01 | -156  MBSFN_RSRP < -155 | dBm / 370Hz
MBSFN_RSRP_02 | -155  MBSFN_RSRP < -154 | dBm / 370Hz
… | … | …
MBSFN_RSRP_95 | -62  MBSFN_RSRP < -61 | dBm / 370Hz
MBSFN_RSRP_96 | -61  MBSFN_RSRP < -60 | dBm / 370Hz
MBSFN_RSRP_97 | -60  MBSFN_RSRP | dBm / 370Hz
Reported value | Measured quantity value | Unit
MBSFN_RSRP_00 | MBSFN_RSRP  -148 | dBm / 2.5 kHz
MBSFN_RSRP_01 | -148  MBSFN_RSRP < -147 | dBm / 2.5 kHz
MBSFN_RSRP_02 | -147  MBSFN_RSRP < -146 | dBm / 2.5 kHz
… | … | …
MBSFN_RSRP_95 | -54  MBSFN_RSRP < -53 | dBm / 2.5 kHz
MBSFN_RSRP_96 | -53  MBSFN_RSRP < -52 | dBm / 2.5 kHz
MBSFN_RSRP_97 | -52  MBSFN_RSRP | dBm / 2.5 kHz

## Slide 5: RSRQ report mapping
  For long numerology with 370.37Hz SCS
  For short numerology with 2.5kHz SCS
Reported value | Measured quantity value | Unit
MBSFN_RSRQ_00 | MBSFN_RSRQ  -38 | dB
MBSFN_RSRQ_01 | -39.0  MBSFN_RSRQ < -38.3 | dB
MBSFN_RSRQ_02 | -38.3  MBSFN_RSRQ < -37.6 | dB
… | … | …
MBSFN_RSRQ_30 | -17.7  MBSFN_RSRQ < -17 | dB
MBSFN_RSRQ_31 | -16  MBSFN_RSRQ | dB
Reported value | Measured quantity value | Unit
MBSFN_RSRQ_00 | MBSFN_RSRQ  -31 | dB
MBSFN_RSRQ_01 | -31  MBSFN_RSRQ < -30.4 | dB
MBSFN_RSRQ_02 | -30.4  MBSFN_RSRQ < -29.8 | dB
… | … | …
MBSFN_RSRQ_30 | -13.6  MBSFN_RSRQ < -13 | dB
MBSFN_RSRQ_31 | -13  MBSFN_RSRQ | dB