## Slide 1: 3GPP TSG-RAN WG4 Meeting #92bis Chongqing, China, 14 – 18 October 2019
Huawei, HiSilicon
WF on euCA RRM
R4-1912804

## Slide 2: Interruption requirement for direct SCell activation/hibernation
For defining the interruption requirement, UE is assumed to do one tuning and AGC (if needed) during the direct SCell activation/hibernation.
The interruption length on PCell and activated SCell is
  2ms, if the PCell and activated SCell are on a different band than the SCell being directly activated/hibernated
  5ms, if the PCell and activated SCell are on the same band as the SCell being directly activated/hibernated

## Slide 3: Interruption requirement for CQI measurement on dormant SCell
Re-use the requirements on interruption length defined for SCell activation of dormant Scell in section 7.8.2.14/15/16.

## Slide 4: S-measure threshold applicability
SnonIntraSearchP and SnonIntraSearchQ will not need to be considered in early measurement requirements.
Exact number of frequency layers UE should measure for early measurement reporting is FFS.
Interested companies are encouraged to provide opinions in RAN4#93.
Reference
  Discussion paper: R4-1912117
  Draft CR: R4-1912118