## Slide 1
3GPP TSG-RAN WG4 Meeting #92Bis R4-1912808
Chongqing, China, 14th – 18th Oct, 2019
Agenda Item: 8.17.2
WF on UE demodulation for NR HST
CMCC

## Slide 2: Agreements
SCS and channel bandwidth
  FDD: 10 MHz, SCS 15 kHz
  TDD: 40 MHz, SCS 30 kHz

## Slide 3: Agreements
Maximum Doppler for 500km/h
  For TDD 30KHz
    For HST single tap, maximum Doppler is 1667Hz
    For HST-SFN, maximum Doppler is
      Option 1: 1500Hz
      Option 2: 1667Hz
      Other values between option 1 and option 2 are not precluded
  For FDD 15KHz
    Single tap HST, maximum Doppler is
      Option 1: 1250Hz
      Option 2: 972Hz
    HST-SFN, maximum Doppler is
      Option 1: 712Hz
      Option 2: 875Hz
      Other values between option 1 and option 2 are not precluded
  If requirements for 350km/h are introduced, smaller Doppler frequency value can be considered

## Slide 4: Agreements
For multi-path fading channel, further study is needed
Whether to define fading channel requirements will be based on simulation, analysis and deployment scenario
  Simulation assumption for multi-path fading channel:
    [TDL-C 300ns] channel model with following Doppler frequency
      FDD: [600 Hz] Doppler frequency with SCS = 15KHz
      TDD: [1200 Hz] Doppler frequency with SCS = 30KHz
  Note 1: further study on the introduction of applicability rule
  Note 2: value of maximum Doppler frequency will be further discussed based on simulation and analysis

## Slide 5: Agreements
Channel model
  For HST single tap
    Ds=300m, Dmin=2m
  For HST-SFN, reuse 4-tap LTE HST-SFN bi-directional channel model
    Ds=700m, Dmin=150m

## Slide 6: Agreements
Transmission scheme
  Study the feasibility and performance benefits for DPS transmission
    Feasibility study should include the complexity of test equipment implementation
  Candidate transmission schemes to be studied are in Annex.

## Slide 7: Agreement
Rank
  Rank 1 for HST single tap
  Rank 2 for HST-SFN

## Slide 8: Agreements
PDCCH
  Do not introduce PDCCH demodulation requirements for fading channel, HST-SFN and HST single tap

## Slide 9: Agreements
Signaling
  Introduce UE capability for HST-SFN
  Introduce NW assistance signaling for HST-SFN
    FFS on the detail on network assistance signaling for HST-SFN
      option 1: similar as NW assistance signaling introduced for LTE HST-SFN (one configuration flag, which is a per-cell signaling)
      option 2: configured in each TRS resource set
      other options are not precluded
  FFS on NW assistance signaling for HST single tap

## Slide 10: Agreement
For all the channel models in this way forward, FFS on the MCS
  Option 1: MCS4
  Option 2: MCS13
  Option 3: MCS17
  Other MCS are not precluded
  MCS should be decided based on whether the maximum throughput can be achieved

## Slide 11: Updated simulation assumption for HST-SFN
Parameter | Value | 
 | FDD 15KHz SCS | TDD 30KHz SCS
Antenna configuration | 2×2; 2×4 | 
DMRS type | type 1 | 
Number of DMRS symbols | DMRS 1+1+1 | 
TDD pattern | 7D1S2U, S: 6D 4G 4U | 
MCS | MCS 4; MCS 13; MCS 17 based on 64QAM table | 
Propagation condition | HST-SFN | 
TRS periodicity | 10ms, 2slot pattern | 
PDSCH mapping | Type A, Start symbol 2, Duration 12 | 
Ds and Dmin | Ds=700m, Dmin=150m | 
Rank | Rank = 2 | 
BW | 10MHz | 40MHz
Maximum Doppler shift | Option 1: 875Hz Option 2: 712Hz | Option 1: 1667Hz Option 2: 1500Hz
Testing metric | SNR @70% of maximum throughput | 
Note: The other parameters are same as Rel-15

## Slide 12: Updated simulation assumption for HST-single tap
Parameter | Value | 
 | FDD 15KHz SCS | TDD 30KHz SCS
Antenna configuration | 2×2; 2×4 | 
DMRS type | type 1 | 
Number of DMRS symbols | DMRS 1+1+1 | 
MCS | MCS 4; MCS 13; MCS 17 based on 64QAM table | 
TDD pattern | 7D1S2U, S: 6D 4G 4U | 
Propagation condition | HST-single tap | 
TRS periodicity | 10ms, 2slot pattern | 
PDSCH mapping | Type A, Start symbol 2, Duration 12 | 
Ds and Dmin | Ds= 300m, Dmin=2m | 
Rank | Rank = 1 | 
BW | 10MHz | 40MHz
Maximum Doppler shift | Option 1: 1250Hz Option 2: 972Hz | 1667Hz
Testing metric | SNR @70% of maximum throughput | 
Note: The other parameters are same as Rel-15

## Slide 13: Simulation assumption for multi-path fading channel
Parameter | Value | 
 | FDD 15KHz SCS | TDD 30KHz SCS
Antenna configuration | 2×2; 2×4 | 
DMRS type | type 1 | 
Number of DMRS symbols | Option 1: DMRS 1+1+1 Option 2: DMRS 1+1+1+1 | 
TDD pattern | 7D1S2U, S: 6D 4G 4U | 
MCS | MCS 4; MCS 13; MCS 17 based on 64QAM table | 
Propagation condition | TDL-C 300ns | 
TRS periodicity | 10ms, 2slot pattern | 
PDSCH mapping | Type A, Start symbol 2, Duration 12 | 
Rank | Rank = 1 and 2 | 
BW | 10MHz | 40MHz
Maximum Doppler shift | 600Hz | 1200Hz
Testing metric | SNR @70% of maximum throughput | 
Note: The other parameters are same as Rel-15

## Slide 14: Annex
Candidate transmission scheme to be further studied
  Transmission scheme 1 - DPS: PDSCH is only transmitted from one TRP at one time
    Transmission scheme 1a: UE only needs to track 1 TCI state (detail can be found in R4-1911003)
    Transmission scheme 1b: UE needs to track more than 1 TCI states (detail can be found in R4-1911091)
  Transmission scheme 2 - PDSCH is jointly transmitted from two or more adjacent TRPs scheduled by multi-DCI(detail can be found in R4-1911091)
  Transmission scheme 3 - Joint transmission + Distributed reference signal (detail can be found in R4-1911003)
    joint transmission + Distributed TRS
    joint transmission + Distributed DMRS