## Slide 1: Way forward on BWP Switching on Multiple CCs
Ericsson
3GPP TSG-RAN WG4 Meeting # 92bis
Chongqing, China, October 14-18, 2019
Agenda: 8.15.1.4
R4-1912837

## Slide 2: Background
Case 1: Simultaneous triggering of BWP switching on multiple CCs
Time
BWP switching on CC1
Trigger BWP switching
Time
Trigger BWP switching
BWP switching on CC2
Figure 1: An example of triggering BP switching on multiple CCs at the same time.
Time
BWP switching on CC1
Trigger BWP switching on CC1
Time
Trigger BWP switching on CC2
BWP switching on CC2
Figure 2: An example of BWP switching on multiple CCs with partially overlapping time.
Case 2: Non-simultaneous triggering of BWP switching on multiple CCs

## Slide 3: WF on Requirements
Candidate BWP switching scenarios for specifying requirements:
  Case 1: Simultaneous triggering of BWP switching on multiple CCs
    When timer-based BWP switching is triggered on multiple CCs.
    When RRC-based BWP switching is triggered on multiple CCs.
    Other scenarios are not precluded.
  Case 2: Non-simultaneous triggering of BWP switching on multiple CCs
    When RRC-based BWP switching is triggered on a CC (CC1) while there is an on going RRC-based BWP switching on another CC (CC2).
      FFS whether to limit CC1 and CC2 in different CGs or within the same CG
    When timer-based or DCI based BWP switching is triggered on a CC (CC1) while there is an on going RRC-based BWP switching on another CC (CC2).
      FFS whether to limit CC1 and CC2 in different CGs or within the same CG
    Other scenarios are not precluded.
RAN4 to investigate the BWP switching delay and interruption requirements for the above scenarios.