## Slide 1: WF on RRM Requirements for NR-U (all agreements in RAN4#92-bis)
Ericsson
3GPP TSG-RAN WG4 Meeting #92-Bis R4-1912846
Chongqing, P. R. of China, 14th – 18th October, 2019
Agenda Item: 8.1.4

## Slide 2
Agreements from
Main Session and Two Ad Hoc Sessions

## Slide 3: Serving Cell Evaluation
M1=2 if [SMTC or DMTC] periodicity (T[SMTC or DMTC]) > 20 ms and DRX cycle ≤ 0.64 second, otherwise M1=1. Further decide if SMTC or DMTC shall be used subject to RAN1 progress on DMTC definition
Ms,max is used to denote the maximum value of Ms (Ms≤Ms,max)
Ms is the number of DRX cycles with at least one SMTC where there are no SSBs available at the UE during Nserv
  FFS whether the Ms definition above is different for the case when two or more SSBs are QCL-ed within the SMTC
Ms,max=[8] for DRX cycle length < 1.28 seconds, [4] for DRX cycle length ≥ 1.28 seconds
Mp=[4] when DRX cycle length <1.28 sec, Mp=[2] when DRX cycle length ≥1.28 sec
Mq=[8] when DRX cycle length <1.28 sec, Mq=[4] when DRX cycle length ≥1.28 sec
Typo correction to the agreement in RAN4#92:
  The NR-U standalone UE shall measure and evaluate the cell selection criterion S for the serving cell at least once every (1+Mn)*M1 DRX cycles in Nserv consecutive DRX cycles, where…

## Slide 4: Cell Reselection
Mm,max is used to denote the maximum value of Mm (Mm≤Mm,max).
Md,max is used to denote the maximum value of Md (Md≤Md,max).
Me,max is used to denote the maximum value of Me (Me≤Me,max).
Mm,max:
  TBD for 0.32 DRX cycle length
  [8] for 0.64 DRX cycle length
  [4] for 1.28 DRX cycle length
  TBD for 2.56 DRX cycle length
Md,max=[4]*Mm,max
Me,max=[2]*Mm,max
Mn=[2]

## Slide 5: SI Reading for PLMN Identification
SI reading for PLMN identification in cell reselection requirements:
  Come back next meeting
SI reading for PLMN identification in HO requirements:
  Come back next meeting

## Slide 6: Handover Delay Requirements
The description of interruption uncertainty of the handover procedure in NR-U should be clarified as: “TIU is the interruption uncertainty due to the random access procedure when sending PRACH to the new cell”
  wait for RAN2 decision on the UL LBT failure mechanism before making the requirements for TIU of the handover procedures in NR-U

## Slide 7: RRC Connection Re-establishment
Maximum values:
  For known cell case
    (during intra-frequency cell search):
      K1,max=[12] when TSMTC ≤ 40 ms, and
      K1,max=[8] when TSMTC > 40 ms
    (during inter-frequency cell search):
      K2.i,max =[10] when TSMTC,i ≤ 40 ms, and
      K1,max=[6] when TSMTC,i > 40 ms
    (during RA):
      K3, max=[8] when Tconfig ≤ 40 ms, and
      K3, max=[4] when Tconfig > 40 ms
  FFS for unknown cell case
Wait for RAN2 decision on the UL LBT failure mechanism before making the requirements for TPRACH in NR-U
When the re-establishment delay is within the upper limit, it is up to UE to select which cell to camp on. No specific requirements will be defined

## Slide 8: RRC Release with Redirection
Maximum values:
  (during cell search)
    L1,max=[8] when TSMTC ≤ 40 ms
    L1,max=[4] when TSMTC > 40 ms
  (during RA)
    L2, max=[4] when Tconfig ≤ 40 ms
    L2, max=[2] when Tconfig > 40 ms
RAN4 should wait for RAN2 decision on the UL LBT failure mechanism before making the requirements for TPRACH in NR-U

## Slide 9: SI Reading Time Period in RRC Release with Redirection Requirements and RRC Re-Establishment Requirements
Analyze how to extend TSI-NR by the next meeting

## Slide 10: RLM In-Sync
Lin is the number of SSBs not available at the UE during TEvaluate_in_SSB, where Lin ≤ Lin,max.
  Lin,max = TBD for Max(TDRX,TSSB)≤40 where TDRX=0 for non-DRX
  Lin,max = TBD for 40<Max(TDRX,TSSB)≤320
  Lin,max = TBD for TDRX>320.
Further complementary agreements to the earlier agreed (in RAN4#92) table:
UE behaviour when Lin,max is exceeded:
  For this evaluation period, UE layer 1 shall not send any in-sync indication to higher layers.

## Slide 11: UE Measurement Capability
NR-U Scenarios A and C, RRC_CONNECTED: the number of frequency layers is the same as for Rel-15 SA NR, excluding the frequency layers for inter-RAT RSTD measurements
  The total number of effective carrier frequency layers is 13, i.e., the same as in Rel-15 SA NR
NR-U Scenario B, RRC_CONNECTED: the number of frequency layers is the same as for Rel-15 EN-DC, excluding the frequency layers for inter-RAT RSTD measurements
  The total number of effective carrier frequency layers is 13, i.e., the same as in Rel-15 EN-DC

## Slide 12: UL Transmit Timing
Reference cell to derive UL transmit timing:
  Investigate Option 1 until RAN4#93
  Option 1:
    Scenario B and C: if the current reference cell (i.e. PCell in Scenairo C or PSCell in Scenario B) is unavailable to UE after certain number of DL SSB detection attempts, then the UE can take any activated SCell with SSB available at the UE within this CG as the new reference cell
    The UE applies one shot timing adjustment.
UL transmit timing requirements in presence of LBT
  UE behavior:
    The UE is allowed to transmit if the UE meets the existing (Rel-15) UL Tx timing requirements (even if no SSB is available during the last 160 ms), otherwise the UE shall not transmit

## Slide 13: Impact of UL LBT on UE reporting
Event-triggered reporting:
  UE measurement reporting delay is extended to account for UL LBT failures resulting in UE being not being able to transmit, provided the UL resources are configured
  This applies for all UL channel access categories other than the channel access category 1
    Existing reporting requirements apply for the reporting based on the UL channel access category 1
FFS for aperiodic measurement reporting
FFS for periodic measurement reporting

## Slide 14: Interruptions
The interruption due to deactivated SCell measurements for an NR-U aggressor cell can reuse the requirements for release 15 NR deactivated SCell measurements
For TS 36.133: For PSCell addition/release interruptions in Scenario B of NR-U, UE is allowed of up to 1 subframe in synchronous EN-DC or 2 subframes in asynchronous EN-DC on PCell and activated SCells in MCG if configured during the RRC reconfiguration procedure
  This interruption is for both uplink and downlink of (E-UTRAN) PCell and (E-UTRAN) SCell(s)

## Slide 15: SCell Activation: Known/Unknown SCell Definition
SSB remains detectable according to the cell identification conditions in clause 9.2 and 9.3 (their corresponding NR-U sections) in the occasions where the SSB is available at the UE.
Investigate further:
  The time period between the receptions of the SCell activation commands and last measurement or report is extended to account for DL and UL LBT failures.
    FFS how to extend

## Slide 16: SCell Activation: Interruption Window
Check with RAN1:
  For the time of the SCell activation/deactivation interruption window, THARQ is extended with HARQ to account for UL LBT failures, and HARQ≤HARQ,max is the delay in HARQ feedback due to UL LBT failure and UE reattempt to transmit HARQ feedback provided the resources are configured for the UE (HARQ =0 for channel access category 1)

## Slide 17: Active TCI State Switching: Known/Unknown TCI State
TCI state remains detectable during the TCI switching period meeting the SNR of the TCI state condition, which is ≥ -3dB, in the occasions where the SSB is available at the UE
Investigate further:
  The time between receiving of the TCI state switching command and the last transmission/measurement is extended to account for DL and UL LBT failures.
    FFS how to extend

## Slide 18: Active TCI State Switching Delay: RRC Based, Known
For RRC based TCI state switching, the UE is required to receive PDCCH using the new TCI state in
slot n + TRRC_processing + TOk*(Tfirst-SSB + TSSB-proc+TSSB* LRRC,known)
LRRC,known ≤LRRC,known,max is the corresponding number of SSB occasions not available at the UE due to CCA failure
  LRRC,known,max=TBD and may depend on TSSB
  UE behavior upon exceeding LRRC,known,max: FFS (e.g., whether the UE may stop the switching and abandon the active TCI state switching procedure, UE stays in the old active TCI state)

## Slide 19: Active TCI State Switching Delay: RRC Based, Unknown
For RRC-based switching, the UE is required to receive PDCCH using the new TCI state in
slot n+TRRC_processing+(TL1-RSRP+TCSI-RS/SSB*L1RRC,unknown)+TOuk*(Tfirst-SSB+TSSB-proc+TSSB*L2RRC,unknown)
L1RRC,unknown≤L1RRC,unknown,max is the corresponding number of occasions with the signal measured for L1-RSRP not available at the UE due to CCA failure
  L1RRC,unknown,max=TBD and may depend on TCSI-RS,SSB
  UE behavior upon exceeding L1RRC,unknown,max: FFS (e.g., whether the UE may restart)
L2RRC,unknown≤ L2RRC,unknown,max is the corresponding number of SSB occasions not available at the UE due to CCA failure
  L2RRC,unknown,max=TBD and may depend on TSSB
  UE behavior upon exceeding L2RRC,unknown,max: FFS (e.g., whether the UE may stop the switching and abandon the active TCI state switching procedure)

## Slide 20: Active TCI State Switching Delay: MAC-CE Based, Known
For MAC-CE based TCI state switching, the UE is required to receive PDCCH using the new TCI state (after switching or the active TCI state list update) in
  slot n + (THARQ,ref+HARQ) + 3 ms + TOk*(Tfirst-SSB+TSSB-proc+TSSB*LMAC,known)
and receive PDCCH using the old TCI state until
  slot n + (THARQ,ref+HARQ) + 3 ms + TOk*(Tfirst-SSB+TSSB*LMAC,known)
LMAC,known≤ LMAC,known is the corresponding number of SSB occasions not available at the UE due to CCA failure
  LMAC,known,max=TBD and may depend on TSSB
  UE behavior upon exceeding LMAC,known,max: FFS (e.g., whether he UE may stop the switching and abandon the active TCI state switching procedure)
Check whether this is aligned with the RAN1 procedure: HARQ≤HARQ,max is the delay in HARQ feedback due to UL LBT failure and UE reattempt to transmit HARQ feedback provided the resources are configured for the UE (HARQ =0 for channel access category 1)
  HARQ,max=TBD
  UE behavior upon exceeding HARQ,max: FFS (e.g., whether the UE may stop attempting to transmit HARQ feedback and may abandon the active TCI state switching procedure)

## Slide 21: Active TCI State Switching Delay: MAC-CE Based, Unknown
For MAC-CE based switching, UE is required to receive PDCCH using the new TCI state in
  slot n+(THARQ,ref+HARQ)+3 ms+(TL1-RSRP+TCSI-RS/SSB*L1MAC,unknown)+TOuk*(Tfirst-SSB+TSSB-proc+TSSB*L2MAC,unknown)
and receive PDCCH using the old TCI state until
  slot n+(THARQ,ref+HARQ)+3 ms+(TL1-RSRP+TCSI-RS/SSB*L1MAC,unknown)+TOuk*(Tfirst-SSB+TSSB*L2MAC,unknown)
L1MAC,unknown≤ L1MAC,unknown,max is the corresponding number of occasions with the signal measured for L1-RSRP not available at the UE due to CCA failure
  L1MAC,unknown,max=TBD and may depend on TCSI-RS,SSB
  UE behavior upon exceeding L1MAC,unknown,max: FFS (e.g., whether the UE may restart the L1-RSRP measurement)
L2MAC,unknown≤L2MAC,unknown,max is the corresponding number of SSB occasions not available at the UE due to CCA failure
  L2MAC,unknown,max=TBD and may depend on TSSB
  UE behavior upon exceeding L2MAC,unknown,max : FFS (e.g., whether the UE may stop the switching and abandon the active TCI state switching procedure)
Check whether this is aligned with the RAN1 procedure: HARQ≤HARQ,max is the delay in HARQ feedback due to UL LBT failure and UE reattempt to transmit HARQ feedback provided the UL resources are configured for the UE (HARQ =0 for channel access category 1)
  HARQ,max=TBD
  UE behavior upon exceeding HARQ,max : FFS (e.g., whether which the UE may stop attempting to transmit HARQ feedback and may abandon the active TCI state switching procedure)

## Slide 22: PSCell Addition: Known/Unknown Target Cell Definition
The known PSCell definition needs to be updated for NR-U
Measured SSB remains detectable according to the cell identification conditions in the occasions where the SSB is available at the UE
Investigate further:
  The time between the reception of the PSCell configuration command and measurement/report is extended to account for DL and UL LBT failures.
    FFS how to extend

## Slide 23: CSSF and Measurement Gaps
CSSF:
  The CSSFwithin_gap,i definition does not need to be updated for NR-U, except clarifying that the existing definition of CSSF applies to frequencies where CCA is performed as well as frequencies where CCA is not performed
Independent measurement gaps for NR-U:
  If we have dedicated measurement gaps for NR-U, this allows for having independent CSSF for measurements within these gaps
  Analyze the benefits and drawbacks until RAN4#93 (e.g., reduced measurement time for NR-U measurements, without increasing the measurement time for other measurements, etc.)

## Slide 24: Measurements: UE Behaviour
UE behaviour upon exceeding the maximum L in measurement requirements:
  Upon exceeding the maximum acceptable number of DL LBT failures over the corresponding period of time, the UE has to restart the corresponding procedure, e.g., time index detection and measurements
  FFS UE behaviour for PSS/SSS detection

## Slide 25: Intra-Frequency Measurements
The following L-max values are to be decided in RAN4#93 for intra-frequency measurement requirements
Other DRX ranges are not precluded
Procedure | Rel-15 samples | Maximum number of DL LBT failures |  | 
 |  | Parameter name | Parameter value | Condition
PSS/SSS detection, no gaps | 5 | LPSS/SSS,max | TBD | Max(TDRX,TSMTC)≤40
 |  |  | TBD | 40<Max(TDRX,TSMTC)≤320
 |  |  | TBD | TDRX>320
PSS/SSS detection for deactivated SCell, no gaps | 5 | LPSS/SSS,deact,max | TBD | Max(TDRX, measCycleSCell)≤40
 |  |  | TBD | 40< Max(TDRX, measCycleSCell)≤320
 |  |  | TBD | TDRX>320
Time index detection, no gaps | 3 | Lind,max | TBD | Max(TDRX, TSMTC)≤40
 |  |  | TBD | 40< Max(TDRX, TSMTC)≤320
 |  |  | TBD | TDRX>320
Time index detection for deactivated SCell, no gaps | 3 | Lind,deact,max | TBD | Max(TDRX, measCycleSCell)≤40
 |  |  | TBD | 40< Max(TDRX, measCycleSCell)≤320
 |  |  | TBD | TDRX>320
Measurement, no gaps | 5 | Lmeas,max | TBD | Max(TDRX, TSMTC)≤40
 |  |  | TBD | 40< Max(TDRX, TSMTC)≤320
 |  |  | TBD | TDRX>320
Measurement on deactivated SCell, no gaps | 5 | Lmeas,deact,max | TBD | Max(TDRX, measCycleSCell)≤40
 |  |  | TBD | 40< Max(TDRX, measCycleSCell)≤320
 |  |  | TBD | TDRX>320
PSS/SSS detection, with gaps | 5 | LPSS/SSS,gaps,max | TBD | Max(TDRX,TSMTC, MGRP)≤40
 |  |  | TBD | 40<Max(TDRX,TSMTC, MGRP)≤320
 |  |  | TBD | TDRX>320
Time index detection, with gaps | 3 | Lind,gaps,max | TBD | Max(TDRX, TSMTC, MGRP)≤40
 |  |  | TBD | 40< Max(TDRX, TSMTC, MGRP)≤320
 |  |  | TBD | TDRX>320
Measurement, with gaps | 5 | Lmeas,gaps,max | TBD | Max(TDRX, TSMTC, MGRP)≤40
 |  |  | TBD | 40< Max(TDRX, TSMTC, MGRP)≤320
 |  |  | TBD | TDRX>320

## Slide 26: Inter-Frequency Measurements
The following L-max values are to be decided in RAN4#93 for inter-frequency measurement requirements
Other DRX ranges are not precluded
Procedure | Rel-15 samples | Maximum number of DL LBT failures |  | 
 |  | Parameter name | Parameter value | Condition
PSS/SSS detection, with gaps | 8 | LPSS/SSS,gaps,max | TBD | Max(TDRX,TSMTC, MGRP)≤40
 |  |  | TBD | 40<Max(TDRX,TSMTC, MGRP)≤320
 |  |  | TBD | TDRX>320
Time index detection, with gaps | 3 | Lind,gaps,max | TBD | Max(TDRX, TSMTC, MGRP)≤40
 |  |  | TBD | 40< Max(TDRX, TSMTC, MGRP)≤320
 |  |  | TBD | TDRX>320
Measurement, with gaps | 8 | Lmeas,gaps,max | TBD | Max(TDRX, TSMTC, MGRP)≤40
 |  |  | TBD | 40< Max(TDRX, TSMTC, MGRP)≤320
 |  |  | TBD | TDRX>320

## Slide 27
Further Agreements

## Slide 28: RSSI and Channel Occupancy
RAN4 to decide the measurement gap patterns applicable for RSSI and channel occupancy measurements and specify the applicability, considering the further progress in other working groups, e.g., on RSSI measurement time configuration periodicities
RAN4 to define measurement reporting mapping for RSSI
FFS whether measurement report mapping is needed for channel occupancy, depending on its definition to be decided by other groups

## Slide 29: Active BWP Switching
  If the delay due to the DL LBT failure in the target BWP becomes too long then:
    Some UE may not have a valid scheduling grant for transmitting in UL there may be additional delay to receive the grant for transmitting PUSCH
    Some UE may need to perform AGC setting
  UE behavior is FFS with respect to TDL,max and TUL,max
    TDL,max is the maximum allowed duration over which the DL signal/channel is unavailable at the UE (“DL signal/channel” is TBD) after the UE has completed the DL BWP switching
    TUL,max is the maximum allowed duration over which the UE was not able to transmit the UL signal/channel due to UL LBT (“UL signal/channel” is TBD) after the UE has completed the UL BWP switching

## Slide 30: Beam Management
RAN4 prioritizes the SSB based BFD and CBD for NR-U. RAN4 can revisit CSI-RS based BFD/CBD if RAN1 decides the CSI-RS configuration for BFD-RS/CBD-RS
CBD
  Maximum values:
    LCBD,max =TBD for max(TDRX,TSSB)≤40 where TDRX=0 for non-DRX,
    LCBD,max =TBD for 40<max(TDRX,TSSB)≤320,
    LCBD,max =TBD for max(TDRX,TSSB)>320
  UE behavior upon exceeding LCBD,max is FFS
BFD
  Maximum values:
    LBFD,max =TBD for max(TDRX,TSSB)≤40 where TDRX=0 for non-DRX,
    LBFD,max =TBD for 40<max(TDRX,TSSB)≤320,
    LBFD,max =TBD for max(TDRX,TSSB)>320
  UE behavior upon exceeding LBFD,max is FFS
Defining LCBD,MAX and LBFD,MAX for other ranges of TDRX, TSSB is not precluded

## Slide 31: L1-RSRP
RAN4 prioritizes the SSB based L1-RSRP measurements for reporting for NR-U. RAN4 can revisit CSI-RS based L1-RSRP measurements if RAN1 decides the CSI-RS configuration for L1-RSRP measurements
L1 is the number of SSBs not available at the UE during TL1-RSRP_Measurement_Period_SSB where L1 ≤ L1max. L1=0 if higher layer parameter timeRestrictionForChannelMeasurement is configured
Maximum values of L1
  L1max =TBD for max(TDRX,TSSB)≤40 where TDRX=0 for non-DRX
  L1max =TBD for 40<max(TDRX,TSSB)≤320
  L1max =TBD for max(TDRX,TSSB)>320
  Defining L1MAX and L1MAX for other ranges of TDRX, TSSB is not precluded
UE reports ‘not valid’ to the network when L1>L1max
Use RSRP_0 to indicate ‘not valid’

## Slide 32: SCell Activation Delay
Check whether this is aligned with the RAN1 procedure:
  THARQ is extended with HARQ to account for UL LBT failures, where HARQ≤HARQ,max is the delay in HARQ feedback due to UL LBT failure and UE reattempt to transmit HARQ feedback provided the resources are configured for the UE (HARQ =0 for channel access category 1)
TCSI_reporting = TCSI_reporting,ref +CSI, where
  TCSI_reporting,ref is the delay (in ms) as defined in Rel-15
  CSI≤CSI,max is the additional delay due to UL LBT failure and UE reattempt to transmit CSI report provided the resources are configured for the UE (CSI =0 for channel access category 1)
  CSI,max=TBD
  UE behaviour: upon exceeding, upon exceeding CSI,max=TBD the UE can stop attempting to transmit CSI report and can abandon the SCell activation procedure
  Check whether this is aligned with RAN1 conclusion on CSI reporting on unlicensed carrier
How to extend Tactivation_time needs further discussion

## Slide 33: SCell Deactivation Delay
Check whether this is aligned with the RAN1 procedure:
  THARQ is extended with HARQ to account for UL LBT failures, where HARQ≤HARQ,max is the delay in HARQ feedback due to UL LBT failure and UE reattempt to transmit HARQ feedback provided the resources are configured for the UE (HARQ =0 for channel access category 1)

## Slide 34: PSCell Addition Delay
TRRC_delay and Tprocessing are the same as in Rel-15 NR
Tsearch is extended by L1*Trs to account for DL LBT failures (L1≤L1max, L1max=TBD depending on Trs)
T∆ is extended by L2*Trs to account for DL LBT failures (L2≤L2max, L2max=TBD depending on Trs)
Check whether this is aligned with RAN2 procedure:
  TPSCell_ DU is extended by PRACH to account for UL LBT failures (PRACH=0 for channel access category 1). The maximum value of PRACH (PRACH,max) is TBD, upon exceeding which the UE can stop attempting to transmit PRACH and can abandon the PSCell addition procedure.

## Slide 35: RLM Out-of-Sync
Out-of-sync evaluation period is extended for NR-U
The extended evaluation period is based on Lout≤Lout,max
  Lout,max is the maximum allowed number of SSBs not available at the UE during TEvaluate_out_SSB
  Lout is the number of SSBs not available at the UE during TEvaluate_out_SSB
    Lout,max=TBD for Max(TDRX,TSSB)≤40 where TDRX=0 for non-DRX
    Lout,max=TBD for 40<Max(TDRX,TSSB)≤320
    Lout,max=TBD for TDRX>320
    FFS: Lout,max is larger when the presence of SSBs is detected in more than 1 samples (compared to 1 sample)
    Defining Lout,MAX and Lout,MAX for other ranges of TDRX, TSSB is not precluded
  FFS: The evaluation time is further extended when the UE needs more than 1 samples for detecting the presence of SSB during (e.g., at SINR<[-6] dB)
  UE behavior is FFS when exceeding Lout,max
RAN4 to discuss how the UE determines that an SSB is not available at the UE when SINR<-6 dB

## Slide 36: EN-DC SFTD
UE behavior upon reaching the maximum NLBT-fail:
  NLBT-fail,max is the maximum value of NLBT-fail (i.e., NLBT-fail≤NLBT-fail,max)
  NLBT-fail,max depends on SMTC period and DRX cycle
  Upon exceeding NLBT-fail,max, the UE terminates the SFTD measurement

## Slide 37: Inter-RAT SFTD
For inter-RAT SFTD towards NR-U with LBT, the UE shall continue to search for a cell until whichever comes first of:
  (a) a cell is found whereby SFTD is reported (as it is in Rel-15)
  (b) the SFTD measurement is deconfigured by MeNB (as it is in Rel-15)
  (c) the PCell is changed (as it is in Rel-15)
  (d) a maximum allowed time (which is FFS) expires