## Slide 1: Way forward on RRM enhancement: CGI reading
ZTE
3GPP TSG-RAN WG4 Meeting #92bis
Chongqing, China, 14 - 18 October, 2019
R4-1912847

## Slide 2: Background
Per WID RP-191601 “NR RRM enhancement in R16”, following requirements is to be specified
  CGI reading requirements with autonomous gap for NR capable UE
    CGI reading for NR cell (NR capable UE in LTE SA, NR SA UE, EN-DC UE, NE-DC UE, and NR-DC)
    CGI reading for LTE cell (NR SA UE, EN-DC UE, NE-DC UE, and NR-DC UE)

## Slide 3: Agreements during the meeting
CGI reading of an LTE cell with autonomous gaps
  Time period to identify CGI of an LTE cell is 150ms.
  Interruptions on NR serving cells during CGI reading of LTE cell:
    In CGI reading for LTE cell with autonomous gap, it could follow the same requirement in RSTD.
      Other options can be considered if identified to be beneficial.
  Interruptions on LTE serving cells during CGI reading of LTE cell in EN-DC or NE-DC
    For NR capable UE in EN-DC or NE-DC operation, legacy interruption requirements for LTE UE can be reused for interruptions on LTE serving cells for CGI reading of LTE neighbor cell

## Slide 4: Agreements during the meeting
CGI reading of an NR cell with autonomous gaps
  [5] samples are needed for MIB decoding in FR1
  SIB1 decoding delay:
    To decide NSIB1, simulation is needed. RAN4 first need to discuss the PDSCH transmission assumption for SIB1 acquisition such as:
      PDSCH transmission parameters, e.g., PRB size, TBS, modulation, etc.
      Whether or not it is assumed soft-combining of PDSCH within SIB1 TTI. If yes, how many?
      Metric to decide the number of PDSCH transmissions, e.g., PDSCH decoding success rate of 90%
      Side condition, e.g., SNR=-6dB
    Based on the assumption interested companies will provide the simulation results and decide NSIB1 according to the results.

## Slide 5: Agreements during the meeting
CGI reading of an NR cell with autonomous gaps
  SINR Side condition for NR CGI reading
    Re-use the SINR side condition of LTE for autonomous gap based CGI reading
    For intra-frequency, Es/Iot = -[6]dB for both SSB and RMSI
    For inter-frequency, Es/Iot = -[TBD]dB for both SSB and RMSI
  NR CGI reading assumes autonomous gaps in downlink and uplink.
  Both intra-frequency and inter-frequency NR CGI reading assume autonomous gaps in downlink and uplink.

## Slide 6: Open issues for CGI reading of NR cell
MIB decoding delay in FR2
  Whether beam switching is needed
AGC/AFC for MIB decoding
  Option 1: AGC/AFC is needed
  Option 2: not needed.
Beam sweeping needed for SIB1 decoding in FR2
  Tentative agreement: Rx beam sweeping is not needed for SIB1 decoding.
AGC for SIB1 decoding
  Option 1: AGC is needed
  Option 2: not needed.
Conditions for known/unknown cell
Interruptions during MIB decoding
  Option 1: 4 symbols + 2*RF tuning time during each autonomous gap
    FFS on additional margin for async case
    FFS the side condition to guarantee that the same SSB can be used by UE for the whole delay

## Slide 7: Open issues for CGI reading of NR cell
Interruptions during SIB1 decoding
  Interruption length
    Option 1
      Each autonomous gap for SIB1 decoding with multiplexing pattern 1 is 2 slots + 2*RF tuning time.
      Each autonomous gap for SIB1 decoding with multiplexing pattern 2/3 is 1 slot + 2*RF tuning time..
    Option 2
      RAN4 discusses from an interruption perspective whether the UE waits until it can guarantee NSIB1 attempts from the same TTI(minimizes interruptions), or follows the same approach as LTE CGI reading and starts SIB1 decoding at any point in the TTI (minimizes best case delay but tail latency needs to be accounted for in interruptions)
    Option 3
      The length of each autonomous gap should include
        twice the RF re-tuning time, the duration of PDCCH and PDSCH for RMSI, and the margin for the receive time difference between the serving cell and the target cell
  FFS on additional margin for async case
  FFS the side condition to guarantee that the same RMSI can be used by UE for the whole delay

## Slide 8: Open issues for CGI reading of NR cell
Spec structure for NR CGI reading
  Option 1
    For NR capable UE in EN-DC, NE-DC, NR-DC, NR SA, or LTE SA operation, for CGI reading of NR neighbour cell
      all the interruption requirements on NR serving cells will be specified in section 8.2 in TS 38.133,
      and all the interruption requirements on LTE serving cells will be specified in TS36.133.

## Slide 9: WF
Companies are encouraged to bring further analysis on the open issues and other potential issues in the RAN4#93 meeting .