## Slide 1: Way Forward on 5G Broadcasting
Qualcomm
3GPP TSG-RAN WG4 Meeting #92bis
Chongqing , China, 14th August – 18th October, 2019
R4-1912849
Document for: Approval

## Slide 2: RRM Requirement
MBSFN measurement period
  Long numerology: MAX(640 ms, period during which the UE decodes 5 symbols containing PMCH transmissions)
  Short numerology: follow legacy MBFSN measurement period
The current measurement requirements on FeMBMS/Unicast-mixed carrier in R14 can be reused in R16 for LTE-based 5G terrestrial broadcast
MCH BLER report period
  Follow legacy MBSFN
Phase synchronization accuracy
  Companies are encouraged to provide analysis or simulation results to determine the 300us CP length requirement
CP length for MBSFN subframe | Requirement
100µs |  5 s
300µs | TBD

## Slide 3: RRM Requirement
Numerology switch interruption requirement
  Option 1(HW): The current numerology switching delay requirements and interruption requirements due to numerology switching in R14 can be reused in R16 for LTE-based 5G terrestrial broadcast
  Other options are not precluded
Cell identification and detection requirement
  No additional requirement is needed, legacy requirement applies to Rel-16 for mixed cells
RSRP/RSRQ accuracy requirement
  Follow legacy MBSFN accuracy requirement

## Slide 4: RSRP report mapping
  Option 1 (QC)
    For long numerology with 370.37Hz SCS
    For short numerology with 2.5kHz SCS
Reported value | Measured quantity value | Unit
MBSFN_RSRP_00 | MBSFN_RSRP  -156 | dBm / 370Hz
MBSFN_RSRP_01 | -156  MBSFN_RSRP < -155 | dBm / 370Hz
MBSFN_RSRP_02 | -155  MBSFN_RSRP < -154 | dBm / 370Hz
… | … | …
MBSFN_RSRP_95 | -62  MBSFN_RSRP < -61 | dBm / 370Hz
MBSFN_RSRP_96 | -61  MBSFN_RSRP < -60 | dBm / 370Hz
MBSFN_RSRP_97 | -60  MBSFN_RSRP | dBm / 370Hz
Reported value | Measured quantity value | Unit
MBSFN_RSRP_00 | MBSFN_RSRP  -148 | dBm / 2.5 kHz
MBSFN_RSRP_01 | -148  MBSFN_RSRP < -147 | dBm / 2.5 kHz
MBSFN_RSRP_02 | -147  MBSFN_RSRP < -146 | dBm / 2.5 kHz
… | … | …
MBSFN_RSRP_95 | -54  MBSFN_RSRP < -53 | dBm / 2.5 kHz
MBSFN_RSRP_96 | -53  MBSFN_RSRP < -52 | dBm / 2.5 kHz
MBSFN_RSRP_97 | -52  MBSFN_RSRP | dBm / 2.5 kHz

## Slide 5: RSRQ report mapping
  For long numerology with 370.37Hz SCS
  For short numerology with 2.5kHz SCS
Reported value | Measured quantity value | Unit
MBSFN_RSRQ_00 | MBSFN_RSRQ  -38 | dB
MBSFN_RSRQ_01 | -39.0  MBSFN_RSRQ < -38.3 | dB
MBSFN_RSRQ_02 | -38.3  MBSFN_RSRQ < -37.6 | dB
… | … | …
MBSFN_RSRQ_30 | -17.7  MBSFN_RSRQ < -17 | dB
MBSFN_RSRQ_31 | -16  MBSFN_RSRQ | dB
Reported value | Measured quantity value | Unit
MBSFN_RSRQ_00 | MBSFN_RSRQ  -31 | dB
MBSFN_RSRQ_01 | -31  MBSFN_RSRQ < -30.4 | dB
MBSFN_RSRQ_02 | -30.4  MBSFN_RSRQ < -29.8 | dB
… | … | …
MBSFN_RSRQ_30 | -13.6  MBSFN_RSRQ < -13 | dB
MBSFN_RSRQ_31 | -13  MBSFN_RSRQ | dB