## Slide 1: WF on Guardbands for NR-U
Nokia,
R4-1912869
3GPP TSG-RAN WG4 #92bis
Chongqing, China,
10th Oct. - 18th Oct. 2019

## Slide 2: Definition of Inter-carrier guardbands OPTION 1
  In the WF [R4-1910386] from previous meeting, it was agreed that:
    RAN4 is tasked to specify necessary sizes of the inter-carrier guardbands and number of PRBs needed for intra-carrier guards to meet spectral emission mask defined for NR-U.
  This meeting it is proposed to:
  -> Reuse the minimum guard-bands definition dependent on configured bandwidth as done for Rel-15 and given in Table 5.3.3-1 (TS 38.101-1).

## Slide 3: Definition of Intra-carrier guardbands OPTION 1
  In the WF [R4-1910386] from previous meeting, it was agreed that:
    Intra-carrier guards for a carrier configured by a serving cell are defined as an integer number of full PRBs. - These are defined on a common RB grid which reference point is configured by the gNB as specified in section 5.3.4 of 38.101-1. - No intra-carrier guards are defined for 20 MHz carriers
  This meeting it is proposed to:
  -> Define the Intra-carrier GBs following the equation given in R4-1911611
Parameter | Value
n | intra-carrier GB (ICGB) index [n=0,1,…,]
FUP | First-usable-PRB CRB index
[kHz] | BW between first usable PRB of a lowest sub-band of a carrier and edge of channel band, needs to meet Minimum inter-carrier GB requirement
BWsb [kHz] | BW of a sub-band, i.e. 20 000 kHz for 5GHz spectrum
GBmin(SCS) [kHz] | Minimum intra-carrier GB requirement (w.r.t. 20 MHz channel raster) for given sub-band size defined separately for each subcarrier spacing (SCS) value. GBmin(SCS) can be a two-dimensional table, where one dimension is sub-band size (i.e. 20 MHz and another dimension is SCS (e.g. 15 kHz, 30 kHz, 60 kHz). Example, 30 kHz SCS: GBmin(20 MHz, 30 kHz)=805 kHz
PRBsize [kHz] | 12*SCS: 180 kHz for 15 kHz SCS and 360 kHz for 30 kHz SCS
Parameter | Value
n | 
FUP | First-usable-PRB CRB index
 | BW between first usable PRB of a lowest sub-band of a carrier and edge of channel band, needs to meet Minimum inter-carrier GB requirement
BWsb [kHz] | BW of a sub-band, i.e. 20 000 kHz for 5GHz spectrum
GBmin(SCS) [kHz] | Minimum intra-carrier GB requirement (w.r.t. 20 MHz channel raster) for given sub-band size defined separately for each subcarrier spacing (SCS) value. GBmin(SCS) can be a two-dimensional table, where one dimension is sub-band size (i.e. 20 MHz and another dimension is SCS (e.g. 15 kHz, 30 kHz, 60 kHz). Example, 30 kHz SCS: GBmin(20 MHz, 30 kHz)=805 kHz
PRBsize [kHz] | 12*SCS: 180 kHz for 15 kHz SCS and 360 kHz for 30 kHz SCS

## Slide 4: Definition of Intra-carrier guardbands OPTION 1
  The second equation could me omitted and a number of needed minimum intra-carrier guard PRBs could be agreed instead. We are proposing 5 PRBs which will be enough to contain the min NR GB of 805kHz plus a margin as it is rounded up to the first integer PRB number.

## Slide 5: Definition of inter- and intra-carrier GB OPTION 2
For each channel bandwidth, ,maximum spectrum utilization (including possible intra-carrier GB) in accordance with licensed bands (with agreed change for 20 MHz@60 k)
CA nominal carrier spacing a multiple of 60 kHz to allow common FFT regardless of SCS
Intra-carrier guards within a wider carrier fully overlap both the intra-carrier and inter-carrier guards of narrower carriers (or at least the inter-carrier GBs of the 20 MHz carriers) to avoid interference between systems using different bandwidths
Enable alignment with Wi-Fi bonded channels (20, 40, 80) MHz (ETSI requirement in case of ‘short-LBT’ on some LBT sub-bands)
Center frequencies of 20 MHz carriers aligned with Wi-Fi center frequencies ±200 kHz (ETSI requirement)
Inter- and intra-carrier guard bands in accordance with the above rules
Example from R4-1911547 (has to be modified to accommodate 60 kHz)

## Slide 6: Definition of Guardbands for Wideband Operation
  In the WF [R4-1910386] from previous meeting, it was agreed that:
    Define two different types of guardbands for NR-U: - Carrier guardbands (inter-carrier guardbands) - In-carrier guardbands (intra-carrier guards)
  This meeting there is consensus to:
  -> Define two different types intra-carrier guards:
    Type-1 Intra-carrier guardband
    Type-2 Intra-carrier guardband

## Slide 7: Scheduling of Intra-carrier guardbands
  In the WF [R4-1910386] from previous meeting, it was agreed that:
    The intra-carrier guard band could be scheduled if it is located within the adjacent contiguous LBT successful sub-bands where all scheduled LBT sub-bands have passed. Introduction of flexible guard-bands at sub-block edge is left FFS. Meaning scheduling of either additional or a reduced number of sub-block edge guard PRBs.
  This meeting there is consensus to:
  -> Scheduling in Type-2 intra-carrier GBs is not feasible

## Slide 8: References:
  R4-1911611, NR-U - Scheduling of guard PRBs, Nokia
  R4-1912382, On channel raster, SSB raster and wide-band operation for NR-U, LG
  R4-1910852, Guard band on wideband operation, Huawei
  R4-1912489, NR-U wideband operation, Qualcomm
  R4-1911547, Channel raster design and intra-carrier GB for wideband (WB2) operation, Ericsson