## Slide 1: WF on the NR-U channel raster on 5GHz band
Ericsson,
3GPP TSG-RAN4 Meeting #92bis R4-1912870 Chongqing, China, 14-18 Oct, 2019

## Slide 2: Background
Different companies have different channel raster design approach with below contribution:
  R4-1910850, "Channel arrangement for NR-U" (Huawei, HiSilicon).
  R4-1911025, "On NR-U channel raster" (Intel Corporation).
  R4-1911729, "Discussion on channel raster for NR-U" (ZTE Corporation).
  R4-1912016, "channel raster design of Rel-16 NR-U for 5GHz band" (Ericsson).
  R4-1912311, "Channel raster in NR-U" (Qualcomm Incorporated).
  R4-1912335, "Channel raster for 5GHz NR-U band n46" (Nokia, Nokia Shanghai Bell).
  R4-1911169, "Discussion on channel raster for NR-U band n46" (vivo).
  R4-1912382, "On channel raster, SSB raster and wide-band operation for NR-U" (LG Electronics Finland).
This slide propose the possible converged channel raster on channel raster design on NR-U on 5GHz band (n46)

## Slide 3: Proposal on design principle
Single channel raster on 60kHz SCS using selection rule to pick Nref closest to corresponding WIFI center. Raster points are defined for bandwidths of 20MHz, 40MHz, 60MHz and 80MHz.
  For 10 MHz channel BW, follow the same rule for the corresponding centre frequencies of 5730 and 5830MHz.
FFS for 100MHz

## Slide 4: Proposal
Nref (10MHz, 20MHz, 40MHz, 60MHz and 80MHz) lists on next slides
Company are encouraged to submit CR to describe the generic n46 channel raster with additional notes for 10MHz, 20MHz, 40MHz, 60MHz and 80MHz channel bandwidth raster for next meeting.

## Slide 5: Further alignement on the specific Nref points with company view
NR-U channel raster following the WIFI bonding rule (20MHz, 40MHz , 80MHz) and 10MHz
  Group 1 is agreed
NR-U channel raster (20MHz, 40MHz , 80MHz) for example at highest end of n46 Band (5850MHz to 5925MHz) not used by WIFI
  Group 2: FFS
Addtional NR-U channel raster ( 40MHz , 80MHz) with overlaping the WIFI channel
  Group 3 : FFS at some of points below, other points in Group3 table agreed.
    Nref at WIFI center frequency of 5330, 5490 MHz
NR-U channel raster 60MHz within an 80 MHz bonded WIFI channel
  Group 4:
    60 MHz aligned with the low frequency edge of an 80 MHz bonded WiFi channel - Agreed
    60 MHz aligned with the high frequency edge of an 80 MHz bonded WiFi channel - Agreed
NR-U channel raster 60MHz partially overlapped with 80 MHz bonded WiFi channel
  Group 5: Agreed
Company are encouraged to propose the NR-U channel raster and adress above FFS points at next meeting

## Slide 6: Nref (group 1)- follow WIFI bonding rule (20MHz, 40MHz, 80MHz) and 10MHz
WIFI channel center frequency (40MHz BW) | Fn on raster (40MHz BW) | Nref (40MHz BW)
5170 | 5170.02 | 744668
5190 | 5190 | 746000
5230 | 5230.02 | 748668
5270 | 5269.98 | 751332
5310 | 5310 | 754000
5510 | 5509.98 | 767332
5550 | 5550 | 770000
5590 | 5590.02 | 772668
5630 | 5629.98 | 775332
5670 | 5670 | 778000
5710 | 5710.02 | 780668
5755 | 5755.02 | 783668
5795 | 5794.98 | 786332
WIFI channel center frequency (80MHz) | Fn on raster (80MHz) | Nref (89MHz)
5210 | 5209.98 | 747332
5290 | 5290.02 | 752668
5530 | 5530.02 | 768668
5610 | 5610 | 774000
5690 | 5689.98 | 779332
5775 | 5775 | 785000
Specific for 10MHz
WIFI channel center frequency for 20MHz | Fn on raster for 20MHz | Nref for 20MHz
5180 | 5179.98 | 745332
5200 | 5200.02 | 746668
5220 | 5220 | 748000
5240 | 5239.98 | 749332
5260 | 5260.02 | 750668
5280 | 5280 | 752000
5300 | 5299.98 | 753332
5320 | 5320.02 | 754668
5500 | 5500.02 | 766668
5520 | 5520 | 768000
5540 | 5539.98 | 769332
5560 | 5560.02 | 770668
5580 | 5580 | 772000
5600 | 5599.98 | 773332
5620 | 5620.02 | 774668
5640 | 5640 | 776000
5660 | 5659.98 | 777332
5680 | 5680.02 | 778668
5720 | 5719.98 | 781332
5745 | 5745 | 783000
5765 | 5764.98 | 784332
5785 | 5785.02 | 785668
5805 | 5805 | 787000
5825 | 5824.98 | 788332

## Slide 7: Nref (group 2)- Channel raster not used by WIFI (20MHz, 40MHz, 80MHz) (FFS)
WIFI channel center frequency (40MHz BW) | Fn on raster (40MHz BW) | Nref (40MHz BW)
5835 | 5835 | 789000
5875 | 5875.02 | 791668
WIFI channel center frequency (80MHz) | Fn on raster (80MHz) | Nref (89MHz)
5855 | 5854.98 | 790332
WIFI channel center frequency for 20MHz | Fn on raster for 20MHz | Nref for 20MHz
5160 | 5160 | 744000
5340 | 5340 | 756000
5480 | 5479.98 | 765332
5700 | 5700 | 780000
5845 | 5845.02 | 789668
5865 | 5865 | 791000
5885 | 5884.98 | 792332
5905 | 5905.02 | 793668

## Slide 8: Nref (group 3)- Addtional raster (40Mhz and 80MHz) overlap with WIFI (FFS on red Nref)
WIFI channel center frequency (40MHz BW) | Fn on raster (40MHz BW) | Nref (40MHz BW)
5330 | 5329.98 | 755332
5490 | 5490 | 766000
5815 | 5815.02 | 787668
WIFI channel center frequency (80MHz BW) | Fn on raster (80MHz BW) | Nref (80MHz BW)
5190 | 5190 | 746000
5795 | 5794.98 | 786332
5170 | 5170.02 | 744668

## Slide 9: Nref (group 4)- 60MHz channel raster Following 80MHz WIFI bonding
WIFI channel center frequency (60MHz BW) | Fn on raster (60MHz BW) | Nref (60MHz BW)
5200 | 5200.02 | 746668
5220 | 5220 | 748000
5280 | 5280 | 752000
5300 | 5299.98 | 753332
5500 | 5500.02 | 766668
5520 | 5520 | 768000
5540 | 5539.98 | 769332
5600 | 5599.98 | 773332
5620 | 5620.02 | 774668
5680 | 5680.02 | 778668
5700 | 5700 | 780000
5765 | 5764.98 | 784332
5785 | 5785.02 | 785668

## Slide 10: Nref (Group 5)- additional 60MHz channel raster overlap 80MHz WIFI bonding
WIFI channel center frequency (60MHz BW) | Fn on raster (60MHz BW) | Nref (60MHz BW)
5180 | 5179.98 | 745332
5320 | 5320.02 | 754668
5580 | 5580 | 772000
5805 | 5805 | 787000