## Slide 1: Draft WF on IAB system parameter
Samsung

## Slide 2: Background-agreement in RAN2#90bis
IAB node specifications should support the below FR2 NR bands.
For new FR2 bands introduced in future, RAN4 will discuss the introducation of new FR2 bands into IAB specifications after RF requirements for FR2 bands are completd.
Introducing FR1 band(s) in IAB specifications are not precluded. Further discussion on introducation of FR1 bands is needed.
Companies are encouraged to bring the analysis for introducing FR1 band(s) in IAB specfications.
NR operating band | Uplink (UL) and Downlink (DL) operating band BS transmit/receive UE transmit/receive FUL,low – FUL,high FDL,low – FDL,high | Duplex Mode
n257 | 26500 MHz – 29500 MHz | TDD
n258 | 24250 MHz – 27500 MHz | TDD
n260 | 37000 MHz – 40000 MHz | TDD
n261 | 27500 MHz – 28350 MHz | TDD

## Slide 3: Background-agreement in RAN2#91
Agreement: It is proposed to introduce FR1 NR bands n41 and n79 in the IAB node specification.
Whether the 1-C BS type will be considered for FR1 is FFS
Note: there is a typo in online agreement.
NR operating band | Uplink (UL) and Downlink (DL) operating band FUL,low – FUL,high FDL,low – FDL,high | Duplex Mode
n41 | 2496 MHz – 2690 MHz | TDD
n79 | 4800 MHz – 5000 MHz | TDD

## Slide 4: Agreement on operating band
Include all FR2 operating bands introduced in Rel-15, i.e. n257, n258, n260 and n261 for IAB specifications.
  For new FR2 bands introduced in future, it is not precluded to be included in IAB specification depending on consensus.
Introduce FR1 band n41 and n79 in IAB specifications.
NR operating band | Uplink (UL) and Downlink (DL) operating band FUL,low – FUL,high FDL,low – FDL,high | Duplex Mode
n41 | 2496 MHz – 2690 MHz | TDD
n79 | 4400 MHz – 5000 MHz | TDD

## Slide 5: WF on FR, SU and channel arrangement
For below aspects existing definition in NR BS spec TS38.104 shall be applied for IAB
  Frequency range, i.e. FR1 and FR2
  Spectrum utilization, including transmission RB allocation in table 5.3.2.-1 for FR1 and table 5.3.2-2 for FR2, and minimum guard band in table 5.3.3-1 for FR1 and in table 5.3.3-2 for FR2.
  Channel arrangement, i.e. channel spacing, channel raster and sync raster defined in subclause 5.4
Regarding how to implement above requirements in IAB specification there are two options:
  Option 1: refer to TS38.104 [Samsung,ZTE, Nokia, Ericsson]
  Option 2: include all corresponding the same definitions of TS38.104 in IAB spec [Huawei, Qualcomm]

## Slide 6: WF on RB alignment
The RB alignment defined in TS38.101-1 and/or TS 38.101-2 shall be applied for IAB-MT
The RB alignment defined in TS38.104 shall be applied for IAB-DU.
Regarding how to implement above requirements in IAB specification there are two options:
  Option 1: refer to TS38.104 for IAB-DU, and TS38.101-1 and/or TS 38.101-2 for IAB-DU and for IAB-MT respectively[ZTE, Nokia, Qualcomm, Samsung]
  Option 2: include all corresponding the same definitions of TS38.104, and TS38.101-1 and/or 38.101-2 in IAB spec[Ericsson,Huawei]

## Slide 7: WF on IAB channel bandwidth per operating band
NR band / SCS / IAB channel bandwidth |  |  |  |  | 
NR Band | SCS kHz | 50 MHz | 100 MHz | 200 MHz | 400 MHz
n257 | 60 | Yes | Yes | Yes | 
 | 120 | Yes | Yes | Yes | Yes
n258 | 60 | Yes | Yes | Yes | 
 | 120 | Yes | Yes | Yes | Yes
n260 | 60 | Yes | Yes | Yes | 
 | 120 | Yes | Yes | Yes | Yes
n261 | 60 | Yes | Yes | Yes | 
 | 120 | Yes | Yes | Yes | Yes
The channel bandwidth per operating band can be brought from TS38.104 for operating bands supported by IAB as table below
IAB-DU channel bandwidth shall be declared
Options for IAB-MT channel bandwidth:
    Alternative 1: IAB MT will support all mandatory bandwidth
      optional bandwidth depends on it capability
    Alternative 2: IAB MT will declare the supported maximum channel bandwidth
      All channel bandwidth smaller that the maximum one would be supported by default to ensure the MT behavior in initial access according to RAN4 agreement on “UE can access the cell if UE supports a channel bandwidth which is equal to or narrower than the channel bandwidth in SIB1 and is equal to or wider than the initial BWP-bandwidth.” in R4-1910522
    Alternative 3: IAB-MT will declare the supported channel bandwidths (same as BS approach) [Ericsson, Huawei]
NR band / SCS / IAB channel bandwidth |  |  |  |  |  |  |  |  |  |  |  |  |  | 
NR Band | SCS kHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 30 MHz | 40 MHz | 50 MHz | 60 MHz | 70 MHz | 80 MHz | 90 MHz | 100 MHz
n41 | 15 |  | Yes | Yes | Yes |  | Yes | Yes | Yes |  |  |  |  | 
 | 30 |  | Yes | Yes | Yes |  | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes
 | 60 |  | Yes | Yes | Yes |  | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes
n79 | 15 |  |  |  |  |  |  | Yes | Yes |  |  |  |  | 
 | 30 |  |  |  |  |  |  | Yes | Yes | Yes |  | Yes |  | Yes
 | 60 |  |  |  |  |  |  | Yes | Yes | Yes |  | Yes |  | Yes