## Slide 1: WF on Full power transmission for eMIMO
vivo
3GPP TSG-RAN WG4#92bis Meeting R4-1912897
Chongqing, China, 14th – 18th Oct, 2019

## Slide 2: Way Forward (1)
Focus on Single layer transmission with two and/or one logical antenna ports configuration
Consider test configurations for measurements.
For Mode 1, Consider verification of the feature including test configurations, at least including rank=1 TPMI=2, i.e.
For Mode 2, consider following verification points:
  [Rank1, 2 ports, TPMI 0/1 to achieve full power.]
    (Note: New feature for capability 3 UE for 2 port transmission. However can be circumvent by single port transmission as in Rel-15)
  Further test point are not precluded
Notes: Agreement
For 2Tx in mode 1,
For rank=1, TPMI=2, TPMI=0, TPMI=1 are included in new codebook subset for non-coherent UEs with power scaling defined as in [38.213] Rel-15
For rank=2, TPMI=0 is included in the new codebook subset
Agreement
For Mode2,
Power scaling factor is equal to 1 for the reported TPMI precoders that supports full power Tx
for the other TPMI precoders, if only one SRS resource is configured, the power scaling factor is determined by #non-zero-PUSCH-port divided by #SRS-ports
for the other TPMI precoders, the power scaling factor is determined by #non-zero PUSCH port/#SRS ports in the SRS resource indicated by SRI

## Slide 3: Way Forward (2)
Test applicability should consider different UE capabilities regarding the Tx power for each RF chain.
  E.g. Whether there is no need for Capability 1 UE to do any testing;

## Slide 4: Reference
[1] R4-1911411, Discussion on impact of NR eMIMO on RF requirement, Samsung, RAN4#92bis
[2] R4-1911171, Impact analysis of RF requirments for eMIMO Full Tx Power, vivo, RAN4#92bis
[3] R4-1912386, New methods of handling UEs with multiple TX ports, Qualcomm Incorporated, RAN4#92bis
[4] R4-1912507, On uplink full power transmission, Huawei, RAN4#92bis