## Slide 1: WF on Assumptions for PI/2 DMRS Simulation for FR1 and FR2
Qualcomm
3GPP TSG-RAN WG4 NR #92bis
Chongqing, China, 14th - 18th Oct 2019
R4-1912898

## Slide 2: Background
Rel-15:
  Pi/2 BPSK modulation for PUSCH was intended to enable a lower PAPR UL waveform relative to QPSK and QAM.
  The full benefit of BPSK could not be realized due to the DMRS of these waveforms being a higher PAPR Zadoff-Chu modulation.
WI [1] was initiated to investigate the use of different modulation schemes for DMRS to lower its PAPR to be closer to that of the PUSCH Pi/2 BPSK modulation.
  RAN1 has defined a new Pi/2 BPSK modulated DMRS[2,3,4,5] which has a lower PAPR compared to that of Zadoff-Chu DMRS
[6] has simulation results that show Pi/2 BPSK having better EVM and ACLR performance for both FR1 and FR2 compared to Zadoff-Chu
RAN4 investigation can help determine if a MPR benefit exists from using the Pi/2 BPSK DMRS over Zadoff-Chu DMRS

## Slide 3: Way Forward (FR1)
Perform MPR simulations based on the following assumptions for PC3 with waveform 1 and waveform 2
Simulation assumptions for FR1
  Waveform1 : shaped DFT-s-OFDM Pi/2 BPSK PUCSH data with 1 symbol of Zadoff-Chu DMRS
  Waveform2 : shaped DFT-s-OFDM Pi/2 BPSK PUCSH data with 1 symbol of Pi/2 BPSK DMRS
  Waveform1 and waveform2 SCS=15KHz
  Waveform1 and waveform2 BW=20MHz
  Waveform1 and waveform 2 RB_start/LCRB allocations :
    RB_case 1 = RB start 0 LCRB=2
    RB_case 2 = RB start 104 LCRB=2
    RB_case 3 = RB start 0 LCRB=1
    RB_case 4 = RB start 105 LCRB=1
    RB_case 5 = RB start 0 LCRB=100
    RB_case 6 = RB start 25 LCRB=50
    RB_case 7 = RB start 1 LCRB=1
    RB_case 8 = RB start 104 LCRB=1
  Waveform1 and waveform2 filter shaping function [0.3 1 0.3]

## Slide 4: Way Forward (FR1)
Results for FR1
Collect MPR results for each RB_case for both waveforms.
Calculate Delta MPR as the difference between the 2 MPR values for each RB_case.
Waveform | MPR |  |  |  |  |  |  | 
 | RB_case1 | RB_case2 | RB_case3 | RB_case4 | RB_case5 | RB_case6 | RB_case7 | RB_case8
1 | MPR11 | MPR12 | MPR13 | MPR14 | MPR15 | MPR16 | MPR17 | MPR18
2 | MPR21 | MPR22 | MPR23 | MPR24 | MPR25 | MPR26 | MPR27 | MPR28
Delta MPR =MPR1x - MPR2x X=[1,2,3,4,5,6,7,8] |  |  |  |  |  |  |  | 

## Slide 5: Way Forward (FR2)
Perform MPR simulations based on the following assumptions for PC3 with waveform 1 and waveform 2
Simulation assumptions for FR2
  Waveform1 : shaped DFT-s-OFDM Pi/2 BPSK PUCSH data with 1 symbol of Zadoff-Chu DMRS
  Waveform2 : shaped DFT-s-OFDM Pi/2 BPSK PUCSH data with 1 symbol of Pi/2 BPSK DMRS
  Waveform1 and waveform2 SCS=120KHz
  Waveform1 and waveform2 BW=100MHz
  Waveform1 and waveform2 RB_start/LCRB allocations :
    RB_case 1 = RB start=0, LCRB=64
    RB_case 2 = RB start=0, LCRB=1
    RB_case 3 = RB start=65, LCRB=1
    RB_case 4 = RB start=22, LCRB=20
    RB_case 5 = RB start=22, LCRB=1
    RB_case 6 = RB start=43, LCRB=1
  Waveform1 and waveform2 filter shaping function [0.3 1 0.3]

## Slide 6: Way Forward (FR2)
Waveform | MPR |  |  |  |  | 
 | RB_case1 | RB_case2 | RB_case3 | RB_case4 | RB_case5 | RB_case6
1 | MPR11 | MPR12 | MPR13 | MPR14 | MPR15 | MPR16
2 | MPR21 | MPR22 | MPR23 | MPR24 | MPR25 | MPR26
Delta MPR =MPR1x - MPR2x X=[1,2,3,4,5,6] |  |  |  |  |  | 
Results for FR2
Collect MPR results for each RB_case for both waveforms.
Calculate Delta MPR difference between the 2 waveforms

## Slide 7: References
RP-182863, “Revised WID: Enhancements on MIMO for NR”, RAN1#82, Sorrento, Italy, December 2018
RAN1 95 Chairman’s notes, Spokane, USA, November 2018
RAN1 1901 Ah meeting Chairman’s notes, Taipei, Taiwan, January 2019
RAN1 96 meeting Chairman’s notes, Athens, Greece, March 2019
RAN1 96b meeting Chairman’s notes, Xi’an, China, April 2019
R4-1912560, “PI/2 BPSK DMRS”, RAN4_#92bis, Chongqing, China, Oct 2019