## Slide 1: WF on Contiguous ULCA MPR for FR1
Qualcomm Inc, Skyworks
3GPP TSG-RAN WG4 NR #92-Bis
Chongqing, China, 14th - 18th Oct 2019
R4-1912909

## Slide 2: Background
WF was agreed to outline general requirements [2] to proceed with simulations and measurements.
Company A has provided measurements [4] and proposal to specify MPR [3].
Company B has provided preliminary simulations and a proposal to specify MPR [1].

## Slide 3: WF Plan for MPR specification and evaluation
Option 1 from Company A
Option 2 from Company B.
Other options not precluded.
Outline a set of common measurement test points and simulation plan with assumptions

## Slide 4: Defining Inner/Outer MPR Option1 – Contiguous Allocations
General requirements for single CC are very similar to that of contiguous ULCA because requirements are derived from BWCA.
Inner/Outer definition is the same as single carrier, but we define thresholds in terms of frequency rather than in terms of RBs due to CCs having different SCS.
With this approach, we can easily determine CA_MPR and leverage the single CC MPR table as discussed in [1] for 2CCs.

## Slide 5: Defining MPR Option1 – Non-Contiguous Allocations
The same approach can be used as in LTE, except the Allocation ratio should be the defined as A = (PRB1*SCS1 +PRB2*SCS2)/ (NRB1*SCS1 +NRB2*SCS2)
Look at EVM, SEM, ACLR and Gen. Spurious
Note that EVM could dominate at higher order modulations or with CP-OFDM waveforms.

## Slide 6: Defining Inner/Outer MPR Option 2
Inner/outer defined in terms of where IMD3 falls
  Inner allocations are such that IMD3 fall within the 2 CC aggregated BW thus
    Worst case IMD5/7/9 fall in -13dBm/MHz SEM region
  Outer allocation has at least 1 IMD3 falling in the adjacent aggregated BW thus
    Worst case IMD3 falls in the -13dBm/MHz region
    Worst case IMD5 falls in the -30dBm/MHz region
  Note that outer allocation are by default non-contiguous while inner allocations can be contiguous or non contiguous but this has no impact on inner MPR.
This results into the following equations from [3]
(2*RBstart1-RBtot1/2)*SCS1+(RBtot2/2-RBstart2-LCRB2)*SCS2 ≥ (BW1+BW2)/24 (A)
AND
(RBstart1-RBtot1/2)*SCS1+(3/2*RBtot2-2*(RBstart2+LCRB2))*SCS2 ≥ (BW1+BW2)/24 (B)
Note: those equations could also use Fstart/Fstop parameters
Separate MPR curves for inner and outer (BW ratio or absolute BW based)

## Slide 7: Simulations and Measurement Plan
Simulation assumptions:
  Contiguous Allocations in each CC, including allocations that span across the gap.
  20MHz+20MHz with same SCS in each CC = 15KHz for Waveform configurations of DFT-s-OFDM + DFT-s-OFDM and CP-OFDM + CP-OFDM. Look at QPSK, 16QAM, 64QAM, and 256QAM
  Other BW combinations can be analysed
  Non-contiguous Allocations with contiguous allocation in each CC, with no allocation spanning across the gap.
  Ensure that IMD of RB configuration lands in general spurious, all regions of SEM as well as within channel BW.
Measurements:
  20+20, 50+50, 100+100, 60+100
  Same SCS, DFT-s-OFDM + DFT-s-OFDM and CP-OFDM + CP-OFDM, QPSK
  Contiguous allocations only in each CC.

## Slide 8: References
R4-1912908, “Intra-band Contiguous ULCA MPR for FR1”, Qualcomm Inc., RAN4#92-Bis, Chongqing, China, October 2019
R4-1910273 “WF for intra-band ULCA for FR1 power class 3”, Huawei, HiSilicon, Qualcomm, Skyworks, MediaTek, RAN4#92, Ljubljana, Slovenia, August 2019
R4-1908815 “Discussion on 2UL Allocation Types and their Impact on Required PA Back-off and MSD”, Skyworks, Ljubljana, Slovenia, August 2019
R4-1908839 “Initial Measurement Results for Intra-band Contiguous NR UL CA for FR1”, Skyworks, RAN4#92, Ljubljana, Slovenia, August 2019