## Slide 1: WF on Rel-15 EN-DC power class
Sprint, vivo, CMCC, OPPO, Skyworks
3GPP TSG-RAN WG4 Meeting #92bis R4-1912918 Chongqing, China, 14-18 Oct 2019

## Slide 2: Background
Proposals [1-3] were presented which discuss ENDC power class.
Because current R15 signalling doesn’t distinguish NR power class (PC) between EN-DC and SA mode, one case was identified as causing the ambiguity
Problematic case: For SA/NSA dual mode UE which support 2Tx UL MIMO in SA with 23+23dBm PA configurations but only 1Tx NR in ENDC.
Identified problem: this UE may report NR=PC2 in “RAN2 NR PC capability signalling”, but can only support NR=PC3 in NSA mode if only 1Tx NR in EN-DC

## Slide 3: WF
RAN4 agrees that
  For the scenario, UE supports PC2 in NR with 2x23 dBm through transparent tx diversity and PC3 for LTE and PC2 for EN-DC will report PC3 for LTE, PC2 for NR, PC2 for EN-DC, even though it only support PC3 for NR in EN-DC
    In above case, in Rel-15 the network would not know that the NR power class was limited to PC3 in EN-DC operation, so performance may be sub-optimal, but functionality is not broken
  no new signalling to be introduced in R15 for this case.
  RAN4 will study the necessity to introduce new power class capability signalling in R16
Inform RAN2 the above RAN4 agreement.

## Slide 4: Draft LS on ENDC power class in R15
1. Overall Description:
RAN4 has discussed the clarification of ENDC power class in R15. For SA/NSA dual mode UE which support PC2 2Tx UL MIMO in SA but only 1Tx NR in ENDC, power class of NR in ENDC may be different from the power class of SA NR in capability signalling because of UE configurations e.g. UE PA configurations of 23+23dBm with transparent tx diversity can support NR=PC2 in SA UL MIMO but may only support NR=PC3 in NSA mode because only 1Tx NR in EN-DC.
As the solution, RAN4 has agreed that for the scenario UE supports PC2 in NR with 2x23 dBm through transparent tx diversity and PC3 for LTE and PC2 for EN-DC will report PC3 for LTE, PC2 for NR, PC2 for EN-DC, even though it only support PC3 for NR in EN-DC.
2. Actions:
To RAN 2:
RAN4 kindly ask RAN2 to be informed about the above agreement in RAN4.

## Slide 5: Reference
(1) R4-1910728 About EN-DC power class clarification OPPO
(2) R4-1910810 On clarification of ENDC power class in R15 vivo
(3) R4-1912509 On EN-DC power class Huawei, HiSilicon