## Slide 1: WF on UL Power Boost and IBE Relaxation
Qualcomm, Skyworks
­­­3GPP TSG-RAN WG4 Meeting #92-Bis R4-1912975
Chongqing, CN, 14-18 Oct. 2019

## Slide 2: Background
Applicability:
  Rel-16 FR2 UE

## Slide 3: WF
UE Tx power boost in exchange for IBE relaxation shall be an optional capability for rel-16 FR2 Ues
The network controls when a supporting UE shall boost its Tx power by not meeting the in-band emission requirements.
Companies that support UE Tx power boost in exchange for IBE relaxation are encouraged to study:
  Feasible power boost values
  Feasibility of increasing MPR=0 power level under boost conditions shall be considered more
  Waveform types, modulation order
  Any RB Allocation limitations to enable boost
  Network control mechanism

## Slide 4: Summary of contributions in RAN4#92-Bis supporting power boost
Source | Waveform type | RB Allocation | Boost Value
[1] | DFT-s-QPSK DFT-s-BPSK | Region 1 in MPR table, ok to extend per [3] | 1.0dB
[2] | DFT-s-QPSK | ‘Extended’ Region 1 | Simulation data suggests > 0.9dB
[3] | DFT-s-QPSK | ‘Extended’ Region 1 | 1.0dB ‘Seems feasible’
Region 1 extension proposed in [3], green region versus interior of red triangle

## Slide 5: WF
R4-1911236, ‘ Power Boost and IBE in FR2’, Qualcomm, RAN4#92-Bis, Chongqing, Oct 2019
R4-1911523, ‘Region 1 Extension for Power Class 3 Operation in FR2 and output power boosting’, Nokia, RAN4#92-Bis, Chongqing, Oct 2019
R4-1912464, ‘Input to WF on Region 1 Extension for Power Class 3 Operation in FR2 and output power boosting’, Skyworks, RAN4#92-Bis, Chongqing, Oct 2019