## Slide 1: WF on UE RF requirements for adding channel BW to band n1
Ericsson, Qualcomm, Huawei, China Unicom
3GPP TSG-RAN WG4 Meeting #92bis R4-1912978
Chongqing, China, October 14-18 2019

## Slide 2: Background
Contributions and discussion on:
  REFSENS values [1], [3] and [4]
  A-MPR simulation assumptions [2], [3], [5], [6].

## Slide 3: REFSENS values: agreement
Following values were agreed:
Operating band / SCS / Channel bandwidth / Duplex mode |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Operating Band | SCS kHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 30 MHz | 40 MHz | 50 MHz | 60 MHz | 80 MHz | 90 MHz | 100 MHz | Duplex Mode
n1 | 15 | 25 | 501 | 751 | 1001 | 1281 | 1281 |  |  |  |  |  |  | FDD
 | 30 |  | 24 | 361 | 501 | 641 | 641 |  |  |  |  |  |  | 
 | 60 |  | 101 | 18 | 24 | 301 | 301 |  |  |  |  |  |  | 
Operating band / SCS / Channel bandwidth / Duplex-mode |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Operating Band | SCS kHz | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | 25 MHz (dBm) | 30 MHz (dBm) | 40 MHz (dBm) | 50 MHz (dBm) | 60 MHz (dBm) | 80 MHz (dBm) | 90 MHz (dBm) | 100 MHz (dBm) | Duplex Mode
n1 | 15 | -100.0 | -96.8 | -95.0 | -93.8 | -92.7 | -91.9 |  |  |  |  |  |  | FDD
 | 30 |  | -97.1 | -95.1 | -94.0 | -92.8 | -92.0 |  |  |  |  |  |  | 
 | 60 |  | -97.5 | -95.4 | -94.2 | -93 | -92.1 |  |  |  |  |  |  | 

## Slide 4: REFSENS values: FFS
Following values are FFS:
Operating band / SCS / Channel bandwidth / Duplex mode |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Operating Band | SCS kHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 30 MHz | 40 MHz | 50 MHz | 60 MHz | 80 MHz | 90 MHz | 100 MHz | Duplex Mode
n1 | 15 |  |  |  |  |  |  | 1281 |  |  |  |  |  | FDD
 | 30 |  |  |  |  |  |  | 641 |  |  |  |  |  | 
 | 60 |  |  |  |  |  |  | 301 |  |  |  |  |  | 
Operating band / SCS / Channel bandwidth / Duplex-mode |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Operating Band | SCS kHz | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | 25 MHz (dBm) | 30 MHz (dBm) | 40 MHz (dBm) | 50 MHz (dBm) | 60 MHz (dBm) | 80 MHz (dBm) | 90 MHz (dBm) | 100 MHz (dBm) | Duplex Mode
n1 | 15 |  |  |  |  |  |  | -90.6 |  |  |  |  |  | FDD
 | 30 |  |  |  |  |  |  | -90.7 |  |  |  |  |  | 
 | 60 |  |  |  |  |  |  | -90.9 |  |  |  |  |  | 

## Slide 5: Coexistence: Agreement
Legacy coexistence requirements (BW <= 20MHz) remain unchanged.
2 new NS will be specified:
  To protect bands 33 and 34
  To protect bands 39 and 34
NS_05 (PHS protection) will not be updated with the added channel BW:
  Only for Japan
  Additional channel BW won’t be added to Regulation
  A note will be added to clarify this in 38.101-1

## Slide 6: Simulation Assumptions (1/3)
  CIM3: 60 dBc.
  IQ image: 28 dB.
  LO leakage: 28 dBc.
  PA calibration point was 20 MHz, 15 kHz, QPSK, DFT-S-OFDM, 100 RB at lower channel edge with 1 dB MPR
  Filter rejection for B34 protection: TBD (to be agreed via email before next RAN4#93).
  Channel bandwidth:
    25 MHz located at the worst-case position(s)
    30 MHz located at the worst-case position(s)
    40 MHz located at the worst-case position(s)

## Slide 7: Simulation Assumptions (2/3)
1st NS to protect bands 39 and 34

## Slide 8: Simulation Assumptions (3/3)
2nd NS to protect bands 33 and 34

## Slide 9: Reference
R4-1910865, UE REFSENS for 25 MHz channel bandwidth for n1, Huawei
R4-1911666, Discussion on A-MPR and addition spurious emissions for n1 25MHz channel bandwidth, China Unicom
R4-1912561, n1 30MHz REFSENS, Qualcomm
R4-1911816, Band n1 Wider CBW, UE requirements – REFSENS, Ericsson
R4-1911817, Band n1 Wider CBW, UE requirements – Spurious and A-MPR, Ericsson
R4-1911818, Band n1 Wider CBW, UE requirements – AMPR simulations results, Ericsson