## Slide 1: 3GPP TSG-RAN WG4 Meeting #92bis Chongqing, China, 14th – 18th October 2019
Qualcomm Incorporated, …
WF for sync raster for NR-U
R4-1912982

## Slide 2: Background
RAN4 is discussing definition of the synchronization raster in band n46 for NR-U operation
In RAN4 #92 it was agreed that only one SSB point would be defined per 20MHz sub-band and this point would be placed near the edge of each sub-band
Several proposals were presented in RAN4 #92bis meeting but the exact values of the GSCN set are still under discussion
This WF presents a proposal for the definition of the synchronization raster for NR-U operation

## Slide 3: Principles for sync raster definition
Definition of synchronization raster for band n46 in RAN4 should take at least the following principles into account:
  Minimum frequency separation from sub-band edge to guarantee compliance with inter-carrier and intra-carrier minimum guard-bands for all possible channel bandwidths
    925kHz for inter-carrier guardband (80MHz channel bandwidth)
    3 full RBs (30kHz SCS) for intra-carrier guardbands
  Maximize spectrum utilization for the case in which SSB is frequency multiplexed with RMSI or CSI-RS
    The GSCN point closest to the edge and compliant with inter and intra-carrier guardbands shall be selected

## Slide 4: Proposal
Considering a frequency offset of minimum 3 full RBs at 30kHz SCS to account for intra-carrier guardbands for each sub-band, define the following GSCN points:
  GSCN = {[8996], 9010, 9024, [9037/9038], 9051, 9065, 9079, 9093, 9107, [9121], [9218], 9232, 9246, 9260, 9274, 9287, 9301, 9315, 9329, 9343, 9357, [9371], 9385, 9402, 9416, 9430, 9444, 9458, [9471], [9485], [9499], [9513]}
Proposed values are conditioned on NR minimum channel guard bands
If it is later found that larger guard bands are needed, it is common understanding that some of the SSB points may need to be changed