## Slide 1: WF on power boosting requirement for NB-IoT operation in NR in-band
Nokia, Ericsson, Huawei, ZTE, CHTTL
3GPP TSG-RAN WG4 Meeting#92bis
Chongqing, China, 14 – 18 October 2019
Agenda Item: 7.11.2
R4-1912998

## Slide 2: Background
Way forward approved in RAN4#91:
R4-1907809, “WF on coexistence of NB-IoT with NR”, Huawei, HiSilicon, Ericsson, Nokia, ZTE, Dish, T-Mobile USA, CHTTL.
Proposals on power boosting requirement when NB-IoT is located within NR channel bandwidth in RAN4#92bis:
[1] R4-1910843, “Further consideration on power boosting”, Huawei, HiSilicon, Chongqing University.
[2] R4-1911221, “Proposals on power boosting requirement when NB-IoT is located within NR channel bandwidth”, Nokia, Nokia Shanghai Bell.
[3] R4-1911724, “Power boosting for NB-IoT coexisting with NR”, ZTE Corporation.
[4] R4-1911808, “NB-IoT - NR coexistence : Power boosting considerations”, Ericsson.

## Slide 3: Way forward
For 5 MHz and 10 MHz channel bandwidth, specify the minimum +6 dB power boosting requirement for in-band 180 kHz NB-IoT RB.
For 15 MHz channel bandwidth, specify the minimum +6 dB power boosting requirement for in-band center 77x180 kHz plus 15 kHz at each edge.
For 20 MHz channel bandwidth, specify the minimum +6 dB power boosting requirement for in-band center 102x180 kHz plus 15 kHz at each edge.
For >20 MHz channel bandwidth, specify the minimum +6 dB power boosting requirement for in-band 180 kHz NB-IoT RB within center 90% of NR channel bandwidth.
For >10 MHz channel bandwidth, specify +3 dB power boosting requirement for other in-band 180 kHz NB-IoT RBs.
BS manufacturer can declare support of higher power boosting.