## Slide 1: Way forward on NR Rx spurious emissions
Agenda Item: 6.7.3.5
Document for: Approval
Source: Ericsson, NTT DOCOMO
3GPP TSG-RAN WG4 #92bis Tdoc R4-1913030
Chongqing, China, 14 – 18 October 2019

## Slide 2: Background
The updated European ERC Recommendation 74-01 [1] introduces new limits (Category B) for Receiver spurious emissions for AAS BS using TDD.
Inputs to 3GPP propose to align also the Category A spurious emission limits with the new Category B limits [2][3][4].
The input in [3] presents two options for how the limits can be aligned.
The input in [4] presents four alternatives for how to take into account of the regulatory requirements in Category A regions.

## Slide 3: Proposed way-forward
Category B Rx spurious emission limits will be changed to reflect the new regulation in ERC Rec 74-01 [1] for BS type 1-O and BS Type 2-O.
Category A Rx spurious emission limits will be aligned with the new Category B limits in the following way:
  Category A receiver spurious emissions limits will be the same as the Category B limits, i.e. a single set of limits will be defined (Option 2 in [3]).
  Add a note for Japanese regulation. After revising Japanese regulation for alignment, remove the note from the 3GPP specifications (Alt. 4 in [4]).
  + 9dB scaling does not apply to BS type 1-O category A Rx spurious emission limits
The new limits will be as shown in Tables 1 and 2.
Limits for BS type 1-C and BS type 1-H will remain unchanged.

## Slide 4: Proposed new FR1 limits for Rx spurious emissions (AAS BS TDD)
A note will be added to the table for Japanese regulation.
Spurious frequency range | Basic limit | Measurement bandwidth | Notes
30 MHz – 1 GHz | -36 dBm | 100 kHz | Note 1
1 GHz – 12.75 GHz | -30 dBm | 1 MHz | Note 1, Note 2
12.75 GHz – 5th harmonic of the upper frequency edge of the UL operating band in GHz |  | 1 MHz | Note 1, Note 2, Note 3
NOTE 1: Measurement bandwidths as in ITU-R SM.329 [2], s4.1. NOTE 2: Upper frequency as in ITU-R SM.329 [2], s2.5 table 1. NOTE 3: This spurious frequency range applies only for operating bands for which the 5th harmonic of the upper frequency edge of the UL operating band is reaching beyond 12.75 GHz. |  |  | 
Table 1. General BS receiver spurious emission limits for BS type 1-O

## Slide 5: Proposed new FR2 limits for Rx spurious emissions (AAS BS TDD)
Spurious frequency range (Note 4) | Limit | Measurement Bandwidth | Note
30 MHz  1 GHz | -36 dBm | 100 kHz | Note 1
1 GHz  18 GHz | -30 dBm | 1 MHz | Note 1
18 GHz  Fstep,1 | -20 dBm | 10 MHz | Note 2
Fstep,1  Fstep,2 | -15 dBm | 10 MHz | Note 2
Fstep,2  Fstep,3 | -10 dBm | 10 MHz | Note 2
Fstep,4  Fstep,5 | -10 dBm | 10 MHz | Note 2
Fstep,5  Fstep,6 | -15 dBm | 10 MHz | Note 2
Fstep,6  2nd harmonic of the upper frequency edge of the UL operating band | -20 dBm | 10 MHz | Note 2, Note 3
NOTE 1: Bandwidth as in ITU-R SM.329 [2], s4.1 NOTE 2: Limit and bandwidth as in ERC Recommendation 74-01 [19], Annex 2. NOTE 3: Upper frequency as in ITU-R SM.329 [2], s2.5 table 1. NOTE 4: The step frequencies Fstep,X are defined in Table 9.7.5.3.2.3-2. NOTE 5: The frequency range from ΔfOBUE below the lowest frequency of the BS transmitter operating band to ΔfOBUE above the highest frequency of the BS transmitter operating band may be excluded from the requirement. ΔfOBUE is defined in subclause 9.7.1. |  |  | 
A note will be added to the table for Japanese regulation.
Table 2: General BS receiver spurious emission limits for BS type 2-O

## Slide 6: References
ERC Recommendation 74-01, “Unwanted emissions in the spurious domain”, amended 29 May 2019 (URL).
R4-1908452, "Alignment of Receiver spurious emission requirements for AAS BS" (Ericsson).
R4-1912297, "Receiver spurious emission requirements for Category A and Category B" (Ericsson).
R4-1912442, "Alignment of receiver spurious emissions requirements for BS type 1-O/2-O" (NTT DOCOMO, INC.).