## Slide 1: Way forward on switching period between case 1 and case 2
3GPP TSG-RAN WG4 Meeting #92bis
Chongqing, China, 14 - 18 Oct, 2019
Agenda: 8.13.6
R4-1913041
China Telecom

## Slide 2: Way Forward
Length of the UL switching period
  RAN4 recommendation on the length of UL switching period for defining UE RF requirements and capability reporting:
    [0]us, 35us, 140 us, [250]us
      RAN4 will decide whether 250us will be defined based on UE implementation in RAN4 #93 meeting
      0us cannot be achieved with the UE implementation of 2 Tx chains in total. RAN4 will decide whether 0us will be defined from RF requirements and/or capability reporting perspective for forward compatibility in RAN4 #93 meeting.
    The same length of switching period for switching from case 1 to case 2 and from case 2 to case 1.
    RAN4 does not preclude the possibility of down-selecting to the single value (e.g., one non-zero value) due to BS complexity issue and system performance.
    RAN4 does not preclude the possibility of introducing UE capability bit to allow different UE implementation.
    Existing RAN4 requirements will be not impact by introducing of the length of UL switching period
  The RAN4 recommendation will be sent to RAN1, and ask RAN1 to reply LS to RAN4 if RAN1 find there is any issues with the RAN4 recommendation.

## Slide 3: Way Forward
Location of the switching period
  For EN-DC: in NR carrier
  For UL CA and SUL: semi-statically configured by RRC on one specific carrier of the two uplink carriers
Applicable carrier(s) of UL outage due to switching
  Both carrier 1 and carrier 2
Transient period
  Define transient period in addition to the switching period
  Length of transient period: 10 us for NR, 20 us for E-UTRA

## Slide 4: Way Forward
Additional time for PUSCH preparation procedure
  Information to RAN1: A potential issue was raised in RAN4 that UL switching period may impact PUSCH preparation procedure time.
  RAN4 can continue discussing on whether the PUSCH preparation time can happen in parallel with the switching time, based on the UE implementation.
Information to RAN1
  RAN4 recommendation on the length of UL switching period
  RAN4 agreement on the location of UL switching period
  Potential issue identified in RAN4 on PUSCH preparation procedure time
  RAN4 agreement on transient period

## Slide 5: Way Forward
Tx in case 1 and case 2
  Clarify in RAN4 that the “Tx” in the WID means Tx chain but not active Tx with UL transmission.
Handling of DL reception interruption
  Option 1: Define different capabilities for UEs with and without DL reception interruption
  Option 2: DL reception interruption is not allowed
  Option 3: DL reception interruption is allowed
  Other options are not precluded.

## Slide 6: For information
Continue discussion on the issues under the following sub-sections of the ad-hoc minutes in R4-1912905:
  1.6 DL reception interruption due to UL switching
  1.7 UE capability reporting for different bands or band combinations
  1.8 Other issues on UE RF requirements
  1.9 WI scope
  1.10 RRM switching delay

## Slide 7
Thanks!