## Slide 1: WF on non-contiguous UL CA in FR2
Apple Inc.
3GPP TSG-RAN4 Meeting #92bis R4-1913044 Chongqing, China, 14-18 Oct, 2019

## Slide 2: Background
The following contributions on the topic of non-contiguous UL CA enhancement in FR2 were discussed:
[1] | R4-1910765 | Qualcomm Incorporated | FR2 Intra-band NC UL CA Feature Definition
[2] | R4-1910766 | Qualcomm Incorporated | TP to TR38.831: Emissions Requirements for FR2 NC UL CA
[3] | R4-1911512 | Apple Inc. | Carrier switching to enable non-simultaneous transmission for intra-band non-contiguous UL CA in FR2
[4] | R4-1911525 | Nokia, Nokia Shanghai Bell | FR2 Intraband Non-contiguous UL CA MPR simulations
[5] | R4-1912401 | Huawei, HiSilicon | On intra-band NC UL CA for FR2

## Slide 3: Occupied bandwidth for CA
As described in [4], the requirement for occupied bandwidth for CA is:
  For intra-band non-contiguous carrier aggregation, the OBW requirement is met when the ratio of the transmitted power in all sub-blocks of the uplink CA configuration to the total integrated power of the transmitted spectrum is greater than 99%.
This agreement is captured in a TP to TR38.831

## Slide 4: Remaining issues with NC UL CA MPR
Emissions in the spurious domain shall be taken into account in the NC UL CA MPR requirement
  No exception points shall be defined
Number of gaps between sub-blocks shall be at least 1

## Slide 5: Non-simultaneous uplink in NC carriers (1)
Definitions
  Simultaneous operation refers to active and allocated UL CCs in multiple non-contiguous sub-blocks
  Non-simultaneous operation refers to active and allocated UL CCs in a single sub-block of contiguous carriers
Proposed mechanisms to enable non-simultaneous operation
  Alt.1: apply the BWP switching framework
    DCI-based, RRC-based, and timer-based scenarios are not precluded
  Alt.2: apply the MAC CE based SCell activation framework
    UL and DL are activated and deactivated together
  Alt.3: apply the RRC based SCell configuration framework
    Only Alt.3 is applicable to SA FR2+FR2 CA or NSA LTE+FR2+FR2 DC scenarios
Alt.1
Alt.2
Alt.3

## Slide 6: Non-simultaneous uplink in NC carriers (2)
RAN4 sees the benefit of non-simultaneous UL in non-contiguous carriers from the points of view of improved output power due to reduced MPR and reduced power consumption
  Benefit applies to FR1 (pcell) + FR2 (scells) configuration
RAN4 confirms the feasibility of non-simultaneous UL in non-contiguous carriers
  A new capability shall be introduced to indicate that the UE only supports non-simultaneous uplink in NC FR2 carriers
  Default UE behavior is simultaneous (unlimited) uplink operation
The switching mechanism shall be down-selected between Alt.1, Alt.2, and Alt.3 during the RAN #93 meeting

## Slide 7: Signaling aspects
TS38.101-2 defines three frequency separation classes
  The UE can signal intraBandFreqSeparationDL and intraBandFreqSeparationUL separately [see TS38.306]
Frequency separation classes I, II, III are applicable for FR2 UL CA (simultaneous uplink operation) in Rel-16
  Whether Fs ≤ 2400 MHz can be applicable to FR2 UL CA with non-simultaneous uplink operation is FFS
Frequency separation class | Frequency separation (Fs)
I | Fs ≤ 800 MHz
II | Fs ≤ 1200 MHz
III | Fs ≤ 1400 MHz