## Slide 1: WF on beam correspondence in Rel-16
Apple Inc., Qualcomm Incorporated, Samsung, Sony
3GPP TSG-RAN4 Meeting #92bis R4-1913049 Chongqing, China, 14-18 Oct, 2019

## Slide 2: Background
The following contributions on the topic of beam correspondence in Rel-16 were discussed:
ref | tdoc | source | title
[1] | R4-1910767 | Qualcomm Incorporated | Rel-16 FR2 Beam Correspondence Enhancement
[2] | R4-1911401 | Samsung | Beam correspondence enhancement considering SNR condition
[3] | R4-1911509 | Apple Inc. | Further views on beam correspondence enhancements in Rel-16
[4] | R4-1911528 | Nokia, Nokia Shanghai Bell | FR2 BC enhancements
[5] | R4-1911549 | Ericsson, Sony | Beam correspondence during initital access and relation to OL power control
[6] | R4-1912312 | Sony, Ericsson | Views on Beam Correspondence
[7] | R4-1912403 | Huawei, HiSilicon | On beam correspondence for Rel-16
[8] | R4-1911511 | Apple Inc. | Views on spherical coverage requirements for initial access

## Slide 3: BC based on SSB only
The SSB configuration from Rel-15 is reused
Study performance difference of BC based on SSB only vs. BC based on CSI-RS only
Remaining tasks for RAN4 #93:
Calculate the SNR corresponding to the configuration
  Specify the side conditions
    The PSD of the RS is equalized to match SNR conditions of the Rel-15 requirement

## Slide 4: BC based on CSI-RS only
Assumption on the CSI-RS configuration
  The table itemizes the parameters which will be updated relative to the Rel-15 configuration
  All other configuration parameters related to CSI-RS are reused from Rel-15
  NOTE: ”P3 CSI-RS” refers to CSI-RS for beam management
Once the CSI-RS configuration is stable:
  Calculate the SNR corresponding to the configuration
  Specify the side conditions
    The PSD of the RS is equalized to match SNR conditions of the Rel-15 requirement
Open issues:
  If we do not reuse CSI-RS periodicity from Rel-15, then new values for this parameter are needed
  The definition of QCL info is FFS
  SSB configuration is FFS
  How to ensure that the UE has to perform BC based on the reference signal that is configured to it instead of e.g. using SSB for CSI-RS only based BC
parameter | Rel-15 value (for reference) | Rel-16 value (this WF)
P1 CSI-RS periodicity | Not defined | Alt.1: 20 ms
P3 CSI-RS repetitions per resource set | 8 | Alt.1: 8 [7] Alt.2: according to UE capability [1]
P3 CSI-RS configuration repetition | on | on
P3 CSI-RS trigger | Not defined | Alt.1: Reuse Rel-15 P3 CSI-RS once for every P1 cycle Alt.2: FFS
Tracking CSI-RS periodicity | 60 kHz SCS: 40 for CSI-RS resources 1 and 2 120 kHz SCS: 80 for CSI-RS resources 1 and 2 | Alt.1: reuse Rel-15 [7] Alt.2: FFS [1]
P3 CSI-RS QCL info | Type D to SSB | FFS
P1 CSI-RS QCL info | Not defined | FFS

## Slide 5: Related to beam correspondence tolerance
If UE support Rel-16 BC and UE is Rel-15 BC bit-1 UE,
  UE test EIRP (peak and spherical) requirement based on UE autonomous BC with updated side condition and/or configuration to be defined in Rel-16;
  If passed, Rel-15 EIRP (peak and spherical) requirement can be skipped. But two times of testing (for SSB-only and CSI-RS only) are needed.
Alt.1: If UE support Rel-16 BC and UE is Rel-15 BC bit-0 UE,
  It is invalid scenario and this is not allowed
Alt.2: If UE support Rel-16 BC and UE is Rel-15 BC bit-0 UE,
  UE test EIRP (peak and spherical) requirement based on UL beam sweeping assistance with updated side conditions and/or configuration to be defined in Rel-16;
  UE test beam correspondence tolerance with updated side condition and/or configuration to be defined in Rel-16;
  If passed, Rel-15 EIRP (peak and spherical) requirement can be skipped. But two times of testing (for SSB-only and CSI-RS only) are needed.

## Slide 6: Other aspects
Two enhancements were proposed:
  Enhancements to measurement reporting [2]:
    Network makes use of UE reported L1-RSRP to roughly improve beam correspondence performance
    Add dynamic signaling from UE to network to accurately improve beam correspondence performance, e.g.: UE can signal to network the UE measured SNR, and/or the necessity of UL beam sweeping, and/or the exact SRS resource number needed
  Introduction of a requirement on beam correspondence for initial access [5]:
    UE spherical coverage for PRACH transmissions (power class 3)
    Radiated spherical coverage sensitivity requirement on RAR (Msg2) reception
    Considering that verification of BC at initial access through open loop power control test would require significantly improved accuracy of the core requirement
  During the RAN4 #93 meeting RAN4 will discuss whether these enhancements are in the scope of the WID
Signaling aspects for the enhanced beam correspondence in Rel-16 are FFS