## Slide 1: WF on FR2 Inter-band DL CA
Sony, Qualcomm Incorporated, Apple Inc., Huawei, HiSilicon
R4-1913054
3GPP TSG-RAN WG4 Meeting #92-Bis
Chongqing, China, 14-18 Oct 2019
Agenda: 8.14.7

## Slide 2: Background
In RAN4#92 Bis, the following aspects have been discussed:
The feasibility of existing 8 us time difference requirement (MRTD) of the received symbols
whether UE is capable for forming beams towards the same directions and different directions for 28 GHz + 39 GHz simultaneously
Whether single AoA or two AoAs shall be adopted for UE RF test.

## Slide 3: WF
The number of bands is assumed to be two for the inter-band CA WI, and the intra-band CA+ inter-band CA is also included in the scope of inter-band CA WI .
UE is assumed to be feasible to have independent beam management for the bands that are part of supported band configuration in inter-band CA for 28 GHz + 39 GHz combinations.
  “28GHz” stands for a band group includes n257, n258, n261
  “39GHz” stands for a band group includes n259, n260
• Spherical coverage requirements for inter-band CA are tested from single AoA for Rel-16 if the following testability solution can be provided.
  Testability SI will study the TE capability of transmitting 28 GHz + 39 GHz from same direction simultaneously.
Defining spherical coverage requirement for inter-band CA.
  Alt.1: The UE shall meet the inter-band CA spherical coverage requirement simultaneously on 28 GHz and 39 GHz, the common spherical coverage range between the two bands shall be 50% for power class 3 UE.
  Alt. 2: The UE shall meet the inter-band CA spherical coverage requirement per band.
  Rel-15 spherical coverage requirement will be taken as baseline.