## Slide 1: WF on non-contiguous UL CA in FR2
Apple Inc.
3GPP TSG-RAN4 Meeting #92bis R4-1913055 Chongqing, China, 14-18 Oct, 2019

## Slide 2: Background
The following contributions on the topic of non-contiguous UL CA enhancement in FR2 were discussed:
[1] | R4-1910765 | Qualcomm Incorporated | FR2 Intra-band NC UL CA Feature Definition
[2] | R4-1910766 | Qualcomm Incorporated | TP to TR38.831: Emissions Requirements for FR2 NC UL CA
[3] | R4-1911512 | Apple Inc. | Carrier switching to enable non-simultaneous transmission for intra-band non-contiguous UL CA in FR2
[4] | R4-1911525 | Nokia, Nokia Shanghai Bell | FR2 Intraband Non-contiguous UL CA MPR simulations
[5] | R4-1912401 | Huawei, HiSilicon | On intra-band NC UL CA for FR2

## Slide 3: Occupied bandwidth for CA
As described in [4], the requirement for occupied bandwidth for CA is:
  For intra-band non-contiguous carrier aggregation, the OBW requirement is met when the ratio of the transmitted power in all sub-blocks of the uplink CA configuration to the total integrated power of the transmitted spectrum is greater than 99%.
This agreement is captured in a TP to TR38.831

## Slide 4: Remaining issues with NC UL CA MPR
Emissions in the spurious domain shall be taken into account in the NC UL CA MPR requirement
Number of gaps between sub-blocks shall be at least 1

## Slide 5: Non-simultaneous uplink in NC carriers (1)
Definitions
  Simultaneous operation refers to active and allocated UL CCs in multiple non-contiguous sub-blocks
  Non-simultaneous operation refers to active and allocated UL CCs in a single sub-block of contiguous carriers
Proposed mechanisms to enable non-simultaneous operation
  Alt.1: apply the BWP switching framework
    DCI-based, RRC-based, and timer-based scenarios are not precluded
  Alt.2: apply the MAC CE based SCell activation framework
    UL and DL are activated and deactivated together
  Alt.3: apply the RRC based SCell configuration framework
    Only Alt.3 is applicable to SA FR2+FR2 CA or NSA LTE+FR2+FR2 DC scenarios
Alt.1
Alt.2
Alt.3

## Slide 6: Non-simultaneous uplink in NC carriers (2)
RAN4 will further study the benefit of non-simultaneous UL in non-contiguous carriers from the points of view of improved output power due to reduced MPR and reduced power consumption, e.g., FR1 (pcell) + FR2 (scells) configuration
RAN4 will further study the feasibility of non-simultaneous UL in non-contiguous carriers
The switching mechanism shall be down-selected between Alt.1, Alt.2, and Alt.3 during the RAN #93 meeting.
  Other options are not precluded

## Slide 7: Signaling aspects
TS38.101-2 defines three frequency separation classes
  The UE can signal intraBandFreqSeparationDL and intraBandFreqSeparationUL separately [see TS38.306]
Frequency separation classes I, II, III are applicable for FR2 UL CA (simultaneous uplink operation) in Rel-16
  Whether Fs ≤ 2400 MHz can be applicable to FR2 UL CA with non-simultaneous uplink operation is FFS
Frequency separation class | Frequency separation (Fs)
I | Fs ≤ 800 MHz
II | Fs ≤ 1200 MHz
III | Fs ≤ 1400 MHz