## Slide 1: WF on FR2 MPE Enhancement
Qualcomm Incorporated,
R4-1913056
3GPP TSG-RAN WG4 Meeting #92-Bis
Chongqing, China, 14-18 Oct 2019
Agenda: 8.14.1

## Slide 2: Scope
Narrow down options what to signal to network
Agree time constraints for signaling
WF intention is not to discuss RAN2 details

## Slide 3: Background
This work item does not aim to propose the same alternatives which were not agreed (i.e. Alt1, Alt2 and Alt3 not agreed in RAN1#98 under Rel-16 NR eMIMO work item)
  Alt.1: default TCI state or QCL assumption of PDSCH (e.g. the most recent slot and the lowest CORESET ID)
  Alt.2: one of an active TCI state of CORESET
    FFS: details of which TCI state
  Alt.3: TCI state of scheduling PDCCH for A-SRS/PUCCH, and default TCI state or QCL assumption of PDSCH for other than A-SRS/PUCCH

## Slide 4: Options proposed for MPE event in RAN4#92 bis
  Rapid indication methods
    P-MPR
      Before P-MPR is taken
      While P-MPR is applied
      Can be one bit or include more information
    Alert/Emergency signal to indicated back off is about to happen
      Is this alert only or does it contain more information?
  Assistance information methods
    Energy headroom
      How much energy UE has for transmissions until specific time
    Power headroom
      PHR reporting is in place already
    Exposure headroom
    Dynamic or Multiple maxUplinkdutycycle

## Slide 5: RAN4#93
In RAN4#93 companies provide further analysis on details of their proposed solution such as
  Expected signaling latency of the proposed solution
  For example what is the time between UE detects MPE event and BS receives the MPE event information
  Provide RAN4 specification impact
  RAN1 and RAN2 specification impact is encouraged to be provided in RAN4 contribution
RAN4 chooses the solutions to address MPE
LS is sent to RAN1 or RAN2 or both if needed