## Slide 1: Summary of Tx diversity and eMIMO full power transmission
Ericsson
R4-1913067
3GPP TSG-RAN WG4 meeting #92bis Chongqing, China, 14 – 18 October 2019
Agenda item: 6.5.6.1
Document for: Approval

## Slide 2: Background
NR power-class (PC2) indication for EN-DC combinations and SA UL-MIMO, change of UE capability indication? (see e.g. [1][2])
  Clarification in 38.306 or ask RAN2 for a capability for UL-MIMO power class
Implementation of PC2 by 23 + 23 dBm and 29 dBm UE by 26 + 26 dBm (see e.g. [3][4])
Support of (transparent) transmitter diversity in 38.101-1 (see e.g. [5])
Relation to eMIMO Rel-16 work item on full power transmission
How to handle/accommodate – if at all – these items in the Rel-15 and Rel-16 specifications?

## Slide 3: Proposed way forward
No new UE capability for NR UL-MIMO power class for NR SA in Rel-15
Clarification on UE behavior for EN-DC mode when UE with 2 23dBm PAs declare PC2 in NR SA operation
  No new RAN4 core requirements introduced in Rel-15
  Alt 1: handled by RAN4 only (see Vivo/Sprint WF), inform RAN2
  Alt 2: by asking RAN2 to add clarification of the EN-DC NR power capability in 38.306 Rel-15 without change of the UE behaviour (no NBC)
  Other alternatives are not precluded.
Clarify the UL-MIMO sub-clause 6.2D.1 in 38.101-1 Rel-15 without changing implied UE behaviour e.g. Remove or further clarify the sentence ”If UE is configured for transmission on single-antenna port, the requirements in subclause 6.2.1 apply.”
Transparent TxD UE behaivor is not specified in Rel-15 RAN4 core requirements
  Further work needed in Rel-16 and impact on RAN5 conformance testing investigateg, e.g, replacement of ”antenna connector” with ”antenna port”

## Slide 4: References (selected)
R4-1912511, “Draft LS on EN-DC power class”, Huawei, HiSilicon
R4-1911544, “PC2 capability indication for SA operation”, Ericsson
R4-190729, “Draft CR for R15 38.101-1 HPUE power class clarification ”, OPPO
R4-1912437, “UL MIMO Power Class ”, Sprint
R4-1910745, “CR to enable tx diversity”, Qualcomm