## Slide 1: WF on FR2 test methodology enhancement
Apple Inc., CAICT, ...
3GPP TSG-RAN4 Meeting #92bis R4-19xxxxx Chongqing, China, 14-18 Oct, 2019

## Slide 2: References
tdoc | source | title
R4-1911501 | Apple Inc., CAICT | TR38.xyz skeleton for FR2 test method enhancement
R4-1912007 | Rohde & Schwarz | Views on FR2 test method enhancement
R4-1912108 | Keysight Technologies | On Test Time Reduction for NR FR2 UE Test Cases
R4-1912903 | Apple Inc., CAICT | Work plan for FR2 test method enhancement
R4-1911342 | Anritsu Corporation | Views on the applicability of NFTF and DNF methods in FR2
R4-1911502 | Apple Inc. | Views on the high DL power and low UL power objective
R4-1912106 | Keysight Technologies | On Relaxation of Low UL and High DL Test Cases
R4-1911503 | Apple Inc. | Views on the polarization mismatch objective
R4-1912107 | Keysight Technologies | On Minimizing Impact of Polarization Basis Mismatch
R4-1912314 | Sony | Views on testability enhancement for UE FR2 test
R4-1912420 | Huawei, HiSilicon | On EIS test metric

## Slide 3: Background
The study item consists of six objectives, three of which are prioritized until RAN #87:
  (prio) Define test methodology for high DL power and low UL power test cases
  (prio) Define solutions to minimize the impact of polarization basis mismatch between the TE and DUT on the RF testing
  (prio) Study testability enhancements to support the verification of RF requirements for inter-band (FR2+FR2) CA
  Support extreme temperature conditions for all applicable FR2 UE RF test cases
  Study testability enhancements to support the verification of RF requirements for FR2 DL 256QAM
  Study testability enhancements to reduce test time

## Slide 4: Objective 1: scope of impacted requirements
Tx regulatory requirement related
Clause | Requirement | Testability issue
6.3.2 | Transmit OFF power | Low UL power
6.5.1 | Occupied bandwidth | Low UL power
6.5.2.3 | Adjacent channel leakage ratio | Low UL power
6.5.3.2 | Additional spurious emissions | Low UL power
Rx regulatory requirement related
Clause | Requirement | Testability issue
7.5 | Adjacent channel selectivity (case 1) | High DL power
7.6.2 | In-band blocking | High DL power
7.9 | Receiver spurious emissions | Low UL power

## Slide 5: Objective 1: scope of impacted requirements
Test requirements which RAN5 agreed NOT to apply relaxation as of RAN5 #84
Clause | Requirement
6.2.1.3 | MOP EIRP/TRP
6.4.1 | Frequency Error
6.5.2.1 | Spectrum Emission Mask
7.3.2 | REFSENS
Test requirements which RAN5 agreed NOT to test as of RAN5 #84
Clause | Requirement | Testability issue
7.4 | Maximum input power | High DL power
7.5 | Adjacent channel selectivity (case 2) | High DL power

## Slide 6: Objective 1: agreements
Strive to achieve 0 dB relaxation in the test cases identified in slide #4
  For the SI outcome for this objective: enhancements of test methodology, gains from the enhancements relative to permitted methods in 38.810, impact on test time, and preliminary MU will be documented
Progress the work on the high DL power / low UL power objective in two tracks:
  Track 1: study possible enhancements to the permitted test methods listed in TR38.810
  Track 2: study NFTF and DNF solutions as alternative methods. Other methods are not precluded.
For Track 2
  Companies are encouraged to provide input on the acceptance equivalence criteria for alternative methods during the next meeting. Equivalence criteria in TR 38.810, clause 4.4, shall be taken as the baseline.
  Companies are encouraged to provide initial input on the NFTF and DNF solutions as alternative methods

## Slide 7: Objective 3: agreements
Companies are encouraged to take the FR2 inter-band CA agreements [R4-1913054] from the FR2 RF enhancement work item into account when planning contributions for the next meeting