## Slide 1: WF on DSS between NR and LTE refarming band
Samsung, Apple, Comcast, CableLabs, Federated Wireless,Google

## Slide 2: Background
UL 7.5kHz shift is used to resolve the sharing between LTE and NR@15kHz SCS;
Guard band is used to resolve sharing between LTE and NR@30/60kHz SCS
  In R15 the guard band is not specified and leaves as implementation

## Slide 3: Agreement on Generic principle for DSS
Enable DSS in LTE refarming bands, including existing NR bands and new refarming bands in the future, should be in line with NR global frequency channel raster and sync raster design;
Enable DSS in existing LTE refarming bands should not change existing band specific channel raster and default sync raster entries;
Changes, if any, in existing LTE re-farming bands should be analyzed for backward compatible issues;
If needed, new bands can be considered, e.g. band n41/n90.

## Slide 4: Agreement on DSS in existing LTE refarming bands
Band specific channel raster and sync raster:
  As a main principle, no changes to existing definitions;
  If changes are needed, then a new band approach can be adopted similar to band n41/n90.
UL 7.5 kHz shift:
  need to be checked in a case by case manner;
  if no NBC issue identified i.e. no early UE support this NR bands, UL 7.5kHz shift can be applied to this band;
  If NBC issue identified, new band approach can be adopted similar as band n41/n90.

## Slide 5: Agreement on New LTE refarming bands in the future
Channel raster:
  For bands below 3GHz, NREF in 100kHz step can be used;
  For bands above 3GHz, NREF in 300 kHz step can be used;
Whether need to support default SSB with 30kHz SCS and SSB block pattern B can be discussed in a case by case manner;
7.5 kHz UL shift should be mandatory supported for newly introduced LTE re-farming bands for DSS purpose only

## Slide 6: Proposals on DSS for band 48/n48
Channel raster
  Option 1: No change to channel raster because 300kHz granularity can be already configured by the network;
  Option 2: Add explicitly 300kHz channel raster (or just a NOTE).
Sync raster:
  MBSFN approach can be used to avoid transmission collisions between NR SSB and LTE CRS;
  FFS: whether further changes in SSB pattern are needed and possible;
UL 7.5kHz shift:
  Since there are no backwards compatibility issues with this band, make UL 7.45 kHz shift mandatory for n48
With above changes DSS for band 48/n48 can be supported without new band introduced.
Note: at least in RAN4#92bis, there is no vendor declare on deployment of device in band n48